## Slide 1: Motivation of dynamic subframe configuration for TDD
RAN #72, Busan, Korea, June 13 - 16, 2016 RP-160918
AI 10.1.1

## Slide 2: Content
Dynamic subframe configuration for TDD Relay
Dynamic configuration of special subframe for TDD

## Slide 3
Dynamic subframe configuration for TDD Relay

## Slide 4: Motivation
In the current stage, TDD is more important since most of the newly allocated spectrum are likely to be unpaired.
  All the bands between 3300~3800 can be used as TDD in certain regions
Efficient supporting TDD is important for LTE enhancement
However, the current TDD frame structure needs more flexibility due to
  Semi-static Backhaul Link(BL) & Access Link(AL) subframe configuration restrict the usage of Relay deployment
  Less flexible dynamic traffic adaptation due to limited UL/DL configuration
  Restricted periodicity of SRS feedback by the special subframe per 5ms/10ms. SRS is a more efficient way to utilize channel reciprocity for large number of antenna
  Slow feedback due to longer DL/UL switching period and TTI

## Slide 5: Background-TDD RN configuration
AL/BL resource configuration, longer than 1s(Considering 640ms system information delay and 200ms RRC delay)
Limited BL/AL ratio, if DL data already in RN the BL resource can not be dynamically allocated for DL
Every subframe have to be either UL or DL
Left figure shows much restrictive for BL/AL subframes

## Slide 6: RN Caching for UDN
For mobile data, significant amount of services have time, geographical characteristics.
  E.g. Map download, Breaking News
RN can use that characteristics to preload content
  predictive caching, which is based on analysis of user behavior and predication
  proactive caching, which is accessed earlier and valuable
The pre-loaded content is more than 30%[1]
TDD RN node allocates more resources for BL for preloaded content and gives to AL when many user start to download
[1]Intel, “Rethinking the small cell business model,” White Paper

## Slide 7: RN Caching – Evaluation on dynamic change of TDD subframe type
Evaluation configurations:
  Static configuration: 4 types of BL:AL ratios
  Semi-static configurations (1s)
  10ms dynamic TDD subframes
Observations:
  For the 4 static configurations, the caching scheme does not show significant different in terms of UPT
  For dynamic schemes, the gains are 20% in 10% RU and 35% in 30% RU, over 1s semi-static configuration. More gains are observed for cached data
Note: Only existing TDD subframe type is used

## Slide 8: Proposal for enhancement
To support Dynamic TDD subframe configuration and allow efficient TDD RN operation
  The DL /UL configuration can be changed dynamically while maintaining backward compatibility
Extending more TDD subframe used for RN BL and dynamic subframe(e-IMTA)
  Not limited to subframe #3, 4, 7, 8, 9
Additional subframe type to enable more efficient Dynamic TDD operation
  It is expected to beneficial for both normal TDD access, faster feedback and lower latency
  It can also improve RN operation

## Slide 9
Dynamic configuration of special subframe for TDD

## Slide 10: Background
Normal subframes can be dynamically reconfigured in eIMTA
  UL subframes configured by SIB can be flexibly used except the UL subframes configured by DL-reference configuration
Subframe #6 can be dynamically reconfigured as special subframe or normal DL subframe
  Special subframe is semi-statically configured by RRC
UL PUSCH in special subframe will be specified according to RP-160664

## Slide 11: Motivation
Dynamic configuration for special subframe
  More flexible resource efficiency according to traffic compared to current eIMTA
  Higher throughput performance

## Slide 12: Objectives
Evaluate the benefits of dynamic configuration for special subframe
Study dynamic reconfiguration for special subframes, taking into account:
  Possibility of more configurations for special subframes
  Signaling for dynamic configuration of special subframe
  Enhancement for interference management
  Backward compatibility with Rel-8/9/10/11/12/13
Identify the related specification impacts

## Slide 13: Thank you