## Slide 1
3GPP TSG RAN Meeting #72
Busan, South Korea, June 13- 16, 2016
Document for Discussion
Agenda Item: 14.2.1
RP-161114
Motivation for Split of DL and UL category 4
Sequans Communications

## Slide 2: Overview of UL/DL split
In RAN#67 UL64QAM based on split of DL and UL categories was introduced
At first stage, UL/DL split was introduced for Rel-12 newly introduced categories and for legacy categories 6,7,9-12
UL/DL categories split enables UEs to couple UL category 5 and UL64QAM with wide spreaded DL categories e.g. DL Category 6
However, UL/DL split is not yet specified for UL category 5 with the wide spreaded DL category 4

## Slide 3: Motivation for UL/DL split of Category 4
Category 4 is still the best fit in terms of cost and DL throughput for many mid-range applications e.g. indoor CPEs for home networking
Such applications would benefit from more balanced throughput. UL/Dl split would allow coupling DL 150MBps with UL 75MBps
For Operators deploying Category 4, UL/DL split increases UL spectral efficiency.
Sequans and its partners see specific demand for DL category 4 / UL category 5 applications from several operators

## Slide 4: Summary of changes
Introduction of UL/DL split for Category 4 from Rel-12 in TS 36.306 and TS 36.331 (without ASN.1 change)
RAN2 have examined the CRs and technically indorsed them

## Slide 5: References
RP-161074 RAN2 technically endorsed CRs on Split of DL and UL category 4
Tdoc | Title | Source | Spec | CR # | rev | cat | Release | SI/WI
R2-164314 | Split of DL and UL category 4 | Sequans Communications | 36.306 | 1324 | 2 | F | Rel-12 | LTE-L23, TEI12
R2-163629 | Split of DL and UL category 4 | Sequans Communications | 36.306 | 1325 | - | A | Rel-13 | LTE-L23, TEI12
R2-164286 | Split of DL and UL category 4 | Sequans Communications | 36.331 | 2157 | 1 | F | Rel-12 | LTE-L23, TEI12
R2-163636 | Split of DL and UL category 4 | Sequans Communications | 36.331 | 2158 | - | A | Rel-13 | LTE-L23, TEI12