## Slide 1: Proposal on handling of eMBMS WI
Huawei, HiSilicon, Intel
3GPP TSG RAN Meeting #72 RP-161223
Busan, Korea, June 13 - 16, 2016
Document for: Discussion
Agenda Item: 10.2.11

## Slide 2: Background-Objectives in WID
The objective of the work item is to evaluate and specify the following eMBMS enhancements for LTE [R1-160675]:
a. Specify means of using a longer cyclic prefix (e.g. greater than 33.33µs) for use in a mixed unicast/eMBMS carrier for large SFN delay spread environment (e.g. 15km or larger inter-site distance), which guarantees coexistence of the legacy and new prefixes on the same carrier, while achieving a spectral efficiency of at least 2 bps/Hz. This objective includes evaluation. (RAN1)
b. Specify means of using subframes 0, 4, 5, 9 (FS1) and 0, 1, 5, 6 (FS2) for MBSFN. (RAN2, RAN1)
  The non-MBSFN subframes for unicast can only be used as Scell
c. Specify means of configuring MBSFN subframes without a unicast control region and cell-specific reference signals. (RAN1, RAN2)
Study the following:
d. Support for standalone carrier with all DL subframes dedicated to MBSFN transmission and self-contained eMBMS signaling including information of SIB13, SIB15, SIB16. (RAN2)
e. Support for multi-carrier eMBMS/unicast operation involving reception from one or more eMBMS cells that may be non-collocated and asynchronous with one or more cells that are simultaneously used for unicast. (RAN4, RAN2)
f. Solutions where a UE can receive the TV transport service without being authenticated (RAN1, RAN2, RAN3)

## Slide 3: Discussion -1/5
For objective a, Specify means of using a longer cyclic prefix (e.g. greater than 33.33µs) for use in a mixed unicast/eMBMS carrier for large SFN delay spread environment (e.g. 15km or larger inter-site distance), which guarantees coexistence of the legacy and new prefixes on the same carrier, while achieving a spectral efficiency of at least 2 bps/Hz. This objective includes evaluation. (RAN1)
  New numerology (new carrier spacing) was not mentioned in RAN #71, and not captured in WID
  New numerology will take long time to investigate and specify, while the allocated TU cannot fit it.
    Examples can be found in R8 numerologies and R13 NB-IoT numerology discussion.
  There are on-going NR discussion in Rel-14 on new numerology including broadcasting service, which covers the scenarios highlighted in the joint paper [RP-160825]
Observation: Discuss new numerology in NR instead of in LTE session for MBSFN with very large ISD can potentially provide more efficient progress

## Slide 4: Discussion -2/5
  For objective b and c,
b. Specify means of using subframes 0, 4, 5, 9 (FS1) and 0, 1, 5, 6 (FS2) for MBSFN. (RAN2, RAN1)
  The non-MBSFN subframes for unicast can only be used as Scell
c. Specify means of configuring MBSFN subframes without a unicast control region and cell-specific reference signals. (RAN1, RAN2)
It is duplicated with the proposal of Lean carrier [RP-160880], which was resubmitted to RAN#72.
Observation: One of the WI (eMBMS or Lean carrier) should be chosen to complete the related work

## Slide 5: Discussion -3/5
  For objective d, Support for standalone carrier with all DL subframes dedicated to MBSFN transmission and self-contained eMBMS signaling including information of SIB13, SIB15, SIB16. (RAN2)
  According to SA1 requirement as well as the joint paper of “RP-160825 Importance of longer eMBMS CP for large ISDs”, mixed carrier is the main focus with:
  support dynamic switching between unicast and broadcast service
  In addition
  Mixed carrier is normally a standalone carrier
  Mixed carrier with more subframes allocated for MBSFN transmission can be close to dedicated MBSFN carrier.
Observation:
  Mixed carrier is the focused scenario
  Completion of objective b and c results in completion of objective d.

## Slide 6: Discussion -4/5
  For objective e. Support for multi-carrier eMBMS/unicast operation involving reception from one or more eMBMS cells that may be non-collocated and asynchronous with one or more cells that are simultaneously used for unicast. (RAN4, RAN2)
  It requires the RRM core-part work in RAN4 but no TU has been reserved.
  It is an extended deployment which may not be as urgent as the other objectives

## Slide 7: Discussion -4/5
  For objective f. Solutions where a UE can receive the TV transport service without being authenticated (RAN1, RAN2, RAN3)
  Observation: It has no specification impact on RAN

## Slide 8: Discussion -5/5
  MBSFN operation requires time synchronization among eNBs. No requirement has been defined in 3GPP for MBSFN operation.
  To ensure of the MBSFN operation performance, inter-cell time synchronization requirement needs to be specified in RAN4, which should be applicable also for legacy MBSFN operation

## Slide 9: Proposal
It is very challenging to complete all of the objectives within Rel-14. Scope reduction is needed to ensure the completion of the most important objective(s) in this WI.
Proposal: Down-scope eMBMS, keep either objective a or objective b&c.
  Include the following objective into eMBMS WI: “to specify inter-cell time synchronization requirement for MBSFN operation [RAN4]”
  If objective a is down scoped, complete the work of objective a in 5G new RAT