## Slide 1: Discussion on eV2X in 5G RAN
LG Electronics
3GPP TSG RAN Meeting #73 RP-161651 New Orleans, USA, September 19 - 22, 2016
Agenda item: 9.2.1
Document for: Discussion

## Slide 2: Introduction
Rel-14 WI “Support for V2V services based on LTE sidelink” can be completed in RAN#73.
  Leftovers can be treated in the ongoing WI “LTE-based V2X Services” until Mar. 2017.
eV2X is also under study in RAN as a part of NR study item.
It has been questioned how Rel-14 LTE V2X is related to solutions to be specified for eV2X by NR and/or LTE evolution in Rel-15 or after (referred to as “5G eV2X” in this Tdoc).
  The life cycle of a UE installed in a vehicle will be longer.
    Especially for sidelink case, it is possible to have a situation where vehicles supporting only Rel-14 V2X, both Rel-14 V2X and 5G eV2X, and only 5G eV2X can coexist.
  Rel-14 V2X focuses on broadcast transmissions that need to be received by all the proximal vehicles including those operating services with 5G eV2X.
This contribution discusses with focus on sidelink
  The relation between 5G eV2X and Rel-14 V2X
  Standardization plan for 5G eV2X

## Slide 3: Design target of 5G eV2X
Rel-14 LTE V2X is expected to provide sufficient performance for the basic ITS services.
  No significant enhancement seems required.
  Even a UE equipped with 5G eV2X needs to use Rel-14 LTE V2X to communicate with vehicles supporting only Rel-14 LTE V2X.
SA1 is defining advanced ITS services that will be difficult to achieve using Rel-14 LTE V2X.
  Achieving this may require substantial deviation from the design of Rel-14 LTE V2X.
  NR will have much more flexibility than evolving LTE further.
Low latency & high reliability
High data rate
Basic road safety
(e.g., forward collision warning)
Basic infotainment
(e.g., traffic flow optimization)
By Rel-14 LTE V2X
Automated driving (e.g., cooperative collision avoidance, remote driving, high-density platooning)
Sensor data dissemination
(e.g., see-through)
Advanced infotainment
(e.g., dynamic map update, high-quality multimedia, augmented reality navigation)
By 5G eV2X
Features introduced in 5G eV2X should focus on advanced services not achievable by Rel-14 LTE V2X.
Rel-14 V2X features are still used for basic services in order to ensure compatibility.

## Slide 4: Design target of 5G eV2X
It will be reasonable to assume “service-specific radio technology.”
  An example scenario
Basic safety using Rel-14 LTE V2X
High density platooning using additional features of 5G eV2X
Remote driving using additional features of 5G eV2X
Advanced infotainment using additional features of 5G eV2X

## Slide 5: Compatibility and coexistence of V2X and eV2X
SA1 discussed this topic and made some agreements.
  “UE using 5G RA(N) based V2X communication shall be able to communicate with UE using E-UTRA(N) based V2X communication” [1].
This may be possible if every UE having 5G eV2X also implements Rel-14 LTE V2X.
  What if a UE supports NR only?
NR
NR
R14 LTE
R14 LTE
Advanced services
Basic services
?

## Slide 6: Compatibility and coexistence of V2X and eV2X
One solution can be to make one NR sidelink configuration which is compatible with Rel-14 LTE sidelink design.
  The other NR sidelink configuration may be non-compatible with Rel-14 LTE design and used for advanced services.
    E.g., in terms of TTI length, subcarrier spacing, …
  These transmission modes should coexist efficiently.
NR sidelink
Transmission mode 0
Transmission mode 1
Transmission mode 2
Compatible with Rel-14 LTE SL mode 3 and 4
Used for basic safety services
Not compatible with Rel-14 LTE SL
Used for advanced services

## Slide 7: Time plan for eV2X standardization
It is reasonable to start discussing technical solutions for NR sidelink for eV2X from March 2017 when Rel-14 LTE V2X will be finalized.
  Solutions for the “LTE SL compatible mode” as well as “LTE SL non-compatible mode.”
  Efficient coexistence of these modes need to be studied.
  Note that SA1 eV2X study is scheduled to be completed in December 2016.
Until March 2017, RAN WGs can conduct background study for eV2X as a preparation of the discussion for the technical solutions. For example,
  How to translate the SA1 requirement to the radio KPI
  Vehicle-specific antenna configuration and channel model [e.g., 2, 3]

## Slide 8: Conclusion
Technologies of Rel-14 LTE V2X are used for the basic safety service, not only in Rel-14 UEs but also in UEs supporting NR or LTE evolution.
NR eV2X study should focus on enabling new services not achievable by Rel-14 LTE V2X.
NR sidelink should support multiple configurations/modes
  One configuration/mode is compatible with Rel-14 sidelink design for V2X and used for the basic safety services.
  Other configurations/modes may be non-compatible with Rel-14 design and used for advanced services.
  The related requirement for NR design is proposed in [4].
Technical solutions for NR SL for eV2X need to start from March 2017.
  Until then, RAN WGs continues background study as the preparation.

## Slide 9: References
[1] S1-162358, “Use Case on NR and LTE interoperability,” LG Electronics Inc.
[2] R1-167932, “WF on system level simulations for V2X NR," Ericsson.
[3] R1-168370, “WF on Modeling Line-of-Sight Blockage for V2V,” Huawei, HiSilicon, Volkswagen, Ericsson, General Motors, Vodafone.
[4] RP-161652, “pCR to 38.913 on eV2X requirements,” LG Electronics.