## Slide 1: RP-161690 Agenda item 9.2.2 3GPP RAN #73 New Orleans, USA, September 2016
Comparison between NR options
assuming NGCN is deployed

## Slide 2: Comparison assumptions
1. NGCN is deployed in the field
2. Sub-6GHz spectrum is available for NR deployment for option 2/4/4a
3. Both sub-6GHz and above 6GHz spectrum are available for NR in option 7/7a
Option 2/4/4a
Option 5/7/7a

## Slide 3: UE requirements (1/2)
 | 2/4/4a | 5/7/7a
5G NAS | support | support
NR features | NR AS features including stand alone specific features (initial access, Inactive state, HO) | NR except for stand alone specific features
eLTE features | eLTE except for initial access | All eLTE features

## Slide 4: UE requirements (2/2)
Comments:
  Considering that 2/4/4a will be deployed in the long term anyway, UE should support stand alone specific features regardless of network deployments in the short term
  Considering NR coverage maybe limited in the initial stage and inter-working with eLTE will be anyway needed, UE should support all eLTE features and not just part of them. In addition the difference is minor.
Observations:
  UE should support both eLTE and NR stand alone mode from the very beginning of NR commercial deployment regardless of migration strategy
  From UE point of view, there is no difference between these two groups of network deployment

## Slide 5: Impact on eLTE eNB (1/2)
 | 2/4/4a | 5/7/7a
UP function | For option 4, no impact is foreseen; For option 4a, need to accommodate new QoS profile | Always needs update to accommodate new QoS profile
CP function | No impact is foreseen | More functions are needed e.g. support of DC scheme; network slicing selection; initial access of new UE; network routing to EPC/NGCN…
Hardware | No impact is foreseen | For option 7, hardware needs be upgraded to accommodate NR throughput
Network interface | Need to support NG-U for option 4a Need to support Xn | Need to support NG-U Need to support NG-C Need to support Xn

## Slide 6: Impact on eLTE eNB (2/2)
Comments:
  Option 4a is mainly used to offload traffic from NR system but not to improve user throughput. Considering considerable better spectrum efficiency and limited number of UEs on the market in the beginning, it is not an attractive option when stand alone NR is deployed
  So if option 4 is deployed as DC architecture, a LTE eNB can almost be reused as an eLTE eNB with very minor change, with the support of Xn interface
  If option 7/7a is deployed, then a LTE eNB needs significant upgrade of both software and hardware
Observation:
  Option 4 will have minor impact on existing LTE eNB while option 7/7a will have significant impact on existing LTE eNB.

## Slide 7: 5G Control plane latency requirement
As pointed out by ZTE’s paper [RP-161691]:
  Option 2/4/4a can meet 5G CP latency requirement, i.e. 10ms delay
  Option 5/7/7a can NOT meet 5G CP latency requirement due to its legacy system nature

## Slide 8: 5G UP performance
 | 2/4/4a | 5/7/7a
Throughput | Comparable between: Option2 and option 7a Option 4a and option 5 Option 4 and option 7 | 
Delay | Comparable between: Option2 and option 7a Option 4a and option 5 Option 4 is better than option 7 due to the fact that the main stream in option 4 is the NR path directly exchanged over NR radio interface while the main stream in option 7 is also the NR path, but delayed by Xn backhaul and scheduling uncertainty | 

## Slide 9: Mobility issues
 | 2/4/4a | 5/7/7a
HO | Between NR and NR within NR coverage; Between NR and eLTE when UE moves out of NR coverage and vice versa* | Between eLTE and eLTE always
SCG change | eLTE has quite good coverage, SCG change of eLTE eNBs is available and throughput will not fluctuate too much | NR may not have continuous coverage and thus lack of SCG change results in high throughput fluctuation
Inter-RAT HO between eLTE and NR will be much like HO between eLTE considering they are within same NGCN and same Xn interface
But option 2/4/4a is better due to the fact that eLTE has already good coverage and hence allows quite smooth SCG change
*in this case option 5 is configured

## Slide 10: Support of vertical industries
Option 2 can meet 5G requirement for verticals, e.g. mTMC and URLLC
Option 5/7/7a can NOT meet 5G requirement for verticals, e.g. mTMC and URLLC

## Slide 11: Summary
 | Option 2/4/4a | Option 5/7/7a
UE requirements |  | 
Impact on LTE eNB | (option4) (option4a) | 
Control plane requirements |  | 
User plane performance |  | 
Mobility issues |  | 
Support of verticals |  | 

## Slide 12: Conclusion
Option2/4/4a is technically better than option 5/7/7 for low NR spectrum and high NR spectrum with dense deployment!

## Slide 13: Thank you