## Slide 1: Requirements for use case in high speed scenario
3GPP TSG-RAN Meeting #73 RP-161807
New Orleans, USA, September 19 - 22, 2016
ZTE, CATR

## Slide 2: Motivation - Classic train traffic types
Real-Time Cyclic (RTC) Traffic (Note1)
  Types: train control information, train rear information, shunting train protecting, etc.
  Reliability in LTE-R: >30s EFP (95% coverage) (Note2)
Real-Time Acyclic (RTA) Traffic (Note1)
  Types: dispatching communication, dispatching command transfer, transmission of train numbers, train safeguard alarm, DMS, 6C, TCDS, etc.
  Reliability in LTE-R: >20s EFP(95%)
Note1: The service requirements of LTE-R (Railway) which is designed in China is based on the QoS requirements of GSM-R [1].
Note2: >30s EFP (95%) means that 95% coverage should fulfill 100% transmission successful rate for more than 30s.
Notes: DMS: Dynamic Monitoring System
6C: 6 checking sub-systems
TCDS: Train Coach Running Diagnosis System
EFP: Error Free Period

## Slide 3: Motivation - Future Railway Mobile Communication
Critical Train Communication [2]:
  Automatic train control communication
  Trackside maintenance warning system communication
  Remote control of engines
  Monitoring and control of critical infrastructure
  On-train safety device to ground communication
  Platform/train interface alert
  Train integrity monitoring data communication
On-train passenger communication
  In 2016, on-train passenger internet service by China Railway Network

## Slide 4: Motivation – Current Status of Railway Mobile Communication for 5G
Current Objectives of European Railway community [2]:
    As GSM-R (Railway) proven as expensive for the railways, both in-terms of capital and operational expenditure, European Railway community has initiated the work to identify a successor for GSM-R, considering the long term life expectancy of ETCS (2050) and the Railway business needs including the critical train services.
  Current Objectives of 3GPP SA1 SID of FRMCS [3]:
    Extract and collect relevant use cases and requirements from the FRMCS user requirement specification that are within 3GPP’s scope of work. If necessary rephrase and align the use cases and requirements according to 3GPP terminology. Group requirements into categories and harmonise similar requirements from different use cases.
Current Objectives of 3GPP RAN high speed scenario:
    High speed scenario approved in 3GPP 38.913 mainly concerns about the services used by passengers, and the critical train services are not included.
Notes: ETCS: European Train Control System).
FRMCS: Future Railway Mobile Communication System

## Slide 5: Motivation – Why starts in RAN now and before SA1 completes the SI
Timing necessity
  The SA1 SI (FS_FRMCS) is scheduled to complete by Dec 2016, and RAN SI for NR is scheduled to complete by Mar 2017. There can be no enough time for RAN to ensure the support to FRMCS or even the forward compatibility if RAN starts the corresponding study after FS_FRMCS completes in SA1.
Timing feasibility
  To reduce the RAN work load, the critical communication for high-speed train can be considered as a special deployment scenario case under URLLC only, if it is not agreed to involve with other usage scenarios.
  During 2016Q4, RAN can take the progress in SA1 as study input.

## Slide 6: 5G Requirements - Future Railway Mobile Communication
Mobility
  Support up to 500 km/h or more (including safety margin)
Handover capability
  This capability refers to handover success rate.
System performance
  User experience data rate, 5th SE and so on.
Reliability
  This refers to the high reliable service requirements of Future Railway Mobile Communication System [1]. The reliability needs further clarification.

## Slide 7: Conclusions
High speed train scenario is a significant scenario in 5G.
The requirements of high speed train, not only for passenger services but also for critical communications, should be considered in TR38.913.

## Slide 8: Reference
[1] “GSM-R Interfaces: Class 1 Requirements”, ERTMS/ETCS - Class 1, 10-Oct-2005
[2] “Future Railway Mobile Communication System: User Requirements Specification”, FRMCS Functional Working Group, 29th of March 2016
[3] S1-161588, “New Study on Future Railway Mobile Communication System”, Nokia, Huawei, Ericsson, Kapsch CarrierCom, Mitsubishi Electric, Korea Railroad Research Institute (KRRI), Qualcomm, ETRI, Fujitsu, US Department of Commerce, ZTE TRUNKING Technology Corp, Venice, Italy, 9 - 13 May 2016