## Slide 1
Motivation for
Advanced Sleep Modes in NR
  Source: Orange, Huawei
3GPP TSG RAN meeting #74
Vienna, Austria, December 5 - 8, 2016
RP-162247

## Slide 2: Reminder: Energy Efficiency Requirement as per the NGMN 5G White paper
“Energy efficiency is defined as the number of bits that can be transmitted per Joule of energy, where the energy is computed over the whole network, including potentially legacy cellular technologies, Radio access and Core networks, and data centres.
5G should support a 1,000 times traffic increase in the next 10 years timeframe, with an energy consumption by the whole network of only half that typically consumed by today’s networks. This leads to the requirement of an energy efficiency increase of x2000 in the next 10 years timeframe.
Every effort should be made to obtain the energy gain without degrading the performance, but the technology should allow native flexibility for the operator to configure trade-off between energy efficiency versus performance where justified.”

## Slide 3: Advanced Sleep Modes: going beyond current sleep modes
Sleep modes are currently available with all radio technologies (2G, 3G and 4G).
For example, with 4G networks, sleep modes allow an energy saving of about -10% on the radio part.
However a huge potential for additional savings remain, since:
      a high part of the radio resources is still unused (in networks deployed for coverage, average resource utilization rate is low),
      efficiency of current sleep modes is limited due to the short time window during which they are effective (limited by the symbol duration, i.e. 71 µs in 4G)
The concept of Advanced Sleep Modes (ASM) aim at shutting down more transmitter resources during longer periods

## Slide 4: Potential energy savings from ASM
Simulations of ASM have been run
        by IMEC [1]
        by Nokia & Orange [2]
        by Huawei [3]
As an outcome of these simulations, up to 90% theoretical power savings may be possible during inactive periods (see table below)
Sleep Mode | Minimum continued sleeping time |  | Theoretical Power Savings (IMEC) [1] | Theoretical Power savings (Nokia & Orange) [2]
SM 1 | 71µs | (Symbol) | -50% | -53%
SM 2 | 1ms | (TTI) | -80% | -89%
SM 3 | 10 ms | (Frame) | -92% | -93%
SM 4 | > 1s |  | -95% | -94%
Source Huawei [3]

## Slide 5: Proposed 3GPP targets for effective Advanced Sleep Modes
      The main limiting factor on the efficiency of ASM is the periodicity of signaling, constrained by the trade-off between energy savings and latency requirements, depending on load, service targets and cells.
  Energy Efficiency also depends on the number of active transmitters. In case of Massive MIMO, high number of transmitters give higher granularity to switch on / off specific transmitters and / or move to lower order MIMO modes when possible, reducing the total radiated power accordingly. As an example, a cell could be switched from MIMO 64xN to 32xN, 16xN or 8xN at low load, in a semi-static and automated manner. Order of magnitude for periodicity of switch could be in order of minutes.
Consequently, the 5G standards should allow flexibility, by studying mechanisms to increase energy efficiency, including:
      operator selection of the periodicity between signaling reference signals (e.g. synch channels)
      automated selection of maximum MIMO order and corresponding number of active transmitters in a semi-static manner
      UE techniques to wake-up inactive cells
  Proposal: RAN plenary should allow RAN1 & RAN2 to study these mechanisms as part of NR SI in Rel14, for actual standardization in Rel15

## Slide 6: References
[1] IMEC, http://www2.imec.be/be_en/research/wireless-communication/power-model-
html.html
[2] L.-M. Dogariu (1) , J. Moilanen (2) , J. Petri (2) , A. Gati (1) , B. Seyra (1) , Next
Generation Sleep Modes for 5G networks, submitted to IEEE Series on Green
Communications and Computing Networks (IEEE Communications Magazine)
(1) Orange
(2) Nokia

## Slide 7
Thank you!