## Slide 1: Motivation for new SI : Study on 3GPP V2X phase 3
LG Electronics
3GPP TSG RAN Meeting #75 RP-170239 Dubrovnik, Croatia, March 6 - 9, 2017
Agenda item: 9.1

## Slide 2: Enhanced V2X services in SA1
SA1 study was completed with TR 22.886 and normative WI is approved in [1].
Four categories of eV2X use cases
(1)
(2)
<Platooning>
<Advanced driving>
<Extended sensors>
<Remote driving>

## Slide 3: Enhanced V2X services in SA1
Summary of KPIs
Observation
  Wide range of KPIs
    Dependent of operation scenarios such as driving automation level
  Challenging requirement for high-end eV2X services
    Substantial enhancement is necessary.
 | Latency | Reliability | Data rate | Communication range
Platooning | 10 ~ 25 ms | 90 ~ 99.99% | 12 kbps ~ [65] Mbps | [5] ~ [10} sec * relative speed
Advanced driving | [3] ~ [100] ms | [99.99] ~ [99.999]% | 65 kbps ~ [50] Mbps (inc. DL [0.5] UL [50] Mbps) | [5] ~ [10} sec * relative speed
Extended sensors | 3 ~ 100 ms | 90 ~ 99.999% | 25 ~ 1000 Mbps | 50 ~ 1000 meters
Remote driving | 5 ~ [20] ms | [99.999]% | UL 25, DL 1 Mbps | 
General requirement on positioning: Relative lateral position accuracy of 0.1 m between UEs |  |  |  | 
Design target of Rel-14 LTE V2X
Latency: 20 ~ 100 ms
Reliability: 90%
Data rate: around 10 kbps
Communication range: 100 ~ 300 meters

## Slide 4: Evolution of 3GPP V2X
Activities outside 3GPP are also important for the successful deployment of V2X services.
  It is important to show clear vision of continuous 3GPP V2X evolution path to regulation bodies, ITS societies, related industry associations, etc.
Rel-14 LTE V2X covers basic safety services. => 3GPP V2X phase 1
Rel-15 WI can start to enhance the V2X performance => 3GPP V2X phase 2
  But big change may not be possible due to the time limitation.
    Low-end eV2X services can be the target.
    Enhancement with backward compatibility needs to be considered.
      Examples include high order modulation and PC5 carrier aggregation
3GPP V2X phase 3 will cover the whole eV2X services.
  Thorough study is necessary to support the challenging high-end services.
    Solutions not compatible with Rel-14 V2X need to be studied.

## Slide 5: Study scope for 3GPP V2X phase 3
The study needs to cover both direct link between UEs and cellular link between UE and network.
  To maximally utilize the benefit of cellular V2X.
Low latency and high reliability
  Sidelink: Techniques such as flexible numerology, multi-antenna for sidelink, HARQ/CSI feedback, enhanced resource allocation, …
  Uplink/downlink: HARQ/CSI feedback for DL multicast/broadcast, reduction of handover interruption/failure (if Rel-15 LTE/NR Uu is insufficient), …
High data rate
  Spectrum above 6 GHz (e.g., 63-64GHz allocated for ITS in Europe), efficient V2X carrier aggregation, …
V2X message coverage extension
  UE-UE relaying, …
Vehicle positioning accuracy improvement
  Ranging via sidelink, …

## Slide 6: Proposal
Approve at RAN#75 an SI for 3GPP V2X phase 3.
  SID is proposed in [2].
  A WI is also expected for 3GPP V2X phase 2 which is to be specified within Rel-15.
Study scope can be prioritized based on input on the commercial demand.
  A spin-off WI can be considered in Rel-15.
Initial study needs to focus on the completion of eV2X evaluation methodology.
  This is a leftover from NR phase 1 SI.
SI on 3GPP V2X phase 3
Rel-15
Rel-16
WI on 3GPP V2X phase 3
WI on 3GPP V2X phase 2
Rel-14
WI on 3GPP V2X phase 1 (Rel-14 LTE V2X)
Backward compatible
Non-backward compatible
3GPP V2X evolution path

## Slide 7: References
[1] S1-171417, “New WID on Enhancement of 3GPP support for V2X scenarios,” LG Electronics, Huawei.
[2] RP-170238, “New SI proposal: Study on 3GPP V2X phase 3,” LG Electronics.
[3] RP-170042, “LS on eV2X Normative Requirements Completion,” SA1.