## Slide 1
NW assisted DL interference
mitigation – Motivation & Goals
RP-170257
3GPP RAN #75
Dubrovnik, March 6-9 2017
Qualcomm Incorporated

## Slide 2: Use case & Motivation/Goal
Ideal case Some real deployments
Use case: UMTS/HSPA deployments with adjacent-channel interference
If NW is aware of specific interference, it can improve UL performance. At the UE side, one way of mitigating DL adj. channel jamming would be to receive/decode with less interference signal, e.g. by appropriate Rx filtering.
=> It would be beneficial to introduce a signalling indication, from the network, to the UE informing about potential DL adjacent channel interference, so that UE could optimize DL performance

## Slide 3: Gains & Observations – Simulations / Lab tests
See Annex for other sim/test assumptions/results
[Reduced NB TX filter] | Legacy UE Rx filter | Optimized UE Rx filter
Geometry [dB] | Tput gains (%) [vs Ideal baseline] | 
0 | -14.5 | 2.6
3 | -17.5 | 0.1
8 | -25.1 | -2.9
15 | -38.9 | -8.5
20 | -49.1 | -15.5
Optimized UE Rx filtering is effective in rejecting the GSM interference.
900 MHz; GSM interference (200KHz) @ 2.2MHz from UMTS center carrier
GSM load ~50%. NB Tx filtering assumed to be reduced.
Baseline : Ideal case (200KHz guard band, Legacy Tx/Rx filtering
[Legacy NB TX filter] | Legacy UE Rx filter | Optimized UE Rx filter | 
GSM Tx [dBm] | Tput [Mbps] | Tput [Mbps] | Gain (%) [vs legacy
No Jammer | 12.9 | 12.8 | -0.78
-40 | 12.8 | 12.8 | 0
-30 | 11.9 | 12.5 | 5.04
-20 | 8.2 | 11.5 | 40.24
-10 | 2.3 | 8.2 | 256.52
Simulation (PA3 channel)
Lab Test
1900 MHz; GSM interference (200KHz) @ 2.2MHz from UMTS center carrier
Legacy NB Tx filtering
Direct comparison

## Slide 4: RAN#75 Proposal
Start a (small) Rel-15 Work Item
  RAN2 only, due in June ’17
  See WID in RP-170256
Main WI objectives, and specifications impacts, are:
  To introduce necessary RRC (DL) signaling for indicating adj. channel interference
  Add proper description of the feature in stage-2/3 specs.

## Slide 5: Annex – Lab/Sim assumptions & additional Sim. results

## Slide 6: Lab Tests
Network/Channel Parameters :
No. of cells – 1
DL Frequency – 1960 MHz
AWGN – OFF; Fading Channel – PA3
WCDMA power at the i/p of spirent : -20dBm
Jammer Parameters :
GSM Frequency bands : 1957.8 MHz (2.2 MHz away from the UMTS carrier)
Amplitude : Varied from -40dBm to -10dBm
Note: -20dBm is the signal power at the input of the SPIRENT test box where the GSM jammer to the WCDMA signal. Channel and cabling adds 35dB attenuation to that signal and the RSSI at the UE receiver is around -55dBm without any AWGN
Test Setup

## Slide 7: Simulations
Scenarios/Assumptions
Further Sim results

## Slide 8: Simulation Scenarios / Assumptions
Coexistence of UMTS 900 and GSM 900:
  UMTS occupies 4.2MHz in 900MHz band
  GSM occupies the neighboring 200KHz bands as the figure below
UMTS transmission power over 4.2MHz is equal to GSM transmission power in 200KHz
UMTS and GSM transmitters are collocated

## Slide 9: Simulation Scenarios / Assumptions (cont’)
Transmitter and receiver’s bandwidths are adjusted by controlling the RRC filter roll-off factor
Test cases:
  UMTS with 4.2MHz is sandwiched between GSM signals (as shown in previous slide)
  (NodeB) Tx filter roll-off factor = 0.05
  (UE) Rx filter roll-off factor = 0.05, 0.11, 0.22
Out of 8 GSM slots, 1, 3, 5, or 8 slots are always occupied during each simulation
Single Cell Geometries: 0, 3, 8, 10, 15, 20 dB
Channels: AWGN, PA3

## Slide 10: Simulation - Baseline
UMTS with 5MHz bandwidth is in between GSM signals with 200KHz guard band (recommended) as the figure below
Equal transmission power for UMTS and GSM
Tx filter roll-off factor = 0.22; Rx filter roll-off factor = 0.22

## Slide 11: Sim. Results - AWGN : Throughput gains w.r.t baseline (%)
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | -0.3 | 0.0 | -7.5
 | 3 | -0.1 | 0.0 | -8.4
 | 8 | 0.3 | 0.5 | -11.9
 | 10 | 0.9 | 1.1 | -16.8
 | 15 | -3.0 | -7.3 | -49.0
 | 20 | -3.3 | -5.8 | -63.0
1/8 GSM Slots
3/8 GSM Slots
5/8 GSM Slots
8/8 GSM Slots
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | -0.1 | -0.2 | -15.4
 | 3 | 0.1 | 0.6 | -15.2
 | 8 | 0.5 | 1.4 | -22.5
 | 10 | 1.7 | 3.6 | -25.5
 | 15 | -9.0 | -13.9 | -47.0
 | 20 | -16.6 | -22.2 | -59.6
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | -0.1 | -0.5 | -16.1
 | 3 | 0.4 | 1.0 | -21.0
 | 8 | 0.9 | 2.6 | -27.4
 | 10 | 3.3 | 4.9 | -35.1
 | 15 | -13.5 | -12.3 | -53.9
 | 20 | -22.6 | -25.8 | -63.3
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | 0.2 | -0.3 | -14.8
 | 3 | 0.4 | 1.0 | -21.5
 | 8 | 1.3 | 3.0 | -39.7
 | 10 | 4.0 | 4.6 | -42.3
 | 15 | -13.2 | -10.4 | -60.1
 | 20 | -13.9 | -24.7 | -67.9

## Slide 12: Sim. Results - PA3 : Throughput gains w.r.t baseline (%)
1/8 GSM Slots
3/8 GSM Slots
5/8 GSM Slots
8/8 GSM Slots
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | -3.0 | -1.3 | -4.4
 | 3 | -0.6 | -0.9 | -8.2
 | 8 | -2.7 | -3.1 | -18.1
 | 10 | -2.3 | -1.6 | -21.1
 | 15 | -5.4 | -7.2 | -37.5
 | 20 | -8.8 | -10.5 | -49.9
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | 0.0 | -0.3 | -9.7
 | 3 | 1.4 | -2.2 | -13.2
 | 8 | -2.5 | -4.4 | -21.3
 | 10 | -0.9 | -3.8 | -23.2
 | 15 | -4.1 | -6.8 | -34.6
 | 20 | -12.0 | -16.1 | -47.3
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | 2.0 | -3.1 | -14.9
 | 3 | 0.0 | -3.2 | -19.1
 | 8 | -2.2 | 0.2 | -29.7
 | 10 | -4.1 | -5.4 | -36.1
 | 15 | -7.6 | -11.9 | -46.8
 | 20 | -13.1 | -18.3 | -55.8
 |  | RRC filter roll-off factor |  | 
 |  | 0.05 | 0.11 | 0.22
Geometry [dB] | 0 | 2.6 | 0.3 | -14.5
 | 3 | 0.1 | -2.2 | -17.5
 | 8 | -2.9 | -3.8 | -25.1
 | 10 | -1.4 | -4.0 | -27.1
 | 15 | -8.5 | -9.3 | -38.9
 | 20 | -15.5 | -18.9 | -49.1