## Slide 1: Motivation for new WI proposal on Further NB-IoT enhancements
3GPP TSG RAN Meeting #75 RP-170337
Dubrovnik, Croatia, March 6-9, 2017
Agenda Item: 10.1.1
Source: Huawei, HiSilicon, Neul
Document for: Information

## Slide 2: Introduction
Rel-13 introduced the fundamental air interface and higher layers for NB-IoT
Rel-14 added some extra functions, e.g. firmware delivery, geo-location, load balancing…
NB-IoT should take every chance to give 3GPP and operators the maximum opportunity to adapt and offer ultra-low cost IoT to new customers and applications
  Standalone/guard-band operation mode improvements in readiness for deployment alongside NR
  Small-cell based relay coverage
  TDD support
Continued enhancements to underlying functionality to underpin an expanding ecosystem
  Cell access, small data transfer, idle mode (to reduce power consumption and latency)
  NPRACH range
  QoS definitions

## Slide 3: Deployment Flexibility

## Slide 4: Standalone operation mode (licensed UL & DL)
Motivation
  In-band operation mode was prioritized for design choices in Rel-13, with limited optimizations for the lower-interference case of standalone and guard-band.
    Standalone (licensed) mode needs to be attractive for deployment alongside NR, and for re-farmed GSM spectrum
  Non-anchor carrier operation is attractive for creating more capacity for unicast, as anchor carriers have heavy broadcast load, but standalone carriers cannot be combined with in-band/guard-band due to time limitations in Rel-13
Proposed objectives
  Use of all DL OFDM symbols for all physical channels and signals in standalone mode [RAN1]
  Signalling and requirements to support (a) standalone anchor with in-band/guard-band non-anchor and (b) standalone non-anchor with in-band/guard-band anchor carrier, without increasing the 20 MHz separation from Rel-13 [RAN2, RAN4]

## Slide 5: Small-cell deployment with NB-IoT backhaul
Motivation：
  In some scenarios, e.g. UEs deep underground may not be able to connect to NB-IoT macro eNB. However, the end user requires 100% coverage services. Small cells with multi-hops should be used in this scenario.
  NB-IoT macro cell and small cell provides a continuous wireless connection solution, so the UEs only need to support NB-IoT, which greatly reduces the cost of deployment.
Proposed objectives
  Introduce L3 relay node having RRC layer and lower, acting as a small cell to the next hop and a UE to the previous hop, and having no support of S1 and X2 interfaces [RAN2, RAN1]  See annex
  Relay nodes and eNB shall be able to differentiate between a normal UE and a small cell [RAN2, RAN1]
R13 NB-IoT
NB-IoT small cell（w/ R15 UE)
R13 NB-IoT
R13 NB-IoT
NB-IoT small cell（w/ R15 UE)
NB-IoT Macro

## Slide 6: TDD – Background
Support of TDD in NB-IoT was considered in Rel-13 and Rel-14, but not included due to time availability in WGs
  However, TDD spectrum exists globally, including regulatory environments and operator markets where there is strong un-met demand for NB-IoT
  This demand has existed since the early days of the Rel-13 evaluations phase, and there are competing non-3GPP technologies which could use TDD spectrum
  Competing M2M radio technologies around the world are not limited to FDD
  Rel-15 is the right time to add TDD support into NB-IoT, with the same deployment, cost, coverage, complexity, and capacity targets as HD-FDD

## Slide 7: TDD – Proposal
  Specify TDD support for in-band, guard-band, and standalone operation modes
  The design shall assume no UL compensation gaps are needed by UE, and strive towards a common design among the operation modes
  Relaxations of MCL and/or latency and/or capacity targets to be considered by RAN1 until RAN#76.

## Slide 8: Enhancements to basic functionality

## Slide 9: Power consumption reduction
Motivation
  In downlink command/data transmission, the latency is dominated by eDRX cycle, and the power consumption is dominated by the eDRX cycle and the paging.
  UE is required to perform cell re-selection measurements even when not moving, and the network topology is not changing
  Several messages have to be transferred when releasing an active UE into IDLE
Proposed objectives
  Specify physical signal(s) and/or channel(s) that can be efficiently decoded or detected prior to decoding the physical downlink control channel [RAN1,2,4]
  Reduced signalling during RRC connection release [RAN2]
  Enable relaxed UE monitoring for cell (re)selection e.g. by (re)configuration [RAN2,4]

## Slide 10: NPRACH enhancements
Motivation
  NPRACH sequence is [111…1], meaning the false alarm probability performance depends on the pseudo-random frequency hopping distance of NPRACH. This can bound the performance when repetitions are short.
  Rel-13 cyclic prefixes support cell radii of 10 km and 40 km, but some NB-IoT deployments will have good propagation over much longer distances, e.g. over large bodies of open water for ‘smart lakes’
Proposed objectives
  Introduce different NPRACH sequences than all-1s [RAN1, RAN2, RAN4]
  Introduce at least additional cyclic prefixes for NPRACH to support cell radius larger than 40 km [RAN1, RAN2, RAN4]

## Slide 11: QoS enhancements
Motivation
  QoS does not currently provide information relevant to NB-IoT such as latency, coverage enhancement authorization, power consumption need, etc.
  For scheduling the UE, it is beneficial to have eNB knowledge of the services, QoS requirements, priorities etc. of the UE and its service provider.
  With this information eNB can adjust its scheduling for a group of UEs according to their subscription or performance, e.g. VIP metering tenant vs. non-VIP tenant
  Multidimensional requirements exchange (coverage authorization, power saving preference, QoS, …) can enable service-based or tenant-based scheduling
  Proposed solution
  Define IE(s) carried on S1 interface to transfer from MME to eNB at least the UE characteristics related to: coverage enhancement authorization, power saving preference(s), and NB-IoT specific QoS requirement(s) [RAN3]
  See annex for an example of using a new SPID definition

## Slide 12: More efficient small message transfer
Motivation
  To send even the smallest messages, NB-IoT has to complete the RACH procedure
    Exchanges several messages with eNB unrelated to the size of the pending data, using UL and DL resources, and UE power consumption
  Data Volume Indicator (DVI) is carried in Msg3, or UE must wait for UL grant, taking time and power. LTE has dedicated SR in the physical layer for this reason.
Proposed objectives
  Support DL/UL data transmission during the Random Access procedure after Msg1, and before Msg5 [RAN2, RAN1]
    E.g. UL in Msg3 and/or DL in Msg4
  Support for dedicated SR [RAN1, RAN2]

## Slide 13: UTDOA
Motivation
  Benefits of UTDOA are well understood in terms of low UE complexity, no UE measurement effort, no UL reporting of measurements, and sophisticated network-side estimation algorithms
  Not introduced in Rel-14 due to artificial restriction to legacy physical signals, but solutions based on updated designs were also discussed showing their advantages
  Standardized interfaces are beneficial to allow network nodes to be provided by different vendors
Proposed solution
  Narrowband UTDOA positioning [RAN1,2,3,4]
    Using an existing, new, or updated UL NB-IoT signal
    Frequency hopping of the signal can also be considered

## Slide 14: Cross-carrier scheduling
Motivation
  Rel-13 RRC re-configures a UE from anchor to non-anchor carrier once. To change the non-anchor, UE must be dropped and re-access the cell. This was simple in PHY and expeditious for Rel-13 timeline.
  eNB typically has multiple non-anchor carriers (variable capacity provision, SC-PTM, Rel-14 paging/RAR), but scheduler cannot take advantage of dynamically available resources
Proposed solution
  Cross-carrier scheduling from anchor to non-anchor and non-anchor to non-anchor [RAN1, RAN2]
  Necessary physical control signalling, and monitoring, transmission, and re-transmission procedures [RAN1, RAN2]

## Slide 16: Annex – Example Subscriber Profile ID extension
IE/Group Name | Presence | Range | IE type and reference | Semantics description
Subscriber profile ID for NB |  |  | INTEGER (1..256) | 
> Coverage enhancement authentication | M |  | {ON or OFF} | Indicate whether allow to use coverage enhancement.
> power preference | M |  | ENUMERATED {normal, lowPowerConsumption, XX,XX} | Indicate the power saving preference
> NB QoS Information | O |  |  | Indicate the QoS requirement for different NB

## Slide 17: Annex – Small cell NB-IoT relay node
Support NB-IoT legacy UEs using CP solution to access the relay node
The relay nodes comprised of two parts:
  A small cell which only support air interface, no need support of S1/X2 interfaces.
  A UE part which support protocol stack from PHY, MAC, RLC and RRC.
Relay node works as L3 relay to forward the user data transparently.
Relay node is not visible from MME point of view.
Relay node maintains the backhaul link semi-statically by cell selection and reselection.
Backhaul link keeps in connected mode for long time to avoid frequent transition from idle mode to connected mode.