## Slide 1
Motivation for WI Proposal on Quality of Experience (QoE) Measurement Collection for streaming services in E-UTRAN
China Unicom, China Telecom
3GPP TSG RAN Meeting #75 RP-170434
Dubrovnik, Croatia, March 6 - 9, 2017
Document for: Discussion
Agenda Item: 10.1.2

## Slide 2: Background
Current status of the video experience evaluation specification
  ITU-T P.NATS (progressive download and adaptive type media streaming) has been discussing the model and evaluation of MOS models for streaming services. The related ITU standards have already been completed in December 2016
  A WI for improved QoE was approved (S4-160300 IQoE) in SA4#87, and the related QoE parameters to be captured have already been approved.
    SA4 has discussed how to introduce the P.NATS model to 3GPP world and found that 3GPP defined QoE in SA4 for the DASH streaming service (TS 26.247) has partially covered the related parameters defined by P.NATS (IQoE, TR26.909).
    At SA4#88 meeting, TR 26.909 v0.2.0 was agreed and it was found that I.11, I.12, I.13 and I.14 input for P.NATS are already covered by 3GPP defined QoE metrics.
  At RAN#73, a WI on QoE Measurement Collection for streaming services in UTRAN was approved (RP-161917).
    At RAN2 #97 meeting and the following email discussion, stage2 & stage3 CRs are approved. The resulting progress can be found in the Status Report and the WI summary of UMTS WI QMC (RP-17xxxxx, RP-17xxxxx)
  =>
Achievements of the video experience evaluation in ITU-T/SA4 are sufficient for the QMC, and we’ve done the UMTS related solutions

## Slide 3: Background
Introduction to the DASH structure
  PSS architecture defined in TS 26.233 supports both progress download and 3GP-DASH(two typical streaming transmission types defined in TS 26.247). 3GP-DASH structure is shown as
  MPD: A media presentation description (MPD) describes segment information (timing, URL, media characteristics like video resolution and bit rates.)
*PSS stands for Packet Switched Streaming Service, which aims at defining the communication protocols between streaming client and server.

## Slide 4: Background
4
QoE Measurement Collection issue
  In TS 26.247, the Quality Reporting Scheme for DASH is defined, and the right figure shows how it works. This Quality Reporting can be configured by either MPD or OMA-DM.
  For MPD, the operator has to request the OTT player to configure QoE metrics in each MPD and thus it is complicated.
  For OMA-DM, it isn’t widely supported by operators yet, so it is impossible for the QoE server to collect QoE metric reports from the PSS client.
*OMA-DM is a device management protocol specified by the Open Mobile Alliance (OMA) Device Management (DM) Working Group and the Data Synchronization (DS) Working Group.
=>
New approach needs to be investigated to allow operators to collect QoE measurements easily for streaming services

## Slide 5: Background
Chaos and inaccuracy of QoE measurement
  Operators now have limited ways to collect the QoE parameters. All of possible ways do not have unified QoE measurement, which achieve diverse understanding of user experience.
  All the feasible ways for QoE measurement do not involve RAN, which actually impact UE experience much.
  It is beneficial to introduce the QoE Measurement Collection for streaming services in LTE RAN.
    It provides means for operators to better understand the user perception and try to find some convenient ways to figure out the problems of user experience on streaming services.
    Based on both QoE and RAN information, operators could choose the appropriate way for network optimization and enhance user experience.

## Slide 6: Motivation
Accurate, cost efficient and unified UE experience evaluation
  Currently, if operators want to know the user experience for streaming services at UE side, one possible way is to install an APP on each UE, which costs some extra expense and more efforts. While UEs might not have willing to report user experience related information, because it is not clear on the motivations, e.g. what rewards will be got from UE point of view.
  Operators regard streaming services (typically video services) as the key booster of the commercial outstanding performance growth rate, customers’ experience should be focused on. The evaluation of UE experience is vital to operators.
  Operators can utilize QoE measurement to evaluate user experience accurately. By correlating QoE measurement with radio parameters, operators can optimize the network accordingly to achieve better user experience .
Applicable to E-UTRAN
  QoE Collection in UTRAN has been specified in the UMTS WI QMC, which is complete.
  E-UTRAN is the main network for streaming services. It should be considered as well.

## Slide 7: Benefit for Operators
QoE measurement parameters
  Network can achieve not only the final evaluation result of streaming services (e.g. video MOS), but also the related parameters for calculation of the final evaluation (e.g. QoE measurements), which can be combined with radio measurements for better understanding of real UE experience.
    The network optimization related parameters
    Whether the terminal or the streaming original quality of the network which impacts
Network control
  Operators could control when, where and how often to collect QoE measurements, for the needs may vary from place to place and the video MOS calculation based on QoE is the trade off between UE/network burden and its usefulness.
Unified metrics
  Both a unified interpretation of video MOS and Unified QoE metrics are beneficial for operators to evaluate real user experience on streaming services.
Network optimization
  Operators can optimize the networks for better user experience according to the collected QoE measurements combining with radio measurements.

## Slide 8: Objective and Scope
The objective of this work item is to determine
  RAN collects QoE measurements for streaming services from the UE side
  The trigger and measurement reporting procedures of QoE measurements for streaming services
The following principles should be followed when developing the QoE Measurement Collection solutions:
  QoE measurements are configured to the UE by E-UTRAN by RRC signaling, based on Network management systems measurement definitions configured to E-UTRAN. QoE measurements may be triggered by various rules, e.g. based on cells.
  The QoE measurement reports are sent via RRC signaling to the E-UTRAN. RRC signaling to report QoE measurements should also consider the SA4 progress on IQoE (S4-160300), e.g. specific QoE measurements/ metrics
  Also basic measurement objects are to be identified, which may be added to the results such as Cell ID, time (if relevant) before being transferred onwards to the respective MDT-entity (or other possible entities) outside the E-UTRAN
  Some metrics may be considered when analyzing the solutions, e.g., latency, capacity, impacts to other groups and the uncertainty of the solution in 3GPP scope.

## Slide 9: Objective and Scope
For the above-mentioned, the work should follow the detailed work plan listed below:
For RAN WG2:
  Define the procedures for configuration and reporting of QoE measurements by using RRC.
  Definition of the delivery functionality towards O&M in co-operation with TSG SA WG5, if needed.
For RAN WG3:
  Define necessary E-UTRAN functionality for QoE Measurement Collection for the interfaces under RAN3 responsibility, it depends on RAN2 progress on solutions.
  Definition of the O&M requirements for the handling of the UE and E-UTRAN measurement data.
Coordination between RAN2 and CT1/SA4/SA5 may be needed when designing the solutions. Also, the potential solutions are generally non user consent for more efficient deployment. Possible optimization of the QoE configuration and reporting should be considered.
*Note: Existing MDT framework should be taken as a baseline.
*Note: Existing MDT framework should be taken as a baseline.

## Slide 10: Time budget proposal
RAN #74 Q3/2016 RAN #75 Q4/2016 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf | R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf
88 | 88 | 97 | 97 | 97 | 95 | 82 | 82 | 82 | 82 | 88bis | 88bis | 97bis | 97bis | 97bis | 95bis | 82bis | 82bis | 82bis | 82bis
 |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  | 
L: LTE, U: UMTS, J: Joint, RD: RRM/demodulation
Q4/2016 RAN #76 Q1/2017 RAN#77 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf | R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf
89 | 89 | 98 | 98 | 98 | 96 | 83 | 83 | 83 | 83 | 90 | 90 | 99 | 99 | 99 | 97 | 84 | 84 | 84 | 84
 |  | 1 |  |  | 1 |  |  |  |  |  |  | 1 |  |  | 1 |  |  |  |