## Slide 1: Study on a simplified HS-SCCH for UMTS
RP-170519 - Motivation for New proposed SI

## Slide 2: Background (1/2)
The HS-SCCH is a downlink control channel used for scheduling HS-DSCH transmissions, as well as for instructing the UE to perform specific actions via HS-SCCH orders.
The HS-SCCH is monitored by the UE at all path-loss conditions within the cell, however according to current observations the HS-SCCH becomes costly in bad radio conditions, which puts a limitation on its usability.
Being more specific, in bad radio conditions the power invested in the control information bits carried on the HS-SCCH limits the available power for the HS-PDSCH.

## Slide 3: Background (2/2)
The decoding of the HS-SCCH is performed by testing against all the codewords that can be carried over the HS-SCCH since any of those codewords could have been transmitted in downlink. Nonetheless under bad radio conditions only small subset of those codewords can occur in practice.
This is something that can be considered to enhance and simplify the decoding of the HS-SCCH channel.

## Slide 4: Proposed RAN Work Item
Study the feasibility and benefits of introducing a simplified version of the HS-SCCH Type1 where some of the control information bits carried on the HS-SCCH part I are made deterministic (e.g., CCS bits and MS bit). The following aspects shall be taken into consideration:
  The L1 processing chain as described in the current UMTS standard shall be reused and no changes are allowed (i.e., adding/removing blocks to the L1 processing chain is not allowed).
  Keep backward compatibility (e.g., re-ordering bits within a slot, or from one to another slot is not allowed).
Study mechanisms for triggering the usage of the simplified version of the HS-SCCH Type 1, if possible by making use of legacy mechanisms.

## Slide 5: benefits
The main advantages of using a simplified HS-SCCH are the following ones:
  Better performance in poor radio conditions
    Improves BLER
    Improves Miss detection Performance
    Improves False detection Performance
  Power savings in DL (can be translated to coverage improvements)
  Backward compatibility: The gains will be seen for the Rel-15 UEs, while legacy UEs can decode the HS-SCCH as usual providing the legacy performance.
  Minimum standard impact (the HS-SCCH ”L1 processing chain” is not modified at all).