## Slide 1
Source: Samsung
Motivation for new WI:
Even further enhanced MTC for LTE
RP-170679
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, March 6 - 9, 2017 Agenda item: 10.1.1 Document for: Discussion

## Slide 2: Justification
eMTC aligns with mMTC requirements
  eMTC was specified in Rel-13 and further enhanced in Rel-14, targeting to IoT/MTC business, with extended coverage, longer battery life, and low complexity device.
  It was agreed that “3GPP’s IMT-2020 self-evaluations towards mMTC requirements will assess NB-IoT
  and/or LTE eMTC”.
IoT/MTC marketing is maturing
  Global operators start to launch cellular IoT/MTC service with eMTC.
  Massive connections of IoT/MTC device will be the challenge in the near future.
Further enhancement on eMTC in Rel-15
  Study the feasibility and, if appropriate, specify the enhancements targeting to mMTC requirements.

## Slide 3: Gap of NB-IoT and eMTC for mMTC
eMTC to 5G mMTC
  ~5dB gap on coverage.
  Some gap on Battery life is expected.
  No evaluation on latency.
KPI | 5G mMTC | eMTC
Coverage | 164dB with 160bps (with 5dB/9dB noise figure) | 155dB MCL (with 5dB/9dB noise figure)
Battery life | Beyond 10 yrs with UL 200 bytes per day followed by 20bytes DL from MaxCL of 164dB | Provide power consumption reduction, to target ultra-long battery life.
Latency | <10s with 20 bytes application package @ 164dB MCL | Need to be evaluated.
Connection density | 1 000 000 device/km2 | To meet the requirement, several sub-bands are needed.
Low cost | Ultra-low cost devices | low complexity UE category/type
Positioning and multi-cast | Supported positioning and multi-cast | Supported

## Slide 4: Massive connections
Motivation:
  To meet mMTC connection density (1e6 per sq km) requirement, several narrow bands are needed, which may impact on human-centric communications.
  Congestion control is needed to handle massive connections.
Possible solutions:
  Enable operating eMTC in unlicensed spectrum to offload the connections.
  UE group scheduling to reduce control overhead and UE power consumption.
  Improved link adaptation for UEs with no or with small coverage enhancements.
  Congestion control.

## Slide 5: Latency reduction and 10 years battery life
Motivation:
  It is required to support less than 10 seconds latency for exception report in extreme coverage.
  Cell search for UEs in extreme coverage can take a long time, e.g., up to 2 seconds, which also results in a high UE power consumption.
  There is no evaluation on battery life for eMTC.
Possible solutions:
  Early termination of uplink and downlink data transmissions with a compact DCI or non-adaptive HARQ.
  Mechanisms to enable data transmission/reception without RRC transition to connected state.
  Enhancements for cell search.

## Slide 6: Coverage
Motivation:
  eMTC can only support 155dB MCL.
  Feasibility study is needed for eMTC to meet 164dB MCL.
Possible solutions:
  Enhancement of DL common channels/signals.
  Specify more repetitions or other techniques (e.g., PSD boosting, channel estimation enhancements, link adaptation enhancements) to further improve coverage of unicast channels.