## Slide 1: Architecture Requirements and Use Cases for Next Generation Access
AT&T
3GPP RAN Ad-Hoc – Next Generation Access
January 28-29, 2016; Barcelona, Spain

## Slide 2: Key Aspects and Drivers for Next Gen Access Architectural Requirements:
NFV based architecture allows rapid deployment of features and services
Flexible HW implementations allows scalable cost effective solutions
  Hierarchical architecture allows for coordination for performance features, load management, and enables NFV/SDN
Configurable functional splits enables adaptation to variable latency on transport
  Integrated backhaul and multi-hop capability supports easier path to network densification
Edge Analytics per user and application – supports metrics, KPIs, QoS, and real-time performance optimization
Support of Network Slicing
Regarding 5G Access Integration with Legacy Systems:
During development of LTE in 3GPP, for its coexistence with legacy 3GPP technologies a tight coupling approach for 2G/3G was adopted that resulted in an increased packet core complexity involving interworking between 2G/3G and EPC packet core entities. A tight coupling of new 5G packet core with legacy RANs would result in introduction of similar complexities as was seen in LTE and 2G/3G interworking

## Slide 3: NGMN Architectural Requirements
NGMN whitepaper lists several key requirements relevant to 5G System and Packet Core including the following:
  A functional decoupling of Core and RAN network domains
  A RAN technology agnostic architecture where introduction and connection of new radio technology will be possible in a plug and play manner
  Independent evolution of core and RAN network domains should be possible.
  C- and U-plane functions should be clearly separated, with open interfaces defined between them, in accordance with SDN principles.
  A decoupling of Hardware and Software functions of network elements in all network domains.
  Cost and effort efficient upgrade path so that Operators can leverage significant investments into existing operational infrastructure and maximize its utilization.
  Real-time and on demand network configuration and automated optimization.
  Flexible and cost efficient network operation.
  Maximize utilization efficiency of available network resources.
  Dynamic relocation of network resources, fully controlled by operator.

## Slide 4: 4GA Architectural Requirements
4G Americas also lists several 5G requirements that are relevant to development of a next generation of packet core:
  The 5G network architecture should be such that the air interface and the core network can evolve and scale independently of each other.
  Changes/enhancements to one domain should not mandate changes/enhancements to the other.
  5G networks must also support multi-RAT connectivity efficiently and effectively.
  Provide access agnostic packet core across multiple Radio Technologies (e.g. cellular, Wi-Fi, etc.) to support uniform Authentication, Session Continuity, and Security across radio technologies.
  Provide Plug and Play capability where a new access technology may be attached to the packet core without any modifications.

## Slide 5: AT&T Proposed - Next Gen RAN Architecture Requirements
The RAN architecture shall support deployment based on network function virtualization (NFV)
The 5G RAN shall support a hierarchical logical architecture (instead of a LTE-like flat functional architecture) while still meeting the latency and throughput requirements
Functional splits within RAN shall be dynamically re-configurable down to level of network slice and bearer
    5G RAN must have tight integration with LTE-Advanced while avoiding CN complexity; LTE Advanced should support a new control plane to connect natively to 5G CN
    5G RAN interworking with legacy 2G/3G MAY not require tight coupling
    For 5G RAN-CN interface / Interworking - NGMN preferred Option 3 should be the way forward
    Support forward compatibility; any current development/releases should facilitate and not preclude reaching the full set of capabilities

## Slide 6: RAN Architecture Details (1 of 4)
The functional splits within RAN (e.g. between a central unit and remote unit) shall be re-configurable (RRC reconfig) and should support and adjust to variable latency budget on the transport
    This implies that a strict timing relationship between various L1/L2 procedures on the control and data plane should be avoided.
    E.g. RRC configurable asynchronous HARQ timing, RRC configurable shift between UL and DL frames timing, RRC configurable asynchronous measurement/reporting (CSI, RRM) (not an exhaustive list)
Separation of the control plane and user plane
All the architecture options as indicated in the following slides should be evaluated
Forward Compatibility - any current development/releases should facilitate and not preclude reaching the full set of capabilities.

## Slide 7: RAN Architecture Details (2 of 4)
Possible logical architecture of 5G RAN (Option 1)
CU-CP
eX3
eX2
C-Plane
eS2 control plane
eS1 control plane
RU
C-Plane
U-Plane
U-Plane
eS1 user plane
eS2 data plane
CU-DP
RF
To Core
To Other CU
RAN is logically split between a central unit (CU) and a remote unit (RU)
The interface from the RU to the CU is split between the control plane and data plane
The control plane and data plane components of the CU are split into two separate logical entities CU-DP and CU-CP with an interface between them
Flexible design allows U-Plane/C-Plan functions to move between CU and RU per bearer

## Slide 8: RAN Architecture Details (3 of 4)
C-Plane
eS2 control plane
eS1 control plane
RU
C-Plane
U-Plane
U-Plane
eS1 user plane
eS2 data plane
CU
RF
To Core
To Other CU
Possible logical architecture of 5G RAN (Option2)
eX2
RAN is logically split between a central unit (CU) and a remote unit (RU)
The interface from the RU to the CU is split between the control plane and data plane
No defined interface between U-Plane and C-Plane
Flexible design allows U-Plane/C-Plan functions to move between CU and RU per bearer

## Slide 9: RAN Architecture Details (4 of 4)
C-Plane
eS1 control plane
RU
C-Plane
U-Plane
U-Plane
eS1 user plane
eS2
CU
RF
To Core
To Other CU
Possible logical architecture of 5G RAN (Option3)
eX2
RAN is logically split between a central unit (CU) and a remote unit (RU)
Flexible design allows U-Plane/C-Plan functions to move between CU and RU per bearer

## Slide 10: 5G RAN-CN interface / Interworking
Full Diagram: Link:
NGMN 5G White Paper
Sec 5.5 Figure 10
- AT&T desires NGMN Option 3 as way forward

## Slide 11: Operational Requirements: It is proposed to add the following text to the Operational Requirements Section of the TR:
The 5G RAT shall support integration of backhaul and access and support multi-hop configuration.
    Whether this is a L2 multi-hop or L3 multi-hop is FFS at this point. Possibly both should be evaluated.
    The integrated backhaul shall support and be optimized for both the eS1 interface as well as the eX2 interface (see RAN architecture diagram)

## Slide 12: Summary of Architectural Requirements: It is proposed to add the following text to the Architecture Section of the TR:
The RAN architecture shall support deployment based on network function virtualization (NFV)
The 5G RAN shall support a hierarchical logical architecture (instead of a LTE-like flat functional architecture) while still meeting the latency and throughput requirements
Functional splits within RAN shall be dynamically re-configurable down to level of network slice and bearer
    5G RAN must have tight integration with LTE-Advanced while avoiding CN complexity; LTE Advanced should support a new control plane to connect natively to 5G CN
    5G RAN interworking with legacy 2G/3G MAY not require tight coupling
    For 5G RAN-CN interface / Interworking - NGMN preferred Option 3 should be the way forward
    Support forward compatibility; any current development/releases should facilitate and not preclude reaching the full set of capabilities

## Slide 13: 5G Capability Perspectives from the ITU-R IMT-2020 Vision Recommendation
Fig 3. Enhancement of key capabilities
from IMT-Advanced to IMT-2020
The values in the Figure 3 above are targets for research and investigation for IMT-2020 and may be further developed in other ITU-R Recommendations, and may be revised in the light of future studies..
Additional descriptions and further details for both Figure are in the IMT-2020 Vision Recommendation (Recommendation ITU-R M.2083)
Fig 4. The importance of key capabilities in different usage scenarios

## Slide 14: AT&T Proposed Use Cases for the RAN Study Item For Proposed Inclusion Use Case Section in TR:
Terrestrial HetNet with Macro and Pico cells
Vehicular (V2V & V2I)
In Flight
High Speed Train
AdHoc Network (out of coverage D2D)
Massive MTC
Critical MTC and Industrial Automation
Mobile broadcast services (eMBMS)
Fixed Access
Internet of Things
Extreme Video and Gaming Applications
Explosive Data Density Usage
Public Safety
Context Aware Services

## Slide 15: THANK YOU