## Slide 1: WF on Handling of PSS/SSS and DM RS in NCT
Intel Corporation, Samsung, InterDigital Communications, ITRI, Broadcom, NEC, ETRI, III
3GPP TSG RAN WG1 Meeting #69
Prague, Czech Republic, May 21st – 25th, 2012
R1-123012

## Slide 2: Proposals
No new DM RS pattern is introduced in Rel-11 for NCT.
  Existing DM RS patterns are kept in any type of subframes.
For FDD, SSS and PSS are transmitted in OFDM symbol 1 and 2, respectively and are transmitted in the first slot of subframe 0 and 5 with normal and extended CP.
For TDD,
  The OFDM symbol spacing and ordering between SSS and PSS are same as Rel-8.
    SSS precedes PSS.
    There are two OFDM symbols between SSS and PSS.
  On time location of SSS and PSS,
    The exact time location will be decided in RAN1#70.