## Slide 1: 3GPP Rel12 prioritization
Telecom Italia
3GPP SA#58 - Release 12 Workshop
10th December 2012

## Slide 2: Telecom Italia priorities
New revenue streams for LTE
  Public Safety & Mission Critical comm.
Network congestion
  Solutions to cope with data/signaling traffic growth, e.g. due to smartphones.
Network rationalization (CAPEX and OPEX reduction)
  Fixed/mobile policy convergence
Note: this presentation focuses on SA2 work streams, where overload issues are more likely to happen

## Slide 3: Public Safety & Mission Critical Communications
Many national and international Public Safety organisations have endorsed or are considering LTE as the next generation technology either to augment their existing systems, or to provide a future migration path
New revenue streams from TETRA replacement for LTE
  Not just Public Safety: Transportation, Utilities, Government, …
Requirements not met by current LTE operations (i.e. not covered by current 3GPP specs)
  Direct mode & Group communications
  Network availability and resilience
  Operation within extreme temperature ranges
  UE operation in receive-only mode in particularly sensitive environments
  Interoperability with existing public safety networks and devices
  ….
  A complete Public Safety & Mission Critical requires a 3GPP-wide coordinated effort (Radio & System)
  A specific umbrella WID for P.S. is needed
  Rel-12 ProSe activity should focus on public safety only
Priority: umbrella WID on Public Safety & related B.Blocks (Public Safety ProSe, GCSE_LTE, possibly others)
NEW WIDs!!

## Slide 4: Solutions to cope with data/signaling traffic growth
Intelligent offload of traffic to WLAN accesses
  We believe that the existing solutions for the interconnection of WLAN accesses with the EPC are sufficient
  more work is needed on WLAN policies, so that the operator can achieve better control on access network selection via the ANDSF
Priority: WLAN_NS; WS_WORM (part related to the inclusion of the RAT type in the ANDSF policies)
Handling/avoidance of congestion situations in 3GPP accesses
  handling of user plane congestion (User Plane Congestion, UPCON WID)
  handling/avoidance of signaling plane congestion (“Core Network Overload ”[FS_CNO] and “Machine-Type and other mobile data applications Communications enhancements” [MTCe])
Priority: UPCON; FS_CNO; MTCe

## Slide 5: Fixed-mobile policy convergence
  Extension of PCC framework for supporting fixed use case scenarios is seen as a benefit to provide a cost effective solution for single operator owning both the EPC and fixed broadband accesses
  reduce the cost of ownership of the network enabling the usage of a single policy framework to address the evolution of new services
  High priority on PCC for fixed terminals; low priority on PCC for Non-Seamless WiFi Offload traffic from 3GPP UEs in fixed broadband access
Priority: P4C-F, Policy and Charging Control for supporting traffic from fixed terminals

## Slide 6
Thank You !
Telecom Italia