## Slide 1: 3GPP and NFV

## Slide 2: Architecture mapping

## Slide 3: NFV architecture (work in progress)
VNF
Manager
NFV
Orchestrator
Virtual
Infrastructure
Manager
NFVI
VNF
domain
OSS/BSS
Os-Nfvo
Nfvo-Vnfm
Vnfm-Vi
Nfvo-Vi
Vn-Nf
VeNf-Vnfm
Nf-Vi
NS Catalog
VNF Catalog
NFV Instances
NFVI Resources
VNF
EM
Based on NFV ISG Management and Orchestration Working Group GS
NMS
VeNm-Vnfm

## Slide 4: NFV architecture (work in progress)
VNF
Manager
NFV
Orchestrator
Virtual
Infrastructure
Manager
NFVI
Enterprise Systems
NS Catalog
VNF Catalog
NFV Instances
NFVI Resources
MME
Based on NFV ISG Management and Orchestration Working Group GS
Network Manager
SGW
PGW
Element Manager
Element Manager
Element Manager

## Slide 5: Status of NFV work Gap analysis
This is a key part of the group’s work
Will identify what work is required in other bodies in order to meet the NFV ISG requirements
Output from the WG’s so far is mixed, and certainly not complete
The TSC will coordinate engagement with the external bodies, but clearly there will need to be member company participation in each of them to move work forward

## Slide 6: NFV schedule for 2014 Meetings and targets
WG approval of all documents by mid-June (and available in public area after that)
Process of alignment across all documents until NFV#8
Formal publication of documents in December 2014
Each of the WG’s is doing a gap analysis to identify which standards might be impacted – planned completion by NFV#6
Jan 14 | Feb 14 | Mar 14 | Apr 14 | May 14 | Jun 14 | Jul 14 | Aug 14 | Sep 14 | Oct 14 | Nov 14 | Dec 14 | Jan 15 | Feb 15
NFV#5
SA#63
NFV#6
NFV#7
NFV#8
SA#64
SA#65
SA#66
NFV#9
SA2
SA2
SA2
SA2
SA2
SA2
SA1
SA1
SA1
SA1
SA2
SA1
SA5
SA5
SA5
SA5
SA5
SA5
SA5

## Slide 7: Impacts on 3GPP Core network
There are characteristics of virtualized deployments that open up new possibilities
  Easier to instantiate a new EPC entity, or entire EPC
  More flexible scaling of EPC entities
  Common deployment environment
In general these seem to be independent of changes to 3GPP interfaces and entities, since our architecture is largely implementation-independent

## Slide 8: Impacts on 3GPP Core network
Looking forward, it seems that new work items for 3GPP could be classified as one of the following:
  Virtualization-specific enhancements/optimizations of the existing logical architecture
  Use cases/features that are made easier/more feasible by virtualisation deployments
  Use cases/features that are independent of whether the deployment environment is virtualized or not
  Re-architecture of the core network (motivated by virtualisation, or other drivers)
The first item could be a tightly-scoped Release 13 study item, if there is sufficient support
Items 2 and 3 should be handled on a case-by-case basis as we do now
Item 4 is clearly a very significant undertaking, and in our view is something to look at in the longer-term

## Slide 9: Impacts on 3GPP Core network
If there is sufficient interest then we suggest starting a Study Item in SA2 in Release 13
SA2 need not necessarily wait for the NFV ISG work to complete
  But if they do identify gaps then these could be considered (input as company contributions in the normal way)
Other groups could be involved as necessary as the study progresses
The scope should be such that the existing logical architecture (functional entities and reference points) is preserved
The focus would be on investigation into new or modified procedures that might help optimize deployment of core network entities in a virtualization environment

## Slide 10: Impacts on 3GPP OA&M
OA&M has been suggested as an area where there might be most impact on 3GPP (i.e. SA5)
At time of writing the NFV MANO WG has not documented possible impacts on 3GPP (but it has identified gaps for OASIS and TMF)
It seems the mapping of the NFV architecture to the SA5 architecture is not yet well understood
Work in SA5 shouldn’t start until the NFV ISG has largely finished its own work, and this looks likely to be mid-June 2014

## Slide 11: Impacts on 3GPP Relationship with 5G
Discussions about 5G are starting to gain momentum in the industry
  But it seems unlikely that 3GPP would start a study item before Release 14
  Normative work might then translate as being in the Release 15 timeframe
Virtualization is a deployment option now and lessons will be learnt as VNFs are deployed
Can expect that as 5G is developed, a virtualized deployment will be the deployment scenario
  This knowledge is likely to have an impact on any new architecture
  Development of 5G seems to be the appropriate time to incorporate new architecture thinking around virtualization into 3GPP

## Slide 12: Impacts on 3GPP Keeping up with pace of feature deployment
  One characteristic of virtualized deployments should be more rapid deployment of new features
  If this is the case then standardisation of these features might need to be accelerated
  The current release-based process in 3GPP seems unlikely to cope with a significant acceleration of current timescales
  Alternative approaches are worth exploring (eg feature-centric planning)

## Slide 13: Impacts on 3GPP Summary of Cisco position
  We expect impacts on EPC architecture and protocols to be minor in the short term (Release 13)
  The impact on OA&M (SA5) might be more significant, but the NFV ISG has yet to complete its gap analysis
  Longer term, 5G development in 3GPP would need to target virtualized deployments and this might be the opportunity for more fundamental reworking of the architecture if deemed necessary
  3GPP Process changes might be needed to keep pace with feature development and deployment