## Slide 1: KDDI Release 16 Focus Area
SP-180301 13 June 2018
Yusuke Nakano
KDDI Corporation

## Slide 2: Items RAN-SA Coordination Needed
QoS_MON (SA1)
  Justification: To ensure E2E QoS for URLLC use-cases, it is necessary to consider the requirements and solution in system-wide manner.
  Potential impacts in RAN: All the objectives which are identified in the WID (i.e., monitoring, assurance and reporting) have impact in RAN.
FS_ID_UAS (SA1)
  Justification: UAS is one of the most promising-looking use-cases. For the remote identification and tracking of UAS linked to 3GPP subscription, it is essential to consider in the 3GPP system wide manner.
  Potential impacts in RAN: Based on the stage 1 requirement discussion, some of contents of identification data (e.g., UAV route data or UAV location) may have impact in RAN.
FS_5G_URLLC (SA2)
  Justification: To meet the URLLC requirement specified in TS 22.261, it is necessary to consider the solutions in system-wide manner.
  Potential impacts in RAN: To minimize the latency and jitter between AN and CN in UE mobility, to realize high reliability in transmission of N3 u-plane tunnel and monitoring E2E QoS have impact in RAN.

## Slide 3: Items with No RAN Impact
FS_LUCIA (SA1)
  Justification: Consideration for next generation identification is one of the most critical issues especially for IoT devices. This discussion is derived from the GSMA requirement.
FS_eNA (SA2)
  Justification: The enhancement of NWDAF functionalities is key issue for the NW automation which enables for operators to provide NW services in TTM manner. Couple of enhancements in this study can strengthen the flexibility and diversity of 5GC e.g., customized mobility management, dynamic traffic steering or resource management based on the service classification.
eSBA (SA2)
  Justification: Rel-15 SBA has couple of remaining issues like realization of fully stateless architecture and enhancement of NRF. Further discussion is necessary to mature the 5GC.

## Slide 4: Items with No RAN Impact
FS_eNS (SA2)
  Justification: The consideration for international roaming case and further enhancement aligned with diversified industry collaboration are needed in the NW slice discussion. This study has a potential to enhance the NW slice functionality defined in Rel-15.
FS_ENTRADE (SA2)
  Justification: The enhancement of charging flexibility enables operators to provide diversified services for the customers. Monitoring HTTPS traffic
DPBDT (SA2)
  Justification: The automotive industry is changing significantly with 5G. The traffic from automobiles increase continuously. It is necessary for operators to manage the traffic and maintain other service quality. This item is important to control the automobiles’ UL/DL traffic via efficient policy delivery.

## Slide 5
Thank you!