## Slide 1
Discussion on Long Range Cell Operation for ProSe
Yi-Hsueh Tsai, lucas@iii.org.tw Hsuan-Li Lin, Tsung-Yu Tsai, Terng-Yin Hsu, Jian-Ya Chu
Shubhranshu shubhranshu@itri.org.tw Zheng Yan-Xiu zhengyanxiu@itri.org.tw
3GPP TSG-SA WG1 Meeting #66 S1-141009 Sapporo, Japan, 12-16 May 2014
Agenda Item 5.2 - New Study and Work Items (including related contributions)
Source: III, ITRI

## Slide 2: Long Range Cell Operation
Possible usage scenarios of Long Range Cell Operation (e.g. 10-100km [1][2])
Difficulty deployment territory
  In areas such as mountain areas, jungles, deserts, or islands, long range cell can provide broadband wireless access solution with good coverage under reasonable cost.
Disaster first responder (Public Safety)
  In major disaster, the ground based communication infrastructure may suffer a severe destruction. In such cases, long range cell could be quickly deployed to temporarily replace the ground communication infrastructure and fast recover the wireless networks to enable critical information access such as the communication for rescue mission, or emergency services.

## Slide 3: Long Range Cell Operation for ProSe
Partial Network Coverage Area: A network coverage area where UE can only listen to the eNB.
ProSe Communication
Oscar
Dashed line shows effective uplink coverage contour
eNB with limited backhaul such as satellite link
Infrastructure Communication
Roger
Peter
UE-to-network relay does not need to relay the downlink traffic in order to efficiently utilize the radio resource
UE outside the uplink coverage contour could receive synchronization signal, system information block, and semi-persistent resource management information for establishing ProSe communication
Partial network coverage area

## Slide 4: Discussion and Proposal
In TR 23703, it mentions that we have to handle out of network coverage scenarios for proximity direct communication in rural area. Therefore, long-range cell is proposed to reduce network converge holes, and thus the phenomenon can be significantly mitigated especially in the rural area.
Although, for receivers located in the fringe areas outside the coverage contour can only receive outbound communication, those UEs can still obtain synchronization signal, system information block, and semi-persistent resource management information for establishing direct communication.

## Slide 5: Discussion and Proposal
However, the UE relay, which does not need to relay the downlink traffic in order to efficiently utilize the radio resource, could be used to extend the uplink range using the direct communication link between UE located inside the coverage contour of the system and UE located in the fringe areas outside the coverage contour.
Therefore, if long range cell communications systems were available, it can ensure the direct communication between Public Safety officers within its coverage.
We propose S1-141010 with additional SA1 requirements for public safety to expand the cell range by improving UE's UL connectivity in partial coverage scenarios.

## Slide 6: References
REV-090003-r1, “LTE-Advanced Physical Layer”
LTE The UMTS Long Term Evolution from Theory to Practice Ed2