## Slide 1: Discussion on eV2X Rel-15: Rel-14 achievement and Rel-15 enhancement plan
LG Electronics Inc.
3GPP TSG-SA WG1 Meeting #74 S1-161231
Venice, Italy 9-13 May 2016 (revision of S1-16xxxx)
Title: Discussion on eV2X Rel-15 (Rel-14 achievement and Rel-15 enhancement plan)
Agenda Item: 5
Source: LG Electronics Inc.
Purpose: Discussion
Contact: Ki-Dong Lee <kidong.lee (at) lge.com>

## Slide 2: Contents
Review of Rel-14 V2X (based on TS*)
  What we have in R14 V2X
  What we don’t in R14 V2X and what we will have via FS_SMARTER
Preparations for Rel-15
  Scope (proposed)
  Time schedule
  Note [*]: as of Apr’16 when this contribution is prepared, V2X Normative Work is 90% complete with possible editorial changes (10%), if needed. The “review of Rel-14 V2X” is therefore based on the outcome of Normative Work (V2XLTE), which TS (3GPP TS 22.185) was approved in SA#71 (Mar.’16).
  Disclaimer: This paper is in part (e.g., Review of Rel-14 V2X) based on LGE’s previous TDoc (S1-160111).

## Slide 3: Prologue (1/2)
R14 V2X Completion: The normative work on Rel-14 V2X (V2XLTE, SP-150573) has completed and the TS 22.185 was approved in SA1#71 with completion rate of 90% (10% for Cat.F CR only, if needed).
To-do for an agreed Working Assumption: While working on Rel-14 V2X, SA1 has also been working on V2X-related topics in FS_SMARTER, which were considered as enhancement for the V2X Rel-14, and the related TDocs were agreed to put on hold until Rel-14 V2X is complete (working assumption made in SA1#71bis adhoc, Vancouver, BC, Canada).
To-do for 5G (e.g., New RAT): Along with the emergence of 5G through 3GPP RAN WS and through many Whitepapers, it is necessary to perform study on enhancement of the Rel-14 V2X in the context of 5G. The currently defined KPI goals in Rel-14 V2X will be re-evaluated from the perspectives of 5G (e.g., services over 3GPP RAT and new RAT) through this feasibility study.

## Slide 4: Prologue (2/2)
SID Proposal: The SID proposal has the details. S1-161222 (subject to change/revisions)
Objective: This paper intends to provide the overview on what's done and what's pending and to propose an SID to enhance Rel-14 V2X including the consideration of 5G aspect (e.g., New RAT).

## Slide 5: Review of Rel-14 V2X (1/2)
Summary of V2X Study/Work (FS_V2XLTE/V2XLTE)
  TR 22.885 v14.0.0 [SP-150765] was approved at SA#70:
    27 Use Cases regarding both safety and non-safety aspects in three categories of V2X (V2V, V2I/N, and V2P), and 142 PRs
    Thirty-three (33) CPRs [S1-154610]
  TS 22.185 v14.0.0: approved @ SA#71 (03/2016)
    Possible CRs of Cat. F
    Available at: http://www.3gpp.org/DynaReport/22185.htm
SA1
SA1#69
2015/02
SID agreed;
9 UCs
SA1#70
2015/04
18 UCs
SA1#71
2015/08
24 UCs
WID agreed
SA1#72
2015/11
27 Ucs
SID completed
Rel-14 V2X Study
SA1#73
2016/02
Target completion
of WID
Rel-14 Normative Work

## Slide 6: Review of Rel-14 V2X (2/2)
Downstream WGs
SA1
SA#67 2015/03
SID approved;
SA#68 2015/06
SA#69 2015/09
WID approved
SA#70 2015/12
TR approved
SA#71 2016/03 (SA1)
Target completion of TS
SA2
SA3
SA#72 2016/06 (SA2)
Target completion of TR
SA#73 2016/09 (SA3)
Target completion of TR
Source: For SA2/SA3, SP-150715 V2X Study; For RAN, RP-151941;
SA2#111 2015/10
SA2 SID agreed
SA3#81 2015/11
SA3 SID agreed
RAN1
RAN#68 2015/06
SID approved
RAN#72 2016/06 (RAN1)
Target completion of TR

## Slide 7: What We Have in R14 V2X
Brief Review on Rel-14 V2X
  Both for safety and non-safety aspects: 27 Use cases
  Types of V2X:
    V2V: covering LTE-based communication between vehicles
    V2P: covering LTE-based communication between a vehicle and a device carried by an individual
    V2I/V2N: covering LTE-based communication between a vehicle and a roadside unit

## Slide 8: What We Don’t in R14 V2X
Brief Review on What’s not included in Rel-14
  Drivers (but also passengers) need additional real-time information
  The types of information include, but not limited to:
    Value-added information (e.g., dynamic map)
    Mobile entertainment: in SA1#71b ad hoc, this part was discussed to be handled in eMBB BB of FS_SMARTER and the priority handling b/w eMBB traffic and V2X traffic (e.g., safety or mechatronics control-related info) to be handled in V2X Rel-15.
    Some detailed study on vehicular use case (e.g. eCall with further enhancement)
  Use Cases:
    Connected Vehicles (semi-/fully autonomous driving)
    Car as mobile office/home
    Service for commercial road users
  Considerations on requirements w.r.t. operations over New RAT

## Slide 9: What We Work on in SMARTER (1/2)
Considerations:
  At Study phase, a minimum level of overlap b/w eV2X Study and what was studied in FS_SMARTER is considered ok if eV2X Study outcome will be incorporated into SMARTER Normative Work, which can be handled in generating normative requirements.
SMARTER items related to V2X
  5.33 Connected vehicles
UCs need further considerations for V2X Rel-15
  UCs not specifically included but need further study in particular aspects of priority handling b/w eMBB and V2X under various types of conditions, e.g., high speed condition, heavy user traffic condition (HD video, etc.):

## Slide 10: What We Work on in SMARTER (2/2)
This slide contains:
  What we stopped at w.r.t. V2X in SMARTER due to the working assumption of making orderly alignment with ongoing R14 V2X (see working assumption @ Vancouver meeting)
Discussion or Postponed Tdocs from SA1#71b ad hoc (5G)
  S1-153074: Automated Cooperative Driving, Qualcomm
  S1-153076: Sensor and State Map Sharing, Qualcomm
  S1-153081: See-through for assisted overtaking, Huawei

## Slide 11: Proposed Considerations (1/4)
Background:
  At SMARTER ad-hoc, it was decided that, V2X-related requirements and use cases would be discussed after Rel-14 V2X is complete. Now that Rel-14 V2X is scheduled to be completed (SP-150573), it is time to begin our analysis on:
    (a) what’s been done in R14,
    (b) what’s been done in FS_SMARTER,
    (c) what’s been postponed by the Vancouver working assumption
    (d) what’s been studied in SDO or in automotive and other industry (e.g., sensor technology sector)

## Slide 12: Proposed Considerations (2/4)
To-Dos:
  (a) Use Cases & PRs in FS_SMARTER
  (b) contributions submitted but put on hold (in Vancouver)
  (c) ideas (yet-to-be called a contribution) not submitted due to this working assumption;
  all of these need to be put on table for study in Rel-15. Based on that, the gap between Rel-14 V2X requirements and requirements for V2X in next generation 3GPP system will be investigated and filled in Rel-15 time frame.
Enhanced support for Multi-RATs:
  Not only for safety but also for non-safety aspects of daily life with vehicles in the near future, a vehicle needs to communicate with other vehicles regardless of used RAT (e.g., New RAT and further enhanced LTE). Accordingly, how to support communication between vehicle/RSU/application servers of different 3GPP generation needs to be studied.
To fully support vertical industry, enhancement in V2X support is needed for new trend such as autonomous driving, car platooning, connected vehicle, etc.

## Slide 13: Proposed Considerations (3/4)
What To Do Next [Proposed]:
  What SA1 to do next is to specify service requirements to enhance 3GPP support for V2X service in the following areas:
    Support for advanced non-safety V2X services (also, referred to as “comfort service”) (e.g. connected vehicle, mobile high-speed entertainment, mobile hot-spot, mobile office/home, dynamic digital map update)
    Supported for advanced safety-related V2X services (e.g. autonomous driving, car platooning, priority handling between safety-related V2X services and other services)
    Support for V2X services in multiple 3GPP RATs (e.g. LTE, New RAT (NR)) and networks environment, including aspects such as interoperability, interworking and mobility
  Note: 5G will cover licensed and unlicensed spectrum usage [3GPP RAN WS, Phoenix, AZ, Sept. 2015]. The interoperability use cases and/or requirements to be investigated in Rel-15 includes, of course, those spectra of 3GPP’s interests but also includes some spectra which automotive industry have interested in. SA1 is expecting to receive feedback from automotive industry in response to SA’s LS sent in SA#70.

## Slide 14: Proposed Considerations (4/4)
Time:
  Target completion by (NLT) SA#73 (09/2016, SA1#75)
SA1
SA1#74
2016/05
SID agree &
Start
SA1#75
2016/08
SA1#76
2016/11
SA1#77
2017/02
Rel-15 V2X
SA1#78
2017/05
SA#76*
*: Rel-15 Stage-1 Target Completion = SA#76 (06/2017)
Based on tentative Future Release milestone (SP-160136, Alain Sultan, ETSI MCC)
To be worked under SMARTER Work Item
TBC: Normative work for eV2X will be handled under SMARTER Work
SMARTER Work Item

## Slide 15: Others
Other Issues:
  SID Proposal in S1-161222 (Tdoc # subject to change upon revisions)
Thank you!