3GPP TSG-SA3 LI Meeting #14 	Tdoc (S3LI04_117r2

Povoa de Varzim , 19-20 July 2004

| CR-Form-v7 |
| --- |
| CHANGE REQUEST |
| ( | 33.107 | CR | CRNum | ( rev | - | ( Current version: | 6.2.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | ICE (Intercepting Control Elements), INE (Intercepting Network Elements) definition |
| --- | --- |
| Source: ( | Siemens AG |
| Work item code: ( | SEC1-LI |  | Date: ( | 07/07/2004 |
| Category: ( | F |  | Release: ( | Rel-6 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) |
| Reason for change: ( | Update was not done with the HLR CR’s |
| Summary of change: ( | Extension of ICE and INE definition with HLR |
| Consequences if ( not approved: | Missing information / not in line with the document |
| Clauses affected: ( | 3.2 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

**** Changes ****

## 3.2	Abbreviations

For the purposes of the present document, the following abbreviations apply:

3GPP MS	3rd Generation Mobile Communication System

3G GGSN	3rd Generation Gateway GPRS Support Node

3G GSN		3rd Generation GPRS Support Node (GGSN/SGSN)

3G MSC		3rd Generation Mobile Switching Center

3G SGSN	3rd Generation Serving GPRS Support Node

3G UMSC	3rd Generation Unified Mobile Switching Centre

ADMF	Administration Function

CC	Content of Communication

DF	Delivery Function

ECT	Explicit Call Transfer

GPRS	General Packet Radio Service

HI	Handover Interface

IA	Interception Area

ICEs	Intercepting Control Elements (3G MSC Server, 3G GMSC Server, P-CSCF, S-CSCF, SGSN, GGSN, HLR)

IMS	IP Multimedia Core Network Subsystem

INEs	Intercepting Network Elements (3G MSC Server, 3G GMSC Server, P-CSCF, S-CSCF, SGSN, GGSN, MGW, HLR)

IP	Internet Protocol

IRI	Intercept Related Information

LDI	Location Dependent Interception

LEA	Law Enforcement Agency

LEMF	Law Enforcement Monitoring Facility

RA	Routing Area

RAI	Routing Area Identitiy

SAI	Service Area Identity

TEL URL		"tel" URL, as defined in [9]

# Comments

Page: 1
 Document numbers are allocated by the Working Group Secretary.

Page: 1
 Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Page: 1
 Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Page: 1
 Enter the revision number of the CR here. If it is the first version, use a "-".

Page: 1
 Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

Page: 1
 For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Page: 1
 Mark one or more of the boxes with an X.

Page: 1
 SIM / USIM / ISIM applications.

Page: 1
 Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

Page: 1
 Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Page: 1
 Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .
The list is also included in a MS Excel file included in the zip file containing the CR cover sheet template.

Page: 1
 Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Page: 1
 Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Page: 1
 Enter a single release code from the list below.

Page: 1
 Enter text which explains why the change is necessary.

Page: 1
 Enter text which describes the most important components of the change. i.e. How the change is made.

Page: 1
 Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Page: 1
 Enter the number of each clause which contains changes.

Page: 1
 Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

Page: 1
 List here the specifications which are affected or the CRs which are linked.

Page: 1
 Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.