3GPP TSG-SA3 LI Meeting #14 	Tdoc (S3LI04_129r2

Povoa de Varzim , 19-20 July 2004

| CR-Form-v7 |
| --- |
| CHANGE REQUEST |
| ( | 33.108 | CR | CRNum | ( rev | - | ( Current version: | 6.6.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Differences between subaddress sections in 33.108 and ETSI TS 101 671 |
| --- | --- |
| Source: ( | Nokia |
| Work item code: ( | SEC-LI |  | Date: ( | 20.07.2004 |
| Category: ( | C |  | Release: ( | Rel-6 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) |
| Reason for change: ( | This CR illustrates differences between subaddress coding clauses in 33.108 and ETSI TS 101 671. “S3LI04_115 correction of the subaddressing” definitions covers part of these differences. However, in some countries more flexible, variable length parameters are required. Besides, in subclauses J.2.2 and J.3.3 reference [30] points to wrong specification. The right reference number should be [31]. |
| Summary of change: ( | Variable length parameters are introduced and reference numbers were corrected. |
| Consequences if ( not approved: |  |
| Clauses affected: ( | J.2.2 and J.3.3 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

## J.2.2	Subaddress options

The coding of a subaddress information element is given in [31]. The following options shall be chosen:

Table J.2.1: Subaddress options

| Option | Value |
| --- | --- |
| Type of subaddress | user specified |
| Odd/even indicator | employed for called party subaddress when no national parameters are used |

## J.2.3	Subaddress coding

The coding of subaddress information shall be in accordance with [31].

### J.2.3.1	BCD Values

The values 0-9 shall be BCD coded according to their natural binary values. The hexadecimal value F shall be used as a field separator. This coding is indicated in table J.2.2.

Table J.2.2: Coding BCD values

| Item | BCD representation |
| --- | --- |
|  | Bit 4 | Bit 3 | Bit 2 | Bit 1 |
| 0 | 0 | 0 | 0 | 0 |
| 1 | 0 | 0 | 0 | 1 |
| 2 | 0 | 0 | 1 | 0 |
| 3 | 0 | 0 | 1 | 1 |
| 4 | 0 | 1 | 0 | 0 |
| 5 | 0 | 1 | 0 | 1 |
| 6 | 0 | 1 | 1 | 0 |
| 7 | 0 | 1 | 1 | 1 |
| 8 | 1 | 0 | 0 | 0 |
| 9 | 1 | 0 | 0 | 1 |
| Field separator | 1 | 1 | 1 | 1 |

When items are packed two to an octet, the least significant item shall be coded by mapping bit 4 to bit 8, bit 3 to bit 7, etc.

### J.2.3.2	Field order and layout

Fields shall be presented into the subaddress in the following order:

Table J.2.3: Fields in the Called Party Subaddress

| Order | Field |
| --- | --- |
| 1 | Operator-ID |
| 2 | CIN |
| 3 | CCLID |
| 4 | National Parameters |

Table J.2.4: Fields in the Calling Party Subaddress

| Order | Field |
| --- | --- |
| 1 | Lawful Interception Identifier (LIID) |
| 2 | Direction |
| 3 | Service Octets |

Apart from National Parameters, inclusion and format of which is determined by national regulations, each field noted above shall be included, whether empty or not. Each of the Operator-ID, CIN, CCLID, LIID and Direction fields shall end by a field separator.

When sending entity does not have a valid value for either of Operator-ID, CIN, CCLID, LIID or Direction fields, then the field is considered empty and it shall be represented only by its field separator.

Table J.2.4A: Example of how field separator should be used when field is empty

| Bits | Octets |
| --- | --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| Called party subaddress identifier | 1 |
| Length of called party subaddress contents | 2 |
| Type of subaddress = user specified, odd/even indicator | 3 |
| Operator-ID ( | Operator-ID ( | 4 |
| Operator-ID ( | Operator-ID ( | 5 |
| Field separator | Operator-ID ( | 6 |
| CCLID ( | Field separator | 7 |
| CCLID ( | CCLID ( | 8 |
| CCLID ( | CCLID ( | 9 |
| CCLID ( | CCLID ( | 10 |
| Field separator | CCLID ( | 11 |
|  |  | 12 |
|  |  | 13 |
|  |  | 14 |
|  |  | 15 |
| (see note) | 16 |
|  | 17 |
|  | 18 |
|  | 19 |
|  | 20 |
|  | 21 |
|  | 22 |
|  | 23 |
| NOTE: The Octets after the final field (CCLID) of the Called Party Subaddress are reserved for national use, e.g. for authentication purposes. |

The parameters within the Information Elements "Called Party Subaddress" and "Calling Party Subaddress" are variable. Because of this variable length the parameters may start in different octets in the related Information Element. I.e. in the Calling Party Subaddress the Direction can be found in octet 17 when the LIID is 25 digits long (table E.3.5).

When the LIID is composed of less than 25 digits, the field separator and direction indicator "moves up" and the rest of the octets is spare till octet 19 as shown in table E.3.7. Between the last digit of the LIID and the Direction is always a Field separator (value F). Also after the "Direction" one Field Separator is given. The last Field separator separates the relevant data from the spare part. So the location of the TMR and the other service Octets below are fixed within the Subaddress. The total length of the Calling Party Subaddress is fixed to 23 octets (including the two Mobile service octets) or 21 octets (without the two Mobile service octets).

The Service Octets as available shall always be mapped into octets 19 to 23 of the Calling Party Subaddress, as appropriate. If one of the parameters TMR, BC or HLC is not available, the octet shall be filled with "FF" hex. If Mobile Teleservice Code is not available, octet 23 shall not be transmitted. If Mobile Teleservice Code and Mobile Bearer Service Code are not available, octets 22 and 23 shall not be transmitted.

As an option the Calling Party Subaddress and Called Party Subaddress may have a variable length. The length is given in octet 2.

When the LIID is composed of less than 25 digits in the Calling Party Subaddress, the Field separator, Direction indicator, Field separator and all the Service Octets "moves up" as shown in table E.3.8.

National Parameters in a variable length Called Party Subaddress may have variable length.

Table J.2.5 represent called party subaddress and table J.2.6 calling party subaddress with the maximum length of the identifiers.

Table J.2.5: Called Party Subaddress

| Bits | Octets |
| --- | --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| Called party subaddress identifier | 1 |
| Length of called party subaddress contents | 2 |
| Type of subaddress = user specified, odd/even indicator | 3 |
| Operator-ID ( | Operator-ID ( | 4 |
| Operator-ID ( | Operator-ID ( | 5 |
| Field separator | Operator-ID ( | 6 |
| CIN ( | CIN ( | 7 |
| CIN ( | CIN ( | 8 |
| CIN ( | CIN ( | 9 |
| CIN ( | CIN ( | 10 |
| CCLID ( | Field separator | 11 |
| CCLID ( | CCLID ( | 12 |
| CCLID ( | CCLID ( | 13 |
| CCLID ( | CCLID ( | 14 |
| Field separator | CCLID ( | 15 |
| see note | 16 |
|  | 17 |
|  | 18 |
|  | 19 |
|  | 20 |
|  | 21 |
|  | 22 |
|  | 23 |
| NOTE: The Octets after the final field (CCLID) of the Called Party Subaddress are reserved for national use, e.g. for authentication purposes. |

Table J.2.6: Calling Party Subaddress

| Bits | Octets |
| --- | --- |
| 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 |  |
| Calling party subaddress identifier | 1 |
| Length of calling party subaddress contents | 2 |
| Type of subaddress = user specified, odd/even indicator according to the amount of BCD-digits | 3 |
| LIID ( | LIID ( | 4 |
| LIID ( | LIID ( | 5 |
| LIID ( | LIID ( | 6 |
| LIID ( | LIID ( | 7 |
| LIID (( | LIID ( | 8 |
| LIID (( | LIID (( | 9 |
| LIID (( | LIID (( | 10 |
| LIID (( | LIID (( | 11 |
| LIID (( | LIID (( | 12 |
| LIID (( | LIID (( | 13 |
| LIID (( | LIID (( | 14 |
| LIID (( | LIID (( | 15 |
| Field separator | LIID (( | 16 |
| Field separator | Direction | 17 |
| spare | spare | 18 |
| ITU-T Recommendation Q.763 [32] TMR (see note 1) | 19 |
| ITU-T Recommendation Q.931 BC [33] octet 3 (see note 2) | 20 |
| ITU-T Recommendation Q.931 HLC [33] octet 4 (see note 3) | 21 |
| Mobile Bearer Service Code (see note 4) | 22 |
| Mobile Teleservice Code (see note 5) | 23 |
| NOTE 1: If available, the Transmission Medium Requirement according to EN 300 356 [29]. If not available, the value is "FF" hex. NOTE 2: If available, only octet 3 of the Bearer Capability I.E. according to EN 300 403 [31] If not available, the value is "FF" hex. NOTE 3: If available, only octet 4 of the High Layer Compatibility I.E. according to EN 300 403 [31]. If not available, the value is "FF" hex. NOTE 4: If available, the Mobile Bearer Service Code according to ETS 300 974 [34], clause 14.7.10. If not available, the octets 22 and 23 shall not be transmitted. NOTE 5: If available, the Mobile Teleservice Code according to ETS 300 974 [34], clause 14.7.9. If not available, the octet 23 shall not be transmitted. |

# Comments

Document numbers are allocated by the Working Group Secretary.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least three digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/ .
The list is also included in a MS Excel file included in the zip file containing the CR cover sheet template.

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2002.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. correction).

Enter the number of each clause which contains changes.

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.