## Slide 1: Encrypted DASH-files over MBMS
S4-121441
SA4#71 meeting
Anne-Marie Praden, Gemalto
06/11/12

## Slide 2: Rationale
3GPP has defined the delivery of DASH files over MBMS (TS 26.346 section 5.6)
This delivery of DASH segments includes the real time delivery (live delivery)
Protection of DASH files is not defined in the current specifications
3GPP has defined a key management system for MBMS (3GPP SA3) adapted for delivery of live services in multicast and broadcast mode and also defined for the download of files.
This key management system is a mandatory feature for MBMS UE terminal.
The proposal is then to use this key management system, which is a 3GPP technology, for the protection of DASH files over MBMS.

## Slide 3: Proposal
The proposal consists then to
  Define the signaling in the MPD of the use of MBMS key management system to protect the DASH files using the content protection element defined for AHS and DASH MPD (TS 26.234 and TS 26.247 section content protection)
  Define in the protected AHS or DASH files the signaling of the location where the Service key may be requested (KeyIssuerURL)
  Define in the protected AHS or DASH files the signaling of the KeyID used for the encryption of the entire representation or individual segment.
  Define how the MTK messages may be included in the encrypted DASH file
    in the initialization segment, if all the segment of a representation are encrypted with the same key
    In each individual segment, if each segment are encrypted with its own key (allowing a key rotation)
This encryption is optionally used by the server and remains a choice of the service provider
This signaling defined for encrypted DASH files is a mandatory feature for the MBMS terminal supporting DASH or AHS.

## Slide 4: What already exists
3GP-DASH and 3GP-AHS has defined a content protection element to signal the fact that the DASH files are encrypted and signaling the Key management system used through the scheme-type and scheme version.
OMA DRM in the OMA DRM XBS specification has defined a Key Info box (‘obki’) to include the keyissuerURL , the KeyID and optionally the MTK message (STKM) in a DCF or PDCF or Adapted PDCF file.
OMA DRM XBS has defined a way to include a STKM stream in-line with the media content in a PDCF file for live delivery or recording of PDCF files: Adapted PDCF file. The STKM stream is defined as a timed metadata track in the PDCF file (‘oksd’).
3GPP SA3 uses the ‘obki’ box in DCF file for the download of files protected with MBMS key. (TS 33.246). A KeyID Type (“ 0x02” ) has been registered by OMNA for 3GPP MBMS KeyID type.
3GPP SA4 uses the Adapted PDCF file (‘oksd’ box) for the protected stream recording (TS 26.244 section 12). A sample_type (“0xf7”) has been registered by OMNA for 3GPP MIKEY MBMS traffic key message .
MPEG has defined the Common Encryption (CENC) for the encryption of ISOBMFF files to enable decryption of the same file using different Key management systems. The definition of the location of the decryption keys and where to get the associated licenses is leaved to each key management system.

## Slide 5: What is proposed in the associated CRs
As adapted PDCF is already used in 3GPP specs, the proposal is to used this kind of file specifically designed for live delivery and including the STKM stream (MTK message) for the DASH files.
This consists of including a ‘obki’ box in the Media segment containing the KeyIssuerURL and the KeyID.
Including also a STKM track ‘oksd’ for the MTK messages
If all the segments of the representation are encrypted with the same key then the ‘obki’ and ‘oksd’ are included in the initialization segment
If each segment is encrypted with its own key the ‘obki’ and ‘oksd’ are included in the media segment.
This is defined in the CRs
  S4-121269, 1270 ad 1271 for the TS 26.244
  and S4121266, 1267, 1268 for the TS 26.234 and TS 26.247 where the initialization and media segments are described.
The signaling of these encrypted files in the content protection element of the MPD is defined in the CRs, S4121266, 1267, 1268

## Slide 6: What is proposed in the associated CRs
As CENC is used also for encryption of DASH files, the use of such ISOBMFF files is also proposed.
  The signaling of these encrypted files in the content protection element of the MPD is defined in the CRs, S4121266, 1267, 1268
CENC has defined a Protection System Specific Data container, the Protection System Specific Header Box (‘pssh’) where data of the specific key management systems may be stored.
  For MBMS key management system the CRs propose to define a header box: MBMS System Specific Metadata box (‘mssm’) included in the ‘pssh’ box where MBMS specific data are included. In this header box the KeyInfo box ‘obki’ already used by 3GPP is included. This box contains the keyIssuer location, the KeyID and the MTK message and is included either in the initialization box or the media segments. (13.7.1 in S4.121269, 1270 and 1271)

## Slide 7: What is proposed in the associated CRs
CENC has defined a Common ENCryption information container for a media track, including default values for the key identifier (KID), initialization vector size, and encryption flag . This container is the Track Encryption Box (‘tenc’).
  For MBMS key management system the CRs proposes to map the KeyID of this ‘tenc’ box with the KeyID of the MBMS KMS. (13.7.2 in S4.121269, 1270 and 1271)
CENC allows also groups of samples of a track to be encrypted with different keys, or a mix of clear and encrypted contents. In this case the encryption parameters are included in a CencSampleEncryptionInformationVideoGroupEntry (‘seig’) or CencSampleEncryptionInformationAudioGroupEntry (‘seig’) depending on the type of the track (Video or Audio). The ‘seig’ box is included in the SampleGroupDescriptionBox (‘sgpd’). And Initialization vector associated to an encrypted sample in a protected track is included in the sample auxiliary information (CencSampleAuxiliaryDataFormat) referenced by ‘saiz’ and ‘saio’ boxes.
  For MBMS key management system the CRs proposes to map the KeyID of this SampleEncryptionInformation entry with the KeyID of MBMS KMS. (13.7.3 and 13.7.4 in S4.121269, 1270 and 1271)

## Slide 8: What is proposed in the associated CRs
For live content the Common ENCryption may be used and MPEG has issued an amendment to the CENC. In this case a CencKeyRotSampleEncryptionInformationVideoGroupEntry is defined including the encryptedkey (MTK message).
  For MBMS key management system the CRs proposes to map the KeyID and the encryptedKey of this SampleEncryptionInformation entry with the KeyID and MTK message of MBMS KMS (13.7.5 in S4.121269, 1270 and 1271)

## Slide 9: Conclusion
What is proposed in the S4-121263 to S4-121271 is not a definition of a Key management system but the use of the key management system already defined in 3GPP SA3 for its application in case of Encrypted DASH files delivered over MBMS. The MBMS Key management system is not modified at all.
What is proposed in the S4-121263 to S4-121271 re-uses what is already defined in 3GPP SA3 and 3GPP-SA4 for its application in the scope of encryption of DASH/AHS files.
What is defined is the signaling of such files in the DASH/AHS MPD
What is define is the mapping of Key management specific information (KeyIssuerURL, KeyID, encryptedKey) of Adapted PDCF key info box or CENC boxes with the MBMS Key Management system parameters. MBMS KMS, with these CRs will be usable on CENC, and prepared for CENC.
The inclusion of MTK messages in the initialization or media segment is also defined using boxes already used in 3GPP SA4 or SA3.
The proposal is then to review and accept the associated CRs