## Slide 1
Overview of 3GPP SA WG6
SA6 Leadership:
Suresh Chitturi (Samsung Research) 3GPP SA WG6 Chairman
Alan Soloway (Qualcomm Technologies) 3GPP SA WG6 Vice-Chair
Jukka Vialen (Airbus) 3GPP SA WG6 Vice-Chair
Contributors:
Basavaraj Pattan (Samsung) Rapporteur: CAPIF, SEAL
Camilo Solano (Ericsson) ` Rapporteur: MCIOPS
Dave Chater-Lea (Motorola Solutions) Rapporteur: MCSMI, MCLog
Dom Lazara (Motorola Solutions) Rapporteur: MCPTT, MCLoc
Jerry Shih (AT&T) Rapporteur: MCData
Kees Verweij (The Police of the Netherlands) Rapporteur: MCover5GS
Martin Oettl (Nokia) Rapporteur: FRMCS/MONASTERY
Niranth Amogh (Huawei) Rapporteur: CFA, MCVideo, V2XAPP, UASAPP
Nishant Gupta (Samsung) Rapporteur: EDGEAPP
Peter Monnes (Harris) Rapporteur: MCCI
Shao WeiXiang (ZTE) Rapporteur: FFAPP

## Slide 2: Outline
Introduction to SA6
  History and Evolution of SA6
  Rel-16 / Rel-17 Overviews
Mission Critical Topics
Vertical Industry Enablement
Conclusions

## Slide 3: Outline
Introduction to SA6
  History and Evolution of SA6
  Rel-16 / Rel-17 Overviews
Mission Critical Topics
Vertical Industry Enablement
Conclusions

## Slide 4: History and Evolution – SA6
3GPP identified as the home for global Mission Critical Services (MCX) Standards
  Over 600 user requirements with inputs from TETRA, P25 and mobile broadband industry
  New Working Group dedicated for Mission Critical Applications (SA6) – first expansion in 20 years!
First global MCPTT standard published in 2016 (Rel-13)
  MC standardization continues to evolve….
SA6 expands its Terms of Reference in June 2017
  Critical Communications and related verticals (e.g. railways)
  Other applications to support industry verticals
  Northbound and device Application Programming Interfaces (APIs) for the above applications
  Common API framework to support 3GPP northbound API development efforts

## Slide 5: SA6 Work-Items

## Slide 6: SA6 Studies

## Slide 7: Outline
Introduction to SA6
  History and Evolution of SA6
  Rel-16 / Rel-17 Overviews
Mission Critical Topics
Vertical Industry Enablement
Conclusions

## Slide 8: Mission Critical Common Functional Architecture (CFA)
Purpose and Scope
  A common functional architecture to support all MC services (i.e., MCPTT, MCVideo, MCData) including the common application plane and signalling plane entities.
  Purpose is to re-use the common functionalities across different MC services.
Key features
  CFA to support mission critical services can be used for public safety applications and also for general commercial applications e.g. utility companies and railways.
  Common services core functions (e.g. group management, configuration management, identity management, key management, location management)
  Supports on-network (Uu based unicast and multicast) and off-network (PC5) operations

## Slide 9: CFA – Architecture
Key Functional Entities
  Application Plane client and servers
    Group mgmt: Groups information mgmt (CRUDN)
    Configuration mgmt: UE, service info configurations
    Identity mgmt: Supports authentication
    Key mgmt: Supports security aspects (encryption)
    Location mgmt: Mgmt of user location information
    Migration mgmt: Migration of users between systems
    Functional alias mgmt: Support railways functional alias
  Signalling Plane
    SIP entities: Compliant with external reference points of IMS. (User agent, SIP AS, SIP core, Diameter proxy)
    HTTP entities: HTTP messaging support (HTTP client, HTTP proxy, HTTP server)
General MC service entities
MCPTT client
MCVideo client
MCData client
MCPTT server
MCVideo server
MCData server
Common services core
Single instance of common services core for all MC services or per MC service
Single user DB for all MC services
Or per MC service

## Slide 10: Mission Critical Push-To-Talk (MCPTT)
The first Mission Critical service produced by SA6. MCPTT is one of the three pillars of Mission Critical services which provides real-time voice communications with a rich set of features to support Public Safety and other verticals (e.g. Railways).
  Supports both private and group communications
  Supports addressing, security, and priority that allows confidentiality from the network plane
  Supports both unicast and multicast delivery of media and signalling, and off-network modes
Key features
  Affiliation and de-affiliation to groups
  Manual and automatic commencement modes
  Off-network utilizing ProSe and ProSe relay
  Sophisticated group and user regrouping
  Pre-established sessions
  Emergency calls (private and group)
  Imminent peril call, Emergency alert
  Ambient listening
  Floor priority and queuing
  Functional alias management

## Slide 11: MCPTT – Architecture
Key Functional Entities
  MCPTT Client includes Media Mixer and Floor Participant
  MCPTT Server includes Media Distribution Function and Floor Control Server
  MCPTT User database is the repository for user based capabilities
  MCPTT Gateway server is link to communication across MCPTT domains
  Interworking Function (IWF) is the link to LMR interoperability (and future GSM-R)

## Slide 12: Mission Critical Video (MCVideo)
Purpose and Scope
  Mission critical video service using E-UTRAN access based on the common functional architecture for mission critical services and the EPC architecture.
  The MCVideo service can be used for public safety applications and also for general commercial applications e.g. utility companies and railways.
Key features
  Group communications
  Private communications
  Video Pull and Video Push
  Capability Information Sharing
  Ambient Viewing
  Transmission and Reception Control
  Supports high video resolution and enables license plate reading, facial and fingerprint recognition and overview of scenes
  Support for Low latency video modes (Emergency scenarios).
  Support high mobility

## Slide 13: MCVideo – Architecture
Key Functional Entities
  Architecture entities developed utilizing CFA
  MCVideo server: Supports the MCVideo communications/services.
    Media distribution function: Media handling (uplink, downlink, replication, storage, mixing.
    Transmission control server: Controls media transmissions to UEs according to network situation and user intentions.
  MCVideo client: Supports the MCVideo transactions and remote device control.
    Media mixer: sending and receiving one or multiple media streams and mixing.
    Transmission control participant: Handling outgoing and incoming transmissions.

## Slide 14: Mission Critical Data (MCData)
One of the three pillars of the Mission Critical services that provides near real-time data communications
  Support both private and group communications
  Support both on and off network environment
  Support both unicast and multicast delivery
Key features
  Short Data Service, using both signaling and media planes
  File distribution, both for real-time and non real-time
  Data streaming (planned for Rel-17)
  IP connectivity
  Conversation management
  Transmission and reception control
  Lossless communication
  Network base message store
  Regular and emergency services

## Slide 15: MCData – Architecture
Key Functional Entities
  MCData UE
  MCData Server
  MCData message store
  MCData content server
  Interworking function to LMR
  MC gateway server

## Slide 16: Mission Critical System Migration and Interconnection (MCSMI)
Mission critical communication between users and groups in different MC systems that are in different security domains
  National and international co-operation; mutual aid between states and territories etc
Interconnection: calls to users and groups in partner MC systems
Migration: obtaining service from partner MC systems
Architectural elements
  MC gateway server – provides topology hiding between MC systems
  Configuration management: local MC system applies local rules to user and group configuration provided by partner MC system
  Migration management – manages access information to partner MC system
MC
System A
MC
System B
UE
A
UE
Z
Communication
Interconnection
MC
System A
MC
System B
UE B
UE
Z
UE A
UE A
Migration
MCPTT
-
3
Other MCPTT server
MCPTT server
MC gateway
server
MCPTT
-
3
MCPTT-10
Other MC system
MC gateway
server
Inter-system reference points
Configuration management server
Group management server
Migration management server
Configuration management server
Group management server
Migration management server
MC system
CSC-16
CSC-17
CSC-18

## Slide 17: Mission Critical Communication Interworking (MCCI)
Purpose and Scope
  Adapts LMR (Land Mobile Radio, i.e. Public Safety radio) systems to MC systems
  The IWF (InterWorking Function), along with its LMR system, will appear as a peer interconnected MC system
Key features
  Group ‘affiliation’
  Group management / Regrouping
  Group calls / Private calls
  Broadcast calls / Emergency and imminent peril calls
  Short messaging
  Location
  Support for LMR end-to-end security

## Slide 18: MC MBMS UE API (MBMSAPI_MCS)
Purpose and Scope
  Enables 3rd party Mission Critical Applications to access MBMS functionality on the UE
Key features
  Application registration/de-registration
  MBMS bearer registration/de-registration
  Get MBMS SAI/update notification
  Get cell info/update notification
  MBMS bearer notification
  Open/close media

## Slide 19: MC Over IOPS (FS_MCSAA)
Purpose and Scope
  This study focused on identifying application architecture solutions needed to support mission critical services during the Isolated E-UTRAN Operation for Public Safety (IOPS) mode of operation
Key features
  Solutions for the IOPS functional model and architectural model
  Solutions to address IOPS MC system synchronization aspects
  Potential application procedures to be utilized on the IOPS mode of operation

## Slide 20: Discreet Listening & Logging (FS_MCLOG)
Discreet listening
  MCPTT and MCVideo private calls
  MCPTT and MCVideo group calls
  MCVideo pull and push
  MCData SDS and file distribution
Logging
  MC logging function
  MC replay equipment
Private communication
Group Communication
Logging and Replay

## Slide 21
Purpose and Scope
  This study focuses on identifying enhancements to the existing location architecture for MC services (MCPTT, MCVideo, MCData). These enhancements include such items as location history reporting and location of current talker.
Some key issues and solutions
  Location of a user logged into more than one device
  Location information in off-network operation
  Sharing of location information
  Triggering criteria in emergency scenarios
  Location accuracy including enhanced capabilities
Location enhancements for MC services (FS_enhMCLoc)

## Slide 22: MC Services over 5G (FS_MCOver5GS)
Purpose and Scope
  To identify the impacts on and the necessary changes in the Stage 2 Mission Critical specifications to ensure that the set of Mission Critical services is supported over the 5GS
Aspects
  Terminology/textual changes
  Technical issues
    Review and identify the 5GS aspects to support the Mission Critical architecture
      Highlight missing 5GS features required for MC services
      Use of new 5GS features
      Impact of 5GS architecture

## Slide 23: Outline
Introduction to SA6
  History and Evolution of SA6
  Rel-16 / Rel-17 Overviews
Mission Critical Topics
Vertical Industry Enablement
Conclusions

## Slide 24: MONASTERY - Mobile Communication System for Railways
Purpose and Scope
  Enhance Mission Critical Communication by rail communication requirements to allow a migration from current GSM-R system towards FRMCS (Future Railways Mobile Communication System). The legacy GSM-R system will be not integral part of the FRMCS. Simply the focus is on interruptible service migration between GSM-R and FRMCS.
Key features
  Functional addressing of the user for operational purposes applicable for voice, video and data service types e.g. train number or current role of the user e.g. train driver;
  IP Connectivity for MC unaware data hosts e.g. train control command signalling (ETCS);
  Dynamic regrouping based on location and user roles;
  Specific railway functions for private and group communications (call forwarding, affiliation based on functional address etc.)
  Interworking with GSM-R;
  Sharing of one UE by multiple users simultaneously (Gateway UE).

## Slide 25: MONASTERY – High Level Services
Key railway communication services
  Operational role management
  Multi-Talker control in group communication
  Location dependent communication
  IP connectivity for safety and non-safety rail applications
  Maintenance services (location based grouping)
  Railway specific services like railway emergency calls/alerts, location-dependent communication
  Interworking with legacy GSM-R

## Slide 26: MONASTERY – High Level Services (2) for further study
Key railway communication services
  Interworking between MCX system using functional addressing
  Off-network communication for virtual coupling and train integrity
  Gateway UE

## Slide 27: Common API Framework (CAPIF)
Purpose and Scope
  During Release 15, the Common API Framework (CAPIF) was developed to enable a unified Northbound API framework across 3GPP network functions, and to ensure that there is a single and harmonized approach for API development (Refer to 3GPP TS 23.222, TS 33.122 and TS 29.222).
  CAPIF provides a framework to host network and service APIs of PLMN and from 3rd party domain.
  This work has been successfully delivered and integrated with Northbound APIs developed by 3GPP SA2 Working Group (SCEF/NEF) and 3GPP SA4 (xMB).
Key features
  On-boarding/off-boarding API invoker
  Register/de-register APIs
  Discovery of APIs
  Support for 3rd party domains i.e. to allow 3rd party API providers to leverage the CAPIF framework
  Support for interconnection between two CAPIF providers
  The federation of CAPIF functions to support distributed deployments.
  CAPIF events Subscription/Notification
  Entity Authentication/Authorization
  Enables secure communication

## Slide 28: CAPIF – Architecture
Key Functional Entities
  CAPIF Core Function (CCF) is a repository of all, PLMN and 3rd party, service APIs - allows discovery of the stored APIs by the API invokers and AEFs - authenticates and authorizes API invokers for use of the service APIs - logging and charging the API invocations
  API Exposing Function (AEF) is the provider of the services as APIs - validates the authorization of the API Invokers - provides the service to the API invoker - logs the invocations on the CCF and requests charging for the service.
  API Invoker is typically the applications that require service from the service providers - discovers the service APIs from the CAPIF Core Function - seeks authorization for API invocations - avails the services provided by the AEFs
Functional model for the CAPIF to support 3rd party API providers

## Slide 29: Service Enabler Architecture Layer for Verticals (SEAL)
Purpose and Scope
  3GPP networks witnessing increasing demand from various vertical industries
  It is apparent that vertical applications will require similar core capabilities in a timely manner
  3GPP Release 16 TS 23.434 specifies application-enabling services that can be reused across vertical applications (e.g. V2X applications)
  SEAL also specifies the northbound APIs (complaint with CAPIF) - to enable flexible integration with vertical applications.
Key features
  SEAL services include
    Group management
    Configuration management
    Location management
  SEAL services are supported both in on-network and off-network
  Interconnection between SEAL servers to support distributed SEAL server deployments
  Inter-service communication between SEAL servers (e.g. location based group management)
    Identity management
    Key management
    Network resource management

## Slide 30: SEAL – Architecture
Key Functional Entities
  SEAL client (client side functionalities corresponding to the specific SEAL service)
    supports interactions with the VAL client(s) and with the corresponding SEAL client between the two UEs
  SEAL server (server side functionalities corresponding to the specific SEAL service)
    supports interactions with the VAL server(s) and with the corresponding SEAL server in distributed SEAL deployments
    acts as CAPIF's API exposing function (AEF)
Generic on-network functional model

## Slide 31: Leveraging CAPIF and SEAL
Enables rapid deployment of new vertical applications, with access to the common SEAL services provided by MNOs:
  SEAL services (e.g. location, group, etc.) are exposed as Northbound APIs
  CAPIF is used for publishing and discovery of SEAL services by the Vertical applications
Benefits
  Vertical Service Provider – reduced time to market
  Network Operator – maximize reuse of their existing deployments

## Slide 32: V2X Application (V2XAPP)
Purpose and Scope
  V2X application enabler layer that is necessary to ensure efficient use and deployment of V2X services over 3GPP systems.
  Currently supports EPS. Study ongoing to support 5GS.
Key features
  V2X service discovery
  Application level location tracking
  V2X message delivery
  File distribution
  Provisioning 3GPP system info
  Network monitoring
  V2X application resource management
  Dynamic group management (platooning support)
  V2X service continuity

## Slide 33: V2XAPP – Architecture
V2X application architecture developed based on SEAL.
Key Functional Entities
  VAE client and server: Abstracts the common V2X support functions and user plane interactions with 3GPP network systems. Provides APIs to the V2X application specific functions
SEAL services
VAE
Uu
PC5
NB APIs
Client APIs

## Slide 34: Edge Application (EDGEAPP)
Purpose and Scope
  Edge Computing in 3GPP will help achieve the performance goals of Verticals, providing low latency and massive broadband.
  The study aims to define a supporting application layer, which enables the deployment of applications on the edge of 3GPP networks, with minimal impacts to edge-based applications on the UE.
Key features
  UE application portability Changes in Application Clients compared to existing cloud environment are avoided.
  Edge application portability Changes in Application Servers compared to existing cloud environment are avoided.
  Service differentiation The mobile operator is able to provide service differentiation (e.g. by enabling/disabling the Edge Computing functionalities).
  Flexible deployment There can be multiple Edge Computing providers within a single PLMN operator network. The Edge Data Network can be a subarea of a PLMN.
  Interworking with 3GPP network Capability exposure, such as location service, QoS, AF traffic influence, to the Edge Applications.
  Service continuity Support for continuation of application context across Edge deployments

## Slide 35: EDGEAPP – Architecture
Key Functional Entities
  Edge Enabler Server: Provides information related to the Edge Applications, such as availability and related configuration, to the Edge Enabler Client; and exposes capabilities of 3GPP network to Edge Applications.
  Edge Enabler Client: Enables discovery of Edge Applications and provisioning of configuration data
  Edge Data Network Configuration Server: Providing Edge Data Network configuration information to the Edge Enabler Client
The study report is being documented in 3GPP TR 23.758, and is expected to be complete by December’2019.
Application architecture for enabling edge applications

## Slide 36: Factories of the Future Application (FFAPP)
FFAPP identifies architecture requirements and application architecture to ensure efficient use and deployment of application layer support for Factories of the Future in 5G network.
  takes into consideration the existing work including stage 1 requirements in 3GPP TS 22.261 and 3GPP TS 22.104, and provides recommendation for normative work
Key features
  support for network slicing, cross network slice coordination
  Geographic location and positioning information support
  clock synchronization, TSN supporting
  QoS monitoring, Managing non-public network
  5GLAN group management

## Slide 37: FFAPP – Architecture
Key Functional Entities
  Not yet design
Other Areas of Interest
  alliance with 5G-ACIA White Paper – 5G Network Exposure Interface for Enterprises

## Slide 38: Unmanned Aerial System Application (UASAPP)
Purpose and Scope
  Identify the application aspects to support UAS that are necessary to ensure efficient use and deployment of UAS services and applications over 3GPP systems.
Key features
  Authentication and authorization
  UTM command communication
  Location tracking
  ….
Study is in progress

## Slide 39: Outline
Introduction to SA6
  History and Evolution of SA6
  Rel-16 / Rel-17 Overviews
Mission Critical Topics
Vertical Industry Enablement
Conclusions

## Slide 40: Conclusions
3GPP has established a mature set of MCX standards
  Enhancements will continue!
Expanded SA6 scope has enabled standardized support for vertical industries
Industry feedback is critical to robust standards
  ETSI Mission Critical Plugtests™
  Additional input through requirements and liaisons
Participation is essential: Please join us
  Contribution-driven approach – Your voice will be heard!

## Slide 41: Thank you for your attention!
www.3gpp.org
info@3gpp.org
s.chitturi@samsung.com
Search for WIDs at http://www.3gpp.org/specifications/work-plan and http://www.3gpp.org/ftp/Information/WORK_PLAN/