## Slide 1: Proposals for 5G Technologies
Mitsubishi Electric Corporation
3GPP RAN Workshop on 5G
Phoenix, AZ, USA, Sept. 17-18, 2015
RWS-150014

## Slide 2
Outline
Use cases for future wireless communication
5G Requirements and possible solutions
5G Candidate Technologies
  Massive MIMO
  Adaptive OFDM-based waveforms
  Enhanced DFT-s-OFDM-based waveform
Conclusions

## Slide 3
Increase in demands for richer contents such as 4K/8K videos is expected
  Need for higher throughput
Various use cases such as IoT and M2M are expected
  Need for ubiquitous availability
Heavier and more impulsive traffic for specific occasions (during a concert in a crowded stadium, etc.)
  Need for larger capacity
Use cases for future wireless communication
Emergency communication
Large-scale
events
Aeronautical communication
M2M communication
New train guidance
4K/8K
digital signage
Multi-angle
real-time communication
B2B
communication
Remote
control
Network
appliances
High-speed railway communication
Automatic
operation
Car telematics

## Slide 4
5G Requirements and possible solutions
User
Throughput [bps/person]
User density
[person/km2]
Rural
Urban
Dense
Extreme
Isolated
Small Cell
Micro Cell
Macro Cell
4G Diagram
Higher Throughput
Increase capacity
Coverage expansion
Massive MIMO
Enhanced OFDM-based waveforms with new numerology

## Slide 5
[Objective]
Achieve higher throughput e.g., 20 Gbps [1]
[Proposal]
Enhance the current MIMO design and increase the number of multiplexed layers higher than 8
[Possible topics for discussion to realize Massive MIMO for 5G]
CSI reporting with higher resolution
Investigation on impact of realistic assumptions on channel reciprocity ( i.e., mismatches in RF circuit characteristics between TX and RX)
User interference cancellation at transmitter: precoding/postcoding design
RS design to reduce pilot contamination
Discovery of a terminal, discovery of eNB/beam
Massive MIMO
[1] Recommendation ITU-R M.[IMT.VISION]

## Slide 6
An example of feasibility study for Massive MIMO
Achieved throughput over 20Gbps by using 16-stream multiplexing [2]
[2] To appear in SmartCom2015, Tokyo, Japan
-48‐element adaptive phase antenna array is used
-Transmission efficiency: ratio of data symbols to the total number of symbols including control information
*
* Obtained from simulation using acquired channel characteristics at 44GHz

## Slide 7
  Adaptive OFDM-based waveforms
[Objective]
Cell coverage needs to be expanded for higher frequency
Foreseeing usage of higher frequency bands in the near future, a scheme that embraces coexistence of backward and forward compatible waveforms is needed
[Proposal]
Switch OFDM-based waveforms adaptively in high SHF: OFDMA for UEs close to a base station, SC-FDMA for isolated and distant UEs
Use of SC-FDMA-based waveform: leads to cell coverage expansion due to low PAPR
For SC-FDMA, allow single user per beam to take advantage of a narrower beam to achieve higher antenna gain
[Possible topics for discussion]
Information gathering mechanism for waveform selection
Signalling scheme to inform selected waveform to UE
Definition of eNB/UE capability
 | Low SHF | High SHF | EHF
Uplink | OFDMA-based | OFDMA/SC-FDMA-based | SC-FDMA-based
Downlink | OFDMA-based | OFDMA/SC-FDMA-based | SC-FDMA-based

## Slide 8
Time →
T-1
T-2
T
T+1
T+2
T+3
UEs near the base station: OFDMA
Legacy/Enhanced UE
(OFDMA DL)

## Slide 9
T-1
T-2
T
T+1
T+2
T+3
Time →

## Slide 10
Time →
Distant UEs: SC-FDMA
T-1
T-2
T
T+1
T+2
T+3
Enhanced UE
(SC-FDMA DL)

## Slide 11
More compact spectrum with enhanced DFT-s-OFDM
QPSK
Output backoff: 5dB
  Enhanced DFT-s-OFDM-based waveform
[Objective]
Limit the number of RS required for massive MIMO systems and create more opportunities for channel and interference estimation
[Proposal]
Insertion of a static or zero sequence in SC-FDMA prior to DFT [3,4]
- Effective use of CPs for synchronization, channel and interference estimation
- Localized signal in frequency due to suppressed out of band emission
Time
Proposed waveform in time domain..
Known static sequence is used for synchronization and channel estimation
Frame format for DFT-s-OFDM with the static sequence
Time
Frequency
CP(Known static sequence)
Existing RS
Data
[3] F. Hasegawa, et al., “Static sequence assisted out-of-band power suppression for DFT-s-OFDM”, PIMRC 2015.
[4] G. Berardinelli, et al., “Zero-tail DFT-spread-OFDM signals”, 2013 IEEE Globecom Workshops.

## Slide 12
Conclusions
Possible topics for technological enhancements for massive MIMO to achieve higher throughput are proposed
An adaptive OFDM-based waveform scheme is proposed to expand cell coverages
Enhanced DFT-s-OFDM based waveform is proposed to satisfy demands for more RS in massive MIMO systems