## Slide 1
Issues for a High Performance Unlicensed Spectrum Access Protocol for 5G
September, 2015
Notes: Patrick Welsh – DC Office – Regulatory affairs
Bill stone – head of network planning – driving development of LTE-U (Sergio)
Sergio Geri – tech lead for LTE-U product development
- Steps that Sergio has taken to be a good neighbor (2014 – LTE-U Forum)
Basis is existing standards, focus is on supplement downlink (lte-uforum.org)
One of the specifications is wifi
Three levels of coexistance
  Implemented by the schedululr
    Dynamic channel selection (wifi sniffer) that continually monitors (uses UNII Band 1 and UNII Band 3), WiFi will continue to have UNI Band 2
      Selects best channel based on energy detection
    Can operate in a cochannel mode – implement an adaptive wave form in a time domain
      Fed to an algorithm that determines duty cycle based on loading [proprietary algorithm]?
- WiFi was the benchmark in March announcement release

## Slide 2: Unlicensed spectrum and 5G
Densification with massive indoor base station deployment is the biggest lever to massively grow capacity for 5G – ~80% of smartphone traffic originates from indoors.
The usage of unlicensed spectrum for access has grown to support over 50% of all Internet traffic dominated by Wi-Fi technology operating at low power and over short distances.
Unlicensed spectrum access is now seen as a key part of 5G with many envisioning a unified approach for licensed, shared and unlicensed spectrum
LAA may be a precursor for unlicensed spectrum and 5G
Issues regarding a common unlicensed spectrum access protocol are of interest to support high performance and coexistence for Wi-Fi, 5G cellular unlicensed spectrum technology and other technologies.

## Slide 3: Today’s smartphones and licensed/unlicensed spectrum
Both Cellular and Wi-Fi are important access technologies for smartphones
Cellular provides seamless mobile access with widespread coverage
Wi-Fi dominates usage for indoor broadband data access
Wireless Access Point
Cellular
System
Notes: In 3GPP, only realtime impact is VoiP, and this is optional
Current WiFi equipment
Google wants to preserve both lines of argument

## Slide 4: Unlicensed spectrum access protocol issues
Coexistence with legacy devices
Limitations of simple Energy Detect protocols
  Hidden nodes
  Reliable weak signal detection
  No support for “smart LBT” procedures
  Effectiveness degrades as antenna directionality increases
DL Issues
  Massive MIMO conflict with ED LBT
  QOS management
  Beacon signal scheduling
  Multi-carrier operation
UL Issues
  Channel contention
  Scheduled UL conflicting with UL LBT
  Double Hidden node problem with no UL LBT

## Slide 5: The Double Hidden node problem with no UL LBT degrades coexistence and beamforming exacerbates this problem
Impairment link is 2 steps removed from the LBT measurement link
Active desired signal is from the Wi-FI AP TX not the STA RX (the victim) and is attenuated at the measurement RX by TX beamforming
Potential impairment signal is from the LAA device (the aggressor) and not from the LAA eNB which performs LBT but has its measurement attenuated by RX beamforming
LAA Device
Wi-Fi STA
Wi-Fi AP
LAA eNB
-62 dBm coverage
-62 dBm coverage
desired
signal
impairment
signal
LBT
measured
signal << -62 dBm
LAA UL
signal

## Slide 6: Observations
Unlicensed spectrum, especially above 5 GHz, is likely to play a major role in 5G cellular systems.
Strong coexistence with existing and evolving devices, especially other broadband access devices, using unlicensed spectrum is a critical consideration for 5G unlicensed spectrum technology.
Strong coexistence may include waveform compatible signaling for enhanced reliability, information exchange and improved unlicensed access protocols between technologies.
Unlicensed spectrum access for 5G base stations (eNB’s or AP’s) to support downlink procedures should consider coexistence and spectrum access issues related to Massive MIMO, high-order TXBF, MU-MIMO, QOS for different types of traffic including real-time traffic, beacons, hidden nodes, and other factors..
Unlicensed spectrum access for 5G user devices (devices or STA’s) for uplink directions should address coexistence and spectrum access issues related to scheduled access by the eNB or AP conflicting with UL LBT procedures, double-hidden nodes, and other factors.
A common method of aggregating carriers for 5G unlicensed spectrum technologies is desirable for best coexistence and efficiency.