## Slide 1: NR Radio interface Protocols
RWS-180010
Workshop on 3GPP submission towards IMT-2020
24-25.10.2018 in Brussels

## Slide 2: Topics
Control plane functions and procedures
  INACTIVE state and state transition to Connected
User plane protocols
  Functions, differences to LTE with motivation
Non standalone specific functions
  Control plane architecture
  Bearer types
Rel-16 topics

## Slide 3: RRC in NG-RAN

## Slide 4: RRC main functions: Connection control
RRC connection control: establishment, reconfiguration and release of the RRC connection
Initial security activation, i.e. initial configuration of integrity protection and ciphering in RAN (SRBs, DRBs)
INACTIVE state management
  suspension/resumption of RRC connection
Mobility related: Handover, measurement configuration/reporting
Failure recovery

## Slide 5: Connection establishment
Procedurally similar to LTE
  RRC connection request, setup, setup complete
  Nx connection establishment with 5GC with UE context and capability transfer
  Security configuration
  DRB setup
  Idle to connected delay different compared to LTE
    5GC NAS service request message design is different and larger than EPC

## Slide 6: Security
Security establishment procedure will be the same as in LTE
Key differences:
  Integrity protection to be supported for DRB
      Data failing Integrity protection to be discarded
  Both ciphering and integrity protection is configurable per DRB
    Certain PDU sessions may not secuirty
  Every handover may not need a key change
    Change of keys expected only if there is change in Central Unit (CU) (i.e., PDCP location) for split CU/DU RAN

## Slide 7: Mobility
Mobility procedures also similar to LTE
  No procedural changes/optimisations for Handover or inter-RAT mobility compared to LTE in Rel-15
    Main changes are to UE measurements based on NR PHY
  Idle mode: Similar to LTE
    Priority based mechanisms of LTE re-used
      Applicable also for INACTIVE
    Changes required to support NR PHY for cell reselection measurements

## Slide 8: RRM
Overall measurement framework is similar to LTE except beam related aspects.
  Three measurement types: intra-frequency, inter-frequency, inter-RAT measurements for E-UTRA
  The association between a measurement object and a reporting configuration is created by a measurement identity
  Reference signal: SSB for idle mode; SSB and/or CSI-RS for Connected mode
  Beam level measurement and reporting
    The UE measures multiple beams of a cell and derive the cell quality from the multiple beams
    Measurement reports may contain beam results (beam identifier only, measurement result and beam identifier, or no beam reporting) in addition to cell quantities
  Measurement gap
    Non-gap-assisted or gap-assisted depends on the capability of the UE, the active BWP of the UE and the current operating frequency

## Slide 9: Slicing
  Network Slicing is a concept to allow Mobile Network Operators (MNO) to consider customers with different service requirements
  Slice selection is “similar” to PLMN sharing in terms of implementation
    Dedicated frequency priorities (as in LTE) can be used by network to prioritise frequencies that support the slices allowed
  UE can support max 8 network slices simultaneously
  Resource management between slices: Partitioning and isolation of resources
    Largely handled via implementation with no RAN standards impact
  No direct relationship in specifications between slicing and other vertical services such as URLLC

## Slide 10: Other RRC functions
System information broadcast and acquisition
  On demand SI transfer – network does not always have to broadcast SI, saves network energy and resources
Access class barring and overload handling
  Unified Access Control mechanism different from LTE, providing similar functionality
Paging similar to LTE
  Paging occasion calculation formula updated to consider NR PHY and is S-TMSI based
Positioning
  UE operating in NR can obtain position using LTE signals and RAT independent methods
  No support for native NR methods in Rel-15 other than E-Cellid
UE capability transfer
  Similar to LTE with storage in AMF
ANR/SON (but no MDT in Rel-15)

## Slide 11: RRC INACTIVE (new state)

## Slide 12: Motivation of the new RRC_INACTIVE state
Significant delay reduction in INACTIVE to CONNECTED compared to IDLE to CONNECTED
Reduce the signalling overhead (on radio and network interfaces), enabling UE power consumption similar to IDLE while improving the UE access latency
Key aspects:
  UE context storage in in RAN during INACTIVE
    UE context stores both 5GC information including security and UE radio configurations
    allowing transitions between INACTIVE and CONNECTED without involving Core Network
    UE centric mobility, e.g. cell (re)-selection in INACTIVE
      Transitions between Inactive and Connected, and mobility while in Inactive are hidden from CN

## Slide 13: State transitions
INACTIVE  CONNECTED
  3-step RRC procedure
CONNECTED  INACTIVE
  1-step RRC procedure
INACTIVE  IDLE
  2-step RRC procedure for RNAU (request/release)
  Autonomously by UE:
    Upon reception of CN initiating paging
    Upon reselecting to other RAT

## Slide 14: RAN-initiated paging, RAN Notification Area (RNA) and RAN Notification Area Update (RNAU)
RRC_INACTIVE is characterized by
  Use of RAN Notification area (RNA) for INACTIVE
    similar to CN tracking area for Idle
  RNA is configured per UE by gNB
    1 to N cells defined by a List of cells or list of RAN Area ID or list of TA IDs
  UE is reachable within a configured RNA via a RAN-initiated paging
    RAN-initiated paging uses a RAN configured UE ID (I-RNTI)
  RNAU triggered periodically and when moving outside of the configured RNA

## Slide 15: UE triggered transition from RRC_INACTIVE to RRC_CONNECTED

## Slide 16: Network triggered transition from RRC_INACTIVE to RRC_CONNECTED

## Slide 17: Security handling: forward compatibility for Early data transmission
“New key” (NCC) provided to UE when UE is suspended to be used at next Resume
  Forward compatibility for Early data transmission
    Possibility to introduce mechanism to send encrypted data using new key immediately after ResumeRequest
      May be discussed in later release
  msg 4 (Resume) can be encrypted to carry RRC reconfiguration information avoiding multi step reconfiguration

## Slide 18: “Fallback” to connection establishment
Fallback for quick recovery in case network cannot resume UE
  E.g., if the RAN cannot retrieve UE context
  Direct step from Resume request to Setup
    Avoids another RACH access compared to new Connection Request
Can also be used with re-establishment

## Slide 19: User plane and 5G QoS

## Slide 20: User plane protocol stack - overview
NR PDCP, RLC and MAC are all new protocols but share many similarities with corresponding LTE protocols
SDAP protocol introduced to support new flow based QoS model of the 5GC

## Slide 21: New QoS model for 5GC
  QoS flow based marking in Core Network instead of EPS bearers to differentiate QoS “streams” in a PDU session
  RAN continue to use DRBs
    All packets in a DRB will receive same QoS treatment
  Mapping of QoS flow to DRB is left to gNB implementation (new concept)
    Results in two step mapping:
    IP to QoS flow in NAS
    QoS flow to DRB in AS

## Slide 22: Service Data Adaptation Protocol (SDAP)
5G CN and upper layers in the UE mark packets for transmission with a QoS flow identifier (QFI)
Each QFI associated with different QoS in terms of delay, reliability, etc
SDAP layer maps QoS flows to radio bearers, with PDCP/RLC of each RB configured appropriately for the QoS
MAC layer gives differentiated handling (e.g. priority) to traffic from different RBs
gNB has flexibility how to achieve the QoS

## Slide 23: SDAP - Reflective mapping of QFI to radio bearer
The mapping from QFI to radio bearer is controlled by the gNB in 2 ways:
RRC configuration signalling
Reflective mapping
  A QFI is transmitted in the UL on the same radio bearer as that QFI was received in DL
  Enable changing QFI to radio bearer mapping in a more dynamic way and with lower signalling overhead

## Slide 24: Packet Data Convergence Protocol (PDCP)
Header compression/decompression through the use of RoHC
Ciphering and integrity protection
  Key difference compared to LTE PDCP is that integrity protection can be applied to user plane traffic as well as control plane signalling
Data duplication
  Key new feature compared to LTE PDCP
Duplication detection and reordering of received PDPC PDUs

## Slide 25: PDCP - Data duplication
  PDCP PDUs can be duplicated for transmission over 2 RLC bearer
  Motivated to enable the reliability/delay requirements for URLLC applications
  In case of carrier aggregation (CA)
    Restrictions configured in the MAC ensure that duplicated data is transmitted via different component carriers
  In case of dual connectivity (DC)
    RLC bearers are mapped to different cell groups (i.e. MCG and SCG)

## Slide 26: Radio Link Control Protocol (RLC)
Similar functionality compared to LTE RLC:
  Segmentation to match the transmitted PDU size to the available radio resources
  Error correction through ARQ
Key differences compared to LTE RLC:
  Does not provide concatenation of RLC SDUs
    Equivalent functionality now provided by the MAC layer. Motivated to enable UL RLC PDUs to be pre processed within the UE before reception of UL grant.
  Does not provide reordering of received RLC SDUs
    Equivalent functionality now provided by the PDCP layer

## Slide 27: Medium Access Control (MAC)
  Similar functionality compared to LTE MAC:
    Multiplexing and demultiplexing of data from different radio bearers to the transport blocks that are carried by the physical layer
    Priority handling between data from different radio bearers
    Error correction through Hybrid ARQ.
    Discontinuous reception (DRX)
  Key differences compared to LTE MAC
    Functionality to support beam based operation for high frequent operation.
    More flexible UL configured grants
    MAC PDU format optimised to enable pre-processing and facilitate low delay

## Slide 28: MAC - Support of beam based operation
  Beam failure detection and recovery
    UE Phy layer monitors beam failure detection (BFD) reference signals to determine a beam failure
    On beam failure detection the UE MAC layer initiates beam failure recovery
      Selects a suitable beam on which to attempt recovery
      Performs random access procedure
  Beam management
    Mobility between beams is performed by a combination of Phy and MAC signalling
    RRC signalling involved only to provide a measurement configuration (e.g. configuration of the reference signals to be measured, etc)

## Slide 29: MAC - UL configured grants
2 types of UL configured grants are available:
  Type 1 - the configured UL grant and periodicity is configured by RRC signalling
  Type 2 - the configured UL grant is provided by Phy signalling (PDCCH) and periodicity is configured by RRC signalling (similar to UL SPS in LTE)
In DL, Semi-Persistent Scheduling (very similar to LTE SPS) is supported

## Slide 30: Control plane for EN-DC

## Slide 31: Non-Standalone: overall architecture
Dual connectivity:
  Master Node (MN):
    Overall master, responsible for connection establishment with UE, connection to Core network, handover etc.
    Master Cell Group (MCG) for UE
    For EN-DC, MN is an LTE eNB
  Secondary Node (SN)
    Secondary Cell Group (SCG) for UE
    For EN-DC, SN is an NR gNB

## Slide 32: Non-standalone: Control plane for EN-DC
Single RRC state machine and control plane connection to CN based at MCG
Network has two RRC entities (MCG and SCG) that can generate full RRC messages
  RRC messages generated by the secondary can be transported transparently by the master (at least in some cases, e.g. for first configuration)
Direct RRC messages from SCG over NR – SCG SRB (SRB3)
Including
SRB3
MCG RRC
SCG RRC
MCG RRC
SCG RRC
RLC
/
MAC
/
PHY
MCG PDCP
MCG PDCP
SCG PDCP
UE
Inter Node
interaction
Interaction
RLC
/
MAC
/
PHY
SCG PDCP
RLC
/
MAC
/
PHY
RLC
/
MAC
/
PHY
RRC
diversity
through
split bearer

## Slide 33: SRB3: SCG SRB
  A new direct SRB between SeNB and UE – SRB3
    Motivation:
      Lower signalling delay over direct NR interface – no Xn delay and faster NR radio
      Less processing at MN
    Can only be used for messages that do not need coordination between MN and SN
  Can be configured based on SN decision.
    The following RRC messages can be sent via the SRB in the SCG
      RRCConnectionReconfiguration, RRCConnectionReconfigurationComplete, MeasurementReport
    SCG SRB is of higher scheduling priority than all DRBs
  UE still processes one message at a time in sequence irrespective of the path the message is received in

## Slide 34: Sub architecture options (3, 3a, 3x) and Bearer types
Different bearer types based on:
  Bearer termination point of the CN interface; and
  Radio interface used for data transfer
Single UE may be configured with different bearer types
MN terminated and SN terminated bearer types
    Indicates where the data from core network for that bearer terminates in RAN
      Also indicates the location of SDAP (for 5GC) and PDCP entities in the network for this bearer
      E.g., MN terminated bearer implies all the data to and from CN for this bearer is through MN
    Does not imply anything about which radio interface is used for this bearer

## Slide 35: MCG And SCG bearer
Indicates which radio interface is used to data for this bearer
  MCG bearer implies all the data for this bearer is sent only over MCG radio interface
    RLC bearer (RLC +MAC logical channel) in MCG
  SCG bearer implies all the data for this bearer is sent only over SCG radio interface
    RLC bearer in SCG
  Figure shows MN terminated MCG bearer (option 3) and SN terminated SCG bearer (option 3a)

## Slide 36: MN terminated split bearer (option 3)
Split bearer:
  Indicates both MN and SN RLC bearers are configured for this bearer
  DL data can be sent over both
  UL data can be configured to be sent over
    Either one of the two UL; or
    Split over both paths; or
    Duplicated over both paths

## Slide 37: SN terminated split bearer (option 3x)
Split bearer as before
CN connection for data transfer is over SN
New option introduced for EN-DC
Allows more flexible network implementation without impacting LTE eNB hardware
  All PDCP processing in SN for this bearer

## Slide 38: Unified bearer at UE
A unified split bearer concept at UE
  Agnostic of the PDCP location (termination point)
    common behaviour at the UE
  Supports MCG/SCG or both RLC bearers for a PDCP entity
  Change of bearer type is simple – by adding or removing RLC bearers

## Slide 39: Split MCG SRBs
Similar to split DRB but for MCG SRBs (SRB1 and SRB2)
  MCG signalling reliability, especially during HO
    But only relevant if there happens to be an SN at MN cell border
For DL, selection of transmission path depends on network implementation
UL packet transmission is configured by RRC to use MCG path, or duplicate on both MCG and SCG
Duplication and duplicate detection functions in PDCP

## Slide 40: Other MR-DC architectures
Other architectural options to be completed by Dec 2018 in Rel-15 late drop
  NG-EN-DC: EN-DC with 5GC
  NR-DC: NR NR Dual connectivity
  NE-DC: NR is master and LTE as secondary node
Based on EN-DC architecture
  Main differences:
    NR-DC coordination and capability handling
    Small changes Security requirements from integrity protection of DRBs

## Slide 41: Release 16

## Slide 42: Release 16 work programme (1)
3GPP will continue to evolve NR functionality in Release 16 (due for completion in Q4 19) and beyond.
These slides provide very brief overview of the Release 16 work items led by 3GPP RAN working group 2 (working group responsibility for radio interface protocols)
There is other work led by other working groups e.g:
  NR in unlicensed spectrum (NR-U), NR V2X, NR positioning, NR for non terrestrial networks, etc

## Slide 43: Release 16 work programme (1)
Integrated Access and Backhaul (IAB)
  Currently in a study phase
  Investigating the architecture and radio protocols impacts to introduce relaying where NR radio interface is also used on the backhaul links to/from the relay nodes
  Motivated by the desire to enable very dense deployment for NR cells while minimising costs associated with the backhaul network
  Aiming to support multi-hop relaying
Enhancements for Industrial IoT
  Currently in study phase
  Main focus of work is the introduction of support for Time Sensitive Networking (TSN) including provision of accurate time reference, Ethernet header compression

## Slide 44: Release 16 work programme (2)
NR mobility enhancements
  Work due to start in Q1 19
  Aiming to provide enhancements for handover interruption time and reliability
NR dual connectivity and carrier aggregation enhancements
  Work due to start in Q1 19
  Aiming to provide various enhancement to CA/DC operation including faster measurement reporting of candidate cells and faster activation of CA and/or DC
Optimisations on UE radio capability signalling
  Currently in study phase
  Investigating mechanisms to reduce the overhead of UE capability signalling

## Slide 45: Summary

## Slide 46: Summary
RRC: Control plane functions and procedures
  INACTIVE state and message flow for transitions to RRC_Connected
User plane protocols
  SDAP and 5G QoS
  PDCP and packet duplication
  RLC functions with optimisation for UE implementation
  MAC functions and enhancements for NR
Non standalone specific functions
  MN and SN, RRC structure, SRB3
  Bearer types and unified bearer in the UE
Rel-16 topics: IAB, IIoT, Mobility, CA/DC enhancements, UE capability transfer optimisation

## Slide 47: Backup

## Slide 48: Terminology
  NR Name of the Radio Access Technology (equivalent to E-UTRA).
  NG-RAN RAN that connects to 5GC
    Could use either the NR or E-UTRA radio access technology
    Note NG-RAN is defined by its connectivity to the 5GC and not by the radio it uses.
  gNB Node B that used the NR Radio Access Technology
    en-gNB - Node B that uses NR for E-UTRA-NR Dual connectivity. You might see this but not expected to be commonly used in RAN2 specs (more in RAN3 specs)
  NR, NG - are 'monolithic' terms - they do not stand for anything!
  5G Marketing name and logo for 3GPP Rel-15 specs related to NR
    Others in the industry may use '5G' in different ways

## Slide 49: Characteristics of RRC states
RRC_IDLE | RRC_INACTIVE | RRC_CONNECTED
UE controlled mobility based on network configuration (cell reselection) |  | Network controlled mobility within NR and to/from E-UTRAN
DRX configured by NAS | DRX configured by NAS or gNB | DRX configured by gNB
Broadcast of system information |  | Neighbour cell measurements
Paging (CN-initiated) | Paging (CN-initiated or NG-RAN-initiated) | Network can transmit and/or receive data to/from UE
UE has an CN ID that uniquely identifies it w/in a tracking area | NG-RAN knows the RNA which the UE belongs to | NG-RAN knows the cell which the UE belongs to
No RRC context stored in gNB | UE and NG RAN have the UE AS context stored, and the 5GC - NG-RAN connection (both C/U-planes) is established for UE | 

## Slide 50: Signalling flow and use of reflective QoS in RAN and CN

## Slide 51: RRC message for unified bearer type
Overall RRC message structure
A split bearer
RRC configuration structure of the
user plane for multiple bearers (FFS)

## Slide 52: RRC message for unified bearer type
Overall RRC message structure
A split bearer configured
as SCG bearer
RRC configuration structure of the user plane
when configured as SCG bearer
pdcp
-
Config
(incl. drb
-
ID)
pdcp
-
Config
(incl. drb
-
ID
)
pdcp
-
Config
(incl. drb
-
ID
)
MCG
-
Config
SCG
-
Config
drb
-
ID
rlc
-
Config
mac
-
LCH
-
Config
drb
-
ID
rlc
-
Config
mac
-
LCH
-
Config
mac
-
MainConfig
p
hy
-
Config
drb
-
ID
rlc
-
Config
mac
-
LCH
-
Config
drb
-
ID
rlc
-
Config
mac
-
LCH
-
Config
mac
-
MainConfig
phy
-
Config

## Slide 53: Deployment Options
Option 2 – NR Standalone
Option 3 – Non Standalone (EN-DC)
Option 5 – Evolved E-UTRA standalone
Option 7 – NSA with NG Core (NG-EN-DC)
Option 4 – NE DC

## Slide 54
Next Generation and Standards (NGS)
Client and Internet of Things (IoT) Businesses and Systems Architecture Group