## Slide 1: 3GPP’s Low-Power Wide-Area IoT Solutions: NB-IoT and eMTC
RWS-180023
Workshop on 3GPP Submission Towards IMT-2020
24-25 October 2018
Brussels, Belgium

## Slide 2: Four KPIs for 3GPP LPWA IoT solutions
Connection density
1 000 000 UEs/km2
UE battery life 10 – 15 years in 164 dB MCL
Coverage extension 164 dB MCL @160 bps
UE complexity and cost
Ultra-low
SmartElec Limited
0
2
3
5
Low-power wide-area IoT

## Slide 3: NB-IoT and eMTC project timelines
Multicast, positioning, higher data rates, etc.
Category NB2 and M2.
Fundamental radio and core networks.
Category NB1 and M1 UEs defined.
Rel-16
Rel-15
Rel-13
Aug/Sep ‘14
Jun ‘16
Mar ‘17
Jun ‘18
Rel-14
Note: Performance parts finish ~6 months later. Conformance testing specification follows.
Dec ‘19
“Wake-up signal”, early data transmission, faster cell access, reduced signalling overheads, etc.
TDD for NB-IoT.
Immediate UE data transmission, finer-grained “wake-up signal”, simplified control signalling, additional UE feedback, etc.

## Slide 4: mMTC connection density
NB-IoT
eMTC
Single-tone and 3/6/12-tone UL allocations
1-tone
3-tone
6-tone
12-tone
15 kHz
15 kHz
×12
…
3.75 kHz
×48
…
3.75 kHz
Non-anchor carriers for capacity and load-balancing
Dense subcarrier spacing
3-tone
6-tone
180 kHz
180 kHz
1.4 MHz
3- and 6-tone allocations within a PRB of a 1.4 MHz narrowband
eMTC narrowband
eMTC narrowband
…
LTE or NR
Deploy multiple independent eMTC narrowbands within LTE/NR bandwidth
1.4 MHz
1.4 MHz
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
…
…

## Slide 5: Ultra-low UE complexity: Signal processing simplifications
0101011100101010110010011001001001101010011011101101010010100010010111011001100101110100100011101010100100111001
1 ms
Cat. 1 data
10 000 bits / ms
101110110001001010001000011101100110010111011110 10101001
1 ms
Cat. M1 data
1000 bits / ms
1011110110001001010001001011101000110010111010011
Cat. NB1 data
UL: 1000 bits / up to 10 ms
DL: 680 bits / up to 10 ms
Up to 10 ms
? | ? | ? | ? | ? | ? | ?
? | ? | ? | ? | ? | ? | ?
? | ? |  | ? | ? | ? | ?
? | ? | ? | ? | ? | ? | ?
? | ? | ? | ? | ? | ? | ?
? | ? | ? | ? | ? | ? | ?
Control channel
~40 candidates / ms
? | ? | ? | ?
? | ? | ? | ?
? |  | ? | ?
? | ? | ? | ?
Control channel
~16 candidates / ms
1 ms
1 ms
?
?
?
?
4 ms

Control channel
~1 candidate / ms
LTE
eMTC
NB-IoT

## Slide 6: Ultra-low UE complexity: Hardware simplifications
RF bandwidth  RF hardware cost
BB bandwidth  signal processing cost
LTE
eMTC
NB-IoT
20 MHz RF & BB
1.4 MHz
180 kHz
X
Single receive RF chain for UE
20 dBm and 14 dBm UE transmit power classes
Lower peak current requirement allows cheaper, smaller batteries
DL
UL
Half-duplex operation allows removal of duplexer from UE
(Mandatory NB-IoT, optional eMTC)
retune
retune

## Slide 7: Ultra-low UE complexity: Further steps in NB-IoT
NB-IoT takes additional steps to allow low-cost hardware:
  Downlink uses convolutional encoding, removing need for turbo decoder in UE
  1 or 2 HARQ processes, instead of 8 in LTE/eMTC, reduces memory for data buffering
  Synchronization signals with low complexity, optimised for reception in deep coverage
  Maximum modulation is QPSK instead of 16-QAM, lessening EVM requirements
  UE is allowed a much longer time to decode a reception before reacting to it, e.g. for DL:
  40 ms gap after each 256 ms of transmission during UL, allowing UE to re-sync to DL
    Allows lower-cost non-temperature compensated crystal oscillators to be used in chipsets
    Mandatory in NB-IoT UEs, optional for eMTC
RX
LTE/eMTC: 4 ms
ACK/NACK
ACK/NACK
NB-IoT: 12 ms
UE receives a DL transport block

## Slide 8: Coverage extension
PSD
f
LTE
eMTC
NB-IoT
PSD boost in bandwidth as small as 3.75 kHz
Low-PAPR π/2-BPSK modulation (and π/4-QPSK in NB-IoT)
A
B
C
D
E
F
G
A
A
A
×1 to ×2048 repetitions
…
…
LTE uses single-subframe transmission
NB-IoT and eMTC repeat same transmission to accumulate RX’d power
t
SINR
BLER
Relaxed requirements to tolerate lower SINR regimes

## Slide 9: Battery life 10 – 15 years
t
TX
paging chances
PSM time
Up to ~400 days
UE is unreachable
t
RX/TX
WUS
“Wake-up signal”
X
X
NB-IoT: No handover measurements / signalling
UE
eNB
DATA
DATA
Earlier data transmission, without tx/rx’ing to complete connection
paging chances
RSRP
t
5 mins
24 hours
±X dB
Stationary UE can suspend measurements of neighbour cells
Power use
t
eDRX time
RX/TX
paging chances
NB-IoT: ≤ 3 hr
eMTC: ≤ 40 min
Power use
Power use

## Slide 10: Hallmarks of 3GPP LPWA IoT technologies
Battery life of 15 years or more on 2AA cells (5 Wh)
Optimised for small infrequent packet transmissions e.g. 50-200 bytes few times/day
Transfer data earlier with fewer transmissions, and less battery consumption
Maximise time UE can spend in low-power states and eliminate avoidable UE RX/TX
SmartElec Limited
0
2
3
5
Support for normal to moderate coverage and deep coverage scenarios
Repetition, PSD boosting, and low-PAPR transmissions
In good coverage, NB-IoT and eMTC do not need repetitions
mMTC connection density of ≥1 000 000 UE/km2
Small resource allocations, 3.75 kHz subcarriers (NB-IoT), scalable network capacity
Reduced signalling overhead to free-up resources for connecting more devices per cell
Complexity and cost is much lower than MBB devices
  Reduced RF and baseband bandwidths of 1.4 MHz for eMTC and 180 kHz for NB-IoT
  Relaxed signal processing requirements, with further relaxations in NB-IoT