## Slide 1: [104#11] Target CSI-RS capabilities & proposed structure
Item | Feature name | Components | values | Curent granularity
2-15a | List of association between CSI-RS and SRS (up to 16) | 1) Maximum number of Tx ports in one resource across all CCs | 2, 4, 8, 12, 16, 24, 32 | Per band per band combination
 |  | 2) Maximum number of resources across CCs | 1 to 64 | 
 |  | 3) Total number of Tx ports across CCs | 2 to 256 | 
2-36 | List of type I single panel codebook (up to 16) | 1) Maximum number of Tx ports in one resource across all CCs | 2, 4, 8, 12, 16, 24, 32 | 
 |  | 2) Maximum number of resources across CCs | 1 to 64 | 
 |  | 3) Total number of Tx ports across CCs | 2 to 256 | 
 |  | 4) Supported codebook mode | Mode 1, Mode 1/2 | 
 |  | 5) Maximum number of CSI-RS resource in a resource set | 1 to 8 | 
2-40 | List of type I multi-panel codebook (up to 16) | 1) Maximum number of Tx ports in one resource across all CCs | 8, 16, 32 | 
 |  | 2) Maximum number of resources across CCs | 1 to 64 | 
 |  | 3) Total number of Tx ports across CCs | 2 to 256 | 
 |  | 4) Supported codebook mode | Mode 1, 2, both | 
 |  | 5) Supported number of panels | 2, 4 | 
 |  | 6) Maximum number of CSI-RS resource in a resource set | 1 to 8 | 
2-41 | List of type II codebook (up to 16) | 1) Maximum number of Tx ports in one resource across all CCs | 4, 8, 12, 16, 24, 32 | 
 |  | 2) Maximum number of resources across CCs | 1 to 64 | 
 |  | 3) Total number of Tx ports across CCs | 2 to 256 | 
 |  | 4) Parameter “Lx” | 2, 3, 4 | 
 |  | 5) Amplitude scaling type | Wideband, wideband & sub-band | 
 |  | 6) Amplitude subset restriction level | Supported | 
2-43 | List of type II codebook with port selection (up to 16) | 1) Maximum number of Tx ports in one resource across all CCs | 4, 8, 12, 16, 24, 32 | 
 |  | 2) Maximum number of resources across CCs | 1 to 64 | 
 |  | 3) Total number of Tx ports across CCs | 2 to 256 | 
 |  | 4) Parameter “Lx” | 2, 3, 4 | 
 |  | 5) Amplitude scaling type | Wideband, wideband & sub-band | 
Proposed Components |  | Proposed granularity
CSI-RS resources common to all supported codebook types (common to all or different?) (up to 16 or reduced?) | 1) Maximum number of Tx ports in one resource across all CCs | Per band combination
 | 2) Maximum number of resources across CCs | 
 | 3) Total number of Tx ports across CCs | 
Supported codebook type | 2-36) Type I single 2-40) Type I multi 2-41) Type II 2-43) Type II with port selection 2-15a) SRS association with CSI-RS | Per band combination
Supported codebook mode (same value for 2-36 and 2-40 or different?) |  | Per UE (or per band?)
Maximum number of CSI-RS resource in a resource set (same value for 2-36 and 2-40 or different?) |  | Per UE (or per band?)
Supported number of panels (2-40 only) |  | Per UE (or per band?)
Parameter “Lx” type (same value for 2-41 & 2-43 or different?) |  | Per UE (or per band?)
Amplitude scaling type (same value for 2-41 & 2-43 or different?) |  | Per UE (or per band?)
Amplitude subset restriction level (2-41 only) |  | Per UE (or per band?)