## Slide 1: On controversy over L1 UE capability CR
NTT DOCOMO, INC.
TSG-RAN meeting #82
10th – 13th December 2018, Sorrento, Italy
RP-182743

## Slide 2: Background
While RAN2 developed the CRs (to 38.306/331) on L1 capability according to the latest RAN1 UE feature list, RAN2 identified the following issues on CSI-RS capabilities in the Sep/2018 spec:
  Astronomically large signaling;
  Definition and signaling granularity are contradictory;
  Lack of the default behavior (in case the capability signaling is absent).
  Supporting/enabling different CSI-RS characteristics/IODT status for individual operating band is not allowed.
RAN2 discussed restructuring the CSI-RS capabilities to iron out the identified issues during and after the Nov/2018 meeting, however has not concluded yet...
  The key issue is whether the CSI-RS capabilities should be restructured or not, and if so, how?

## Slide 3: Proposals
Two company CRs are submitted for approval.
  RP-182742, “Update of L1/RF capabilities,” CR to 38.331, NTT DOCOMO
  RP-182744, “Update of UE capabilities,” CR to 38.306, Intel Corporation
  These CRs reflect the up-to-date consensus achieved by RAN2 together with RAN1
Consequences if the CRs are not agreed:
  Need to live with the risk of huge signaling potentially exceeding the maximum SDU size.
  The network may not be able to configure CSI-RS due to the incomplete definition and lack of the default behavior.
  CSI-RS capabilities (e.g. max number of Tx ports, etc.) cannot be differentiated for FDD/TDD and/or FR1/FR2.