## Slide 1: 147-E MBS pre-meeting discussion
LiMeng
2021.09

## Slide 2: Topics
Topic #1: Multicast PCC related issues
  1.1: Terminology (e.g., “Configuration” versus “Creation”);
  1.2: Possible procedure enhancement (e.g., mentioned in S2-2105653);
Topic #2: Handle associated QoS flows in PCC.
  2.1: Possible procedure enhancement (e.g., mentioned in S2-2106433).
Others:
  Topic #3: Policy control service for multicast and data
  Topic #4: Documentation of NRF NF profile extensions in TS 23.501
  Topic #5: Inform RAN of UE Join
  Topic #6: Replacement reference point architecture
Click here to join the meeting
Topic | Scheduled time
1.1 | 20 min.
1.2 | 30 min.
2.1 | 30 min.
3 | 40 min.
4 | 
5 | 
6 | 

## Slide 3: Topic #1: Multicast PCC related issues -- 1.1 Terminology (e.g., “Configuration” versus “Creation”)
Option #1: Replace “Session Configuration” with “Session Creation”:
  Rationale:
    “Session Configuration” cannot really reflect the situations for the broadcast sessions. For broadcast, receiving from AF will be followed by the creation of Broadcast context at RAN nodes.
    “Configuration” is more used for OAM purpose.
    For the status that only TMGI is allocated, “Creation” seems more proper.
Option #2: Current description in TS.
  Rationale:
    Better to provide more evidences to justify the terms update.
Companies | Views
Nokia | If we go for “creation”, then other subheadings in 7.1.1 would also need to be updated to remove “configuration”, and the figures I pasted in and related description would also be impacted. I could live with that. But my take from our last discussions was that the term “MBS Session Management" also caused some concerns as session management is also used for quite different procedures. So we should also check if that one is now agreeable to everybody.
Qualcomm | In the end it is a term, so we hope we don’t spend too much time on this one. We’re ok with “configuration” as it seems less changes to current TS. However, one way forward can be to have explicit text that configuration for broadcast also triggers configuration in RAN, and explicitly mention the distinction with respect to multicast case.
Huawei | We consider “creation and configuration” issue is rather a terminology issue and we are open to keep the original ones or have a new set of terms. The previous one seems easier. Possible way forwards: We keep using “configuration”, and we add terms for configuration in 3.1 to describe configuration (along the same line as we defined Multicast Session Configuration in section 4.3), and we also specify for broadcast, configuration triggers session start procedure, as suggested by Qualcomm. Or, For the related description, we replace “configuration” with “create” (and similar for others). For this option, it is suggested to have a single CR that include the changes for all related clauses, e.g., 7.1.1, 4.2.
Ericsson | 1.1_S2-210xxxx_23247CRxxx_MBSsessionManagementvsConfig_r1.docx
CATT | We support Qualcomm’s view and No.1 way forward proposed by Huawei. We don’t believe the use of “configuration “ is confined to OAM and cannot be used for MBS, considering that we have already made clear definition of MBS session configuration.
ZTE | No strong view on whether option 1 or option 2. This is quite terminology issue. Maybe an easy way is, for the broadcast, we rename the “configuration procedure” to “configuration and session establishment procedure”. In the multicast configuration procedure, the NG-RAN is not involved. For multicast the sequence are: Configuration, join and session establishment, UE leave and session release For broadcast the sequence are: Configuration and session establishment, session release
Topic | Scheduled time
1.1 | 20 min.

## Slide 4: Topic #1: Multicast PCC related issues -- 1.2 Possible procedure enhancement for session configuration
Alternative-1 (S2-2105653): It is always MB-SMF that interacts with PCF when necessary;
Alternative-2 (S2-2105653): Only MB-SMF – PCF interaction for MBS session start, AF (maybe via NEF/MBSF) interaction with PCF for MBS Session update of QoS;
Alternative-3: Status-quo
Rationales provided by companies were (summarized from S2-2105653 and the comments):
  Simplify NEF/AF/MBSF/MB-SMF realization when PCC is used – NEF/AF/MBSF/MB-SMF do not need to differentiate the cases for deploying PCC or not.
  No need to further optimize the procedure when PCC is used, i.e., in 7.1.1.3-1, step 24 will update the session that is started in step 13, which causes potential signally waste.
  Unclear for the default Policy (for temporary use) when PCC is used, i.e., in 7.1.1.3-1, the MBS policy in step 16.
  Potential high failure possibility of the configuration procedure due to the number of interactions.
Companies | Views
Nokia | Alternative-3. Rational is to keep PCC procedures and SBIs as similar as possible to existing non-MBS procedures / APIs as possible. It is an advantage to enable reuse of existing implementations for both for service producer (PCF) and service consumers (MB-SMF (assuming that is derived from SMF) and NEF / AF. In particular I do not agree that MB-SMF implementation would be simplified. To the contrary, the function to split service information for PCC and other service information would be added which is otherwise in the NEF. Complexity is thus simply shifted. Issue with default policy can be easily resolved via policy update or via preconfigured information in UDR. Alternative 2 of Ericsson would also be a nightmare for the service design (PCF resources to describe an MBS session created by MB-SMF and subsequently modified by NEF)
Qualcomm | We are ok with Alternative-1 or Alternative-3, not OK with Alternative-2. It seems to us both 1 and 3 can work from system perspective, there’s an inherent complexity in PCF interaction, we’re open to either approach.
Huawei | Alternative-1 is acceptable for us. But if we cannot reach consensus on alternative-1, alternative-3 (i.e., keeping current specification) is also OK since it is workable and we already specified that.
Ericsson | 1.2a_S2-210xxxxDP_5MBS_PCC.doc 1.2b_S2-210xxxx_23247CRxxx_MBS_PCC_r1.docx
CATT | We support alt3, i.e. the existing MBS session configuration procedures as specified in clause 7.1.1, incl. initial MBS session configuration/configuration update with/without PCC. (--Meanwhile, we also support to study AF interacts with PCF via NEF/MBSF and UDR for MBS session establishment and update in Rel-18.)
ZTE | Alternative-3. Similar view with Nokia.
Topic | Scheduled time
1.2 | 30 min.

## Slide 5: Topic #2: Handle associated QoS flows in PCC -- 2.1 Procedure enhancement on policy control for individual fallback
Companies provided documents for several meeting on the issue of individual fallback in policy control, see step 7 of Figure 7.2.1.3-1 in TS 23.247.
The issue is whether it is acceptable to continue to complete the procedure to align with the call-flow.
Proposals: see page 3 of S2-2106433.
Rationales: see follows (excerpt from S2-2106433):
  The SMF obtains the information about the QoS flows for multicast from the MB-SMF. (But) other QoS flows are determined by the SMF based on Policy Rules supplied by the PCF.
  QoS flows contain QoS rules with Packet filters and priorities and QFIs that need to be harmonized and decided upon based on policies. Associated QoS flows should be kept separate from QoS flows where radio resources are always reserved. Thus, special 5QIs not used for the PDU session may need to be allocated. This conflicts with existing QoS flow binding procedures in TS 23.503.
  Total available bandwidth also needs to be considered
  Policy control should be able decide which services the user can obtain simultaneously
Companies | Views
Nokia | Positive.
Huawei | We consider it would be better to provide additional evidence for introducing SMF-PCF interaction: On establishing the associated QoS flows which are separated from the unicast QoS flow: SMF may have the sufficient information and SMF can determine the binding – there is no obvious evidence for let PCF involve in such part. On session AMBR, introducing SMF-PCF interaction is beneficial but not that necessary: during initial PDU Session establishment or after UE join, the session AMBR can be set to a higher value by triggering the PDU session modification procedure. The SMF-PCF interaction seems beneficial regarding the charging issue: since it is not easy for the MB-SMF to assume the charging responsibility for the individual delivery. But whether such part is a must needs to be confirmed by the operator.
Ericsson | 2.1a_S2-210xxxxDP_5MBS_IndividualDelivery_PCC_r1.doc 2.1b_S2-210xxxxwas6437was4017_23503CR0579_AssociatedQF_PCC impacts.docx
CATT | We prefer not to introduce SMF-PCF interaction for unicast QoS flow handling, to reduce complexity & signalling interactions during UE join procedures. The session AMBR can be set taking into account that the PDU Session is associated with MBS session, and QFIs can be reserved for mapped unicast QoS flows.
ZTE | Similar view with Huawei. If SMF-PCF interaction is needed, we’d identify the necessary scenario.
Topic | Scheduled time
2.1 | 30 min.

## Slide 6: Topic #3: Policy control service for multicast and data
 | Candidates | Currently specified
Additional parameters for PCC rule | DL sharing indication Bind to QoS Flow associated with the default QoS rule Bind to QoS Flow associated with the default QoS rule and apply PCC rule parameters Charging key Service Identifier Charging method (online/offline) Measurement method (Volume/duration/combination/event) Service Identifier level reporting | Rule identifier. Service data flow detection: Precedence, Service data flow template (only for IP PDU traffic). Policy Control: 5G QoS Identifier (5QI), DL-maximum bitrate, DL-guaranteed bitrate, ARP, Priority Level, Averaging Window, Maximum Data Burst Volume.
Additional Parameters for MBS session | Authorized MBR per QCI Explicitly signalled QoS Characteristics Authorized default 5QI/ARP Charging Information (CHF address + set) Default charging method | Authorized Session-AMBR
MBS Session policy control data in UDR | Provider categories Subscribed GBR QoS flows | 

## Slide 7: Topic #4: Documentation of NRF NF profile extensions in TS 23.501
Option 1: Define NF profile extensions in 23.247 and add reference in 23.501 clause 6.2.6.2
Option 2: Define NF profile extensions in 23.247 without reference in 23.501

## Slide 8: Topic #5: Inform RAN of UE Join
See the paper
  5_S2-210xxxxDP_5MBS_5GCInformRANofUEJoin_ed_r2.doc

## Slide 9: Topic #6: Replacement reference point architecture
See the paper:
  6_Draft S2-21xxxxx TS23.247 Replacement reference point architecture figure+ER.docx

## Slide 10: Annex

## Slide 11
SMF informs PCF that UE joined a multicast session and provides QoS flows obtained from MB-SMF for that multicast session
The PCF determines Policy Rules from the QoS flow information for the multicast session and selects 5QIs and priorities taking into account other installed PCC rules.
PCF provides Policy rules for associated QoS flows that contain an indication that those rules are for QoS flows associated with a multicast session
S2-2106433 – Proposal

## Slide 12
At the time when the UE joins, QoS flows associated to the multicast session will be added by the SMF to the unicast PDU session and marked as being associated with the multicast session in preparation to a fallback to individual delivery.
The SMF obtains the information about the QoS flows for multicast from the MB-SMF.
Other QoS flows are determined by the SMF based on Policy Rules supplied by the PCF
QoS flows contain QoS rules with Packet filters and priorities and QFIs that need to be harmonized and decided upon based on policies. Associated QoS flows should be kept separate from QoS flows where radio resources are always reserved. Thus, special 5QIs not used for the PDU session may need to be allocated. This conflicts with existing QoS flow binding procedures in TS 23.503.
Total available bandwidth also needs to be considered
Policy control should be able decide which services the user can obtain simultaneously
S2-2106433 – Problem