## Slide 1: Way forward on Identity protection, KI#3
Sony,…more?

## Slide 2: Issue to be resolved
Identity protection for group Inventory
Identity protection for Individual Inventory
  May or may not be followed by a Command.

## Slide 3: Group Inventory case
What format of the Identity Information:
  Filtering information of the permanent ID or a dedicated Group ID?
  Will a new Group ID be assigned by the Application or by the MNO?
In SA3#121 (Göteborg), A new threat related to the filtering of the permanent ID was discussed but the proposed new text was not agreed to be added.
The “ALL device” Inventory request was mentioned as a difficult case that needs to be analyzed more and should be considered in the Way forward.

## Slide 4: Individual Inventory case
All companies agrees that the identification Information in the request must be protected.
Conclusion agreed is that Temp ID shall be used. Two options
  Network assign a new Temp ID using a write command.
  Both the network and the AIoT Device derive a new Temp ID based on shared secrete and freshness parameters.
In SA3#121 (Göteborg), during a drafting the following evaluation criteria for the Temp ID were captured:
  ID Collision, Group paging, Re-Synchronization, AIoT device capability, Initial temp ID, Avoid frequently writing to NVM, Temp ID allocation should be securely protected, Temp ID update frequency, Command one by one to update the temp ID.
  Legacy Temp_ID update requirements (i.e., The Temp_ID shall be updated when used in the paging message) should be considered.

## Slide 5: Evaluation – Group Inventory (incl. filter/group ID)
 | Concealed ID (in the response) | Network Assigned Temp_ID (in the response) | Locally derived Temp_ID (in the response)
ID Collision | Yes (low probability) | No | Yes (low probability)
Re-Synchronization | No | No | Yes, if indicator is set there is risk for out-of-synch
AIoT device capability | Low | NVM | NVM
Avoid frequently writing to NVM | N/A | Network controlled (risk to send Temp_ID multiple times) | Network controlled (risk to send Temp_ID multiple times)
Initial temp ID | N/A | Command is needed or device must be provisioned before deployed. | Use initial group Inventory Request
Temp ID allocation should be securely protected | N/A | Encrypted Command message | N/A
Temp ID update frequency | N/A | Network send Command after Inventory. | Network include indicator in the Inventory request.
Inventory (ALL) | High network load (depends on group size) | Ok | Ok
Way forward: Use Concealed ID for group Inventory, but do not allow Inventory (ALL) requests.

## Slide 6: Evaluation – Individual Inventory
 | Concealed ID (in both request and response) | Network Assigned Temp_ID (in both request and response) | Locally derived Temp_ID (in both request and response)
ID Collision | Yes (low probability) | No | Yes (low probability)
Re-Synchronization | No | Yes | Yes
AIoT device capability | High compute load to decode the paging message – drain the energy storage | NVM | NVM
Avoid frequently writing to NVM | N/A | Individual Inventory is not assumed to be used frequently. | Individual Inventory is not assumed to be used frequently.
Initial temp ID | N/A | Command is needed or device must be provisioned before deployed. | Use initial group Inventory Request (use NONCE_nw as SEED)
Temp ID allocation should be securely protected | N/A | Encrypted Command message | N/A
Temp ID update frequency | N/A | Always – Must send a write command with new Temp_ID after Inventory. | Always
The high compute load for all devices to constantly decode concealed IDs in the paging messages is a show stopper as it may lead to that the devices will never be able to respond back as no/too little energy remains in the energy storage.
Way forward: Use Locally derived Temp_ID for Individual Inventory.

## Slide 7: Other important considerations
ID protection and message authentication and integrity check are tightly connected. (NONCE_nw is needed in the paging message/Inventory request)
Group Inventory is assumed to be the most important and most frequent use case in Rel-19
Individual Inventory is assumed to be less frequent:
  Individual Inventory only. – (The AF needs to locate the specific device)
  Individual Inventory preceding a write/read command. (The AF needs to write/read information)
Rel-19 devices are assumed to be very low complexity devices, reading and writing information to such devices is assumed to be a very uncommon service to support by an AIoT device.

## Slide 8: Group Inventory – WF proposal
Paging message includes:
  Target device information i.e., Filtering information of the permanent ID or a dedicated Group ID.
  NOTE: Assuming it is ok to re-use this target device information in future group inventory.
  New Nonce_nw
Matching AIoT Device:
  Calculate Concealed ID using the Nonce_nw + Key
  Derive Nonce_d
  MAC=HMAC (key, Nonce_nw, Nonce_d)
AIoT Device supporting individual inventory
  If no Temp_ID stored -> derive a Temp_ID using Nonce_nw
  Temp ID ≠ Concealed ID => Store this Temp_ID in NVM
  Network also derive the same Temp_ID and store it in the Device profile in ADM.
  Further group inventory will not trigger a new Temp_ID

## Slide 9: Group Inventory – WF proposal cont.
Pros:
  Devices that ONLY support group inventory do not need NVM
  Device complexity reduced.
Cons:
  The network needs to derive all Concealed IDs within the group to match the responses to the Devices that responded.
  Group Inventory targeting ALL devices – is not good as the network will have to derive all Concealed ID from all devices stored in the ADM.
Other:
  Group Inventory can be used to derive the “Initial” Temp_ID
  A group inventory will not trigger a new Temp_ID to be stored in the NVM. (only the first group inventory in this proposal).

## Slide 10: Individual Inventory – WF proposal
Paging message includes:
  Temp_ID (stored in the AIoT Device Profile).
  New Nonce_nw
Matching AIoT Device:
  Derive Nonce_d
  MAC=HMAC (key, Nonce_nw, Nonce_d)
  Derive new Temp_ID => store the Temp_ID
  Send a NAS Inventory response => Network derive and store the new Temp_ID
No response from AIoT Device:
  Not within range
  Temp_ID out-of-synch
    Option 1: Retry with previous and next Temp_ID as it can only be one Temp_ID off in the sequence.
    Option 2: Perform group inventory including an indication to use the Nonce_nw to generate a new Temp_ID (re-start the sequence)
    No response = out of range of the reader is confirmed

## Slide 11: Individual Inventory – WF proposal cont.
Pros:
  AIoT Device can match the Temp_ID without performing any calculations
  Consecutive Command procedure is not need to provision a new Temp_ID in the device.
  Resynch w. Option 1: Network can retry with Temp_ID in the sequence to get back into synch with the device.
  The permanent device ID or the concealed permanent device ID is not used to re-synchronize the Temp_ID.
Cons:
  AIoT Device needs to support NVM.
  ID collision may happen to with the probability of 2-n bits, where n is the number of bits used in the Temp_ID. However, if network detects devices with the same Temp_ID they would not generate the same MAC in the response. The network can resolve the ID collision.
  Resynch with option 2: Using Group Inventory to reset the Temp_ID will trigger all responding devices to reset their Temp_IDs.

## Slide 12: Way Forward Summary
Two methods used to Protect the Device ID depending on the use case:
  Group Inventory: Device responds with a concealed ID
  Individual Inventory: Device and Network locally derive Temp_ID
LS to RAN2
  Ask if the paging message can include a Nonce_nw
LS to SA2 and RAN2
  Informing that ID protection for large groups will consume proportional network compute resources.
  Inventory request (ALL) shall not supported.