## Slide 1: AIoT Temp ID way forward
OPPO

## Slide 2: Temp ID based AIoT ID protection
Network is aware whether Inventory only or Inventory and Command procedure is used and can decide which of the following to use.
  For the Inventory only procedure, new Temp ID (which is used for the next round of paging procedure) is generated by the device and the AIoTF separately.
  For the Inventory and Command procedure, new Temp ID is secured allocated to the device by the AIoTF.

## Slide 3: Temp ID based AIoT ID protection for Inventory
The AIoTF and device pre-stored the Temp ID (e.g., initial pre-provisioned Temp ID).
The AIoTF receives AIoT service operation (i.e., Inventory) request, it sends Inventory Request to the NG-RAN.
  If it targets to one/multiple individual AIoT device, message includes one or multiple Temp ID(s), and a Nonce;
  If it targets to a group of AIoT devices, message includes filter info, a Nonce, and an indicator (indicate device to generate Temp ID);
The device(s) matches the ID info in the paging message, and check indicator. The device(s) generate new Temp ID using (TID = F(PSK, Temp ID/permanent ID, Nonce), and stores new Temp ID for next paging;

## Slide 4: Temp ID based AIoT ID protection for command
The AIoTF and device have pre-stored the Temp ID (e.g., pre-provisioned initial TID).
The AIoTF receives AIoT service operation (i.e., Command) request. The AIoTF performs inventory procedure with the device(s) using current Temp ID. Then the AIoTF allocates the new Temp ID to the device in the Command procedure.
The device receives new Temp ID sent protected in the Command Request, and stores the new Temp ID for subsequent paging.
The AIOTF receives Command response from the device, to make sure that the device has refreshed the Temp ID.

## Slide 5: Temp ID based AIoT ID protection——synchronization
If Inventory procedure failed (e.g., AIoT Device did not complete Inventory Report message), AIoTF does not update Temp ID.
In inventor-only procedure, only after the device receives ACK after ID transmission to the reader, then device updates the Temp ID with new generated Temp ID. Otherwise, the device remains the Temp ID.