## Slide 1: 3GPP Standards Update
Adrian Scrase
Head of 3GPP Mobile
Competence Centre

## Slide 2: The role of 3GPP
GSM, GPRS, EDGE, W-CDMA, HSPA and LTE are all [RAN] Technologies specified by 3GPP
Core network and Systems architecture evolution have kept pace
The 3GPP Organizational Partners are Regional and National Standards Bodies;
Companies participate through their membership of one of these 6 Partners

## Slide 3: 3GPP Membership
378 Organisations (November 2010)

## Slide 4: Where the work is done
Chart: 
| Asia | Europe Middle East & Africa | North America
 | 4517 | 4689 | 2006
Meeting Delegates* by region (June 2010):
* Participants in TSG and WG meetings over the last year
Plenary meetings every 3 months, approve specifications and the Freezing of 3GPP Releases
The 50th TSG Plenary will be in Istanbul in December 2010

## Slide 5: Spanning the Generations...
3GPP Specified Radio Interfaces
  2G radio: GSM, GPRS, EDGE
  3G radio: WCDMA, HSPA, LTE
  4G radio: LTE Advanced
3GPP Core Network
  2G/3G: GSM core network
  3G/4G: Evolved Packet Core (EPC)
3GPP Service Layer
  GSM services
  IP Multimedia Subsystem (IMS)
  Multimedia Telephony (MMTEL)
  Support of Messaging and other OMA functionality
  Emergency services and public warning
  Etc.
...UMTS became the dominant 3G technology, setting the foundations for a single worldwide 4G standard in future years
“
”
Radio-Electronics.com

## Slide 6: 3GPP Evolution
Radio Interfaces
  Higher Data Throughput
  Lower Latency
  More Spectrum Flexibility
  Improved CAPEX and OPEX
IP Core Network
  Support of non-3GPP Accesses
  Packet Only Support
  Improved Security
  Greater Device Diversity
Service Layer
  More IMS Applications (MBMS, PSS, mobile TV now IMS enabled)
  Greater session continuity
Through successive standards releases, 3GPP offers the wireless industry a coherent framework to serve the evolving needs of its customers while optimising the value of operators’ current network investments.
“
”
J-P Bienaime, UMTS Forum

## Slide 7: Building on Releases
Release 10 LTE-Advanced meeting the requirements set by ITU’s IMT-Advanced project.
Also includes quad-carrier operation for HSPA+.
Release 99: Enhancements to GSM data (EDGE). Majority of deployments today are based on Release 99. Provides support for GSM/EDGE/GPRS/WCDMA radio-access networks.
Release 4: Multimedia messaging support. First steps toward using IP transport in the core network.
Release 5: HSDPA. First phase of Internet Protocol Multimedia Subsystem (IMS). Full ability to use IP-based transport instead of just Asynchronous Transfer Mode (ATM) in the core network.
Release 6: HSUPA. Enhanced multimedia support through Multimedia Broadcast/Multicast Services (MBMS). Performance specifications for advanced receivers. Wireless Local Area Network (WLAN) integration option. IMS enhancements. Initial VoIP capability.
Release 7: Evolved EDGE. Specifies HSPA+, higher order modulation and MIMO. Performance enhancements, improved spectral efficiency, increased capacity, and better resistance to interference. Continuous Packet Connectivity (CPC) enables efficient “always-on” service and enhanced uplink UL VoIP capacity, as well as reductions in call set-up delay for Push-to-Talk Over Cellular (PoC). Radio enhancements to HSPA include 64 Quadrature Amplitude Modulation (QAM) in the downlink DL and 16 QAM in the uplink. Also includes optimization of MBMS capabilities through the multicast/broadcast, single-frequency network (MBSFN) function.
Release 8: HSPA Evolution, simultaneous use of MIMO and 64 QAM. Includes dual-carrier HSPA (DC-HSPA) wherein two WCDMA radio channels can be combined for a doubling of throughput performance. Specifies OFDMA-based 3GPP LTE.
Defines EPC.
Release 9: HSPA and LTE enhancements including HSPA dual-carrier operation in combination with MIMO, EPC enhancements, femtocell support, support for regulatory features such as emergency user-equipment positioning and Commercial Mobile Alert System (CMAS), and evolution of IMS architecture.
Text adapted from 3G Americas White Paper, September 2010

## Slide 8: Evolving EDGE
GERAN H(e)NB Enhancements (Release 9)
Voice services over Adaptive Multi-user channels on One Slot (VAMOS) (Release 9)
GERAN Improvements for Machine Type Communications
GERAN/E-UTRAN Inter-working
Multicarrier and Multi-RAT BTS
Local call local switch (Release 10 onwards)
Conformance Test development

## Slide 9: Evolving HSPA
Improved spectrum efficiency (modulation 16QAM, Reduced radio frame lengths
New functionalities within radio networks (incl.re-transmissions between NodeB and the Radio Network Controller)
Latency reduced (100ms for HSDPA and 50ms for HSUPA)
3GPP R5 & R7 added MIMO antenna and 16QAM (Uplink)/ 64QAM (Downlink) modulation

## Slide 10: 3GPP LTE Release 8
Broadband data throughput
  Downlink target 3-4 times greater than HSDPA Release 6
  Uplink target 2-3 times greater than HSUPA Release 6
Increased cell edge bit rates
  Downlink: 70% of the values at 5% of the Cumulative Distribution Function (CDF)
  Uplink: same values at 5% of the Cumulative Distribution Function (CDF)
Significantly reduced latency
High mobility
Significantly reduced CAPEX and OPEX
www.3gpp.org/releases
10

## Slide 11
Continuing femtocell integration
Added functionality, broadens LTE deployment scenarios
Feeding back results from first LTE deployments
Emergency user-equipment positioning and Commercial Mobile Alert System (CMAS)
Further evolution of IMS architecture.
Work on integrating non-LTE technologies
www.3gpp.org/releases
3GPP LTE Release 9

## Slide 12: LTE network commitments

## Slide 13: LTE-Advanced
LTE Release 8 can meet most requirements of IMT-Advanced.
  Two additional improvements to LTE performance needed:
Wider bandwidth
  To improve peak data rate and spectrum flexibility
  Spectrum/carrier aggregation based on component carrier(CC) concept to keep backward compatibility and allow smooth network migration
    Support of maximum 5 component carriers
    Each component carrier has a bandwidth defined in Release 8/9
    Intra-band contiguous(, intra-band non-contiguous) and inter-band non-contiguous aggregation
    RRC management of primary and secondary component carriers per UE
    Dynamic cross-carrier scheduling by MAC
  Specified under the work item, “Carrier aggregation for LTE”
Advanced MIMO techniques
  To improve peak data rate and cell/cell-edge spectrum efficiency
  Up to 8-layers for DL and 4-layers for UL
    Dynamic SU/MU-MIMO switching
    Support 4 spatial layers for MU-MIMO with maximum 2 layers per user
    Improved CSI feedback using double codebook structure
    Dedicated reference signal structure to support advanced precoding
    New codebook for 2Tx and 4Tx uplink MIMO
  Specified under the work items, “Enhanced Downlink Multiple Antenna Transmission for LTE” and “UL multiple antenna transmission for LTE”

## Slide 14: LTE-Advanced
Other improvements in LTE Release 10 are set to improve LTE performance even further:
Heterogeneous network
  To improve cell-edge user throughput, coverage and deployment flexibility
  Interference coordination for overlaid deployment of cells with different Tx power
  Sspecified under the work item, “Enhanced ICIC for non-CA based deployments of heterogeneous networks for LTE”
Relaying
  To improve coverage and cost effective deployment
  Type 1 relay node terminating up to layer 3, which can be seen Release 8 eNodeB from Release 8 LTE terminal
  To be specified under the work item, “ Relays for LTE”
Coordinated multipoint transmission and reception (CoMP)
  To improve cell-edge user throughput, coverage
  To be studied under the study item, “Coordinated Multi-Point Operation for LTE”
LTE Self Optimising Networks (SON) Enhancements
HNB and HeNB mobility enhancements

## Slide 15: LTE-Advanced Timeline LTE-Advanced is the 3GPP submission for the ITU’s IMT-Advanced system
Study Item, “LTE-Advanced” approved in 3GPP - Mar 2008 
LTE-Advanced Requirements (TR 36.913) - Jun 2008 
LTE-Advanced “Early Submission” made to ITU-R - Sep 2008 
“Complete Technology Submission” to ITU-R - Jun 2009 
“Final submission” to ITU-R - Oct 2009 
Evaluation Process “Final Decision” by ITU-R - Oct 2010 
Completion of LTE-Advanced specifications by 3GPP - Mar 2011

## Slide 16: Spectrum
Additional spectrum can be added to the specifications as required
(eg. 3500MHz currently being added)
16
Re-farming
900/1800MHz GSM bands are attracting a lot of attention, as “spectrum re-farming” in those bands is seen as one way to allow the roll out of mobile broadband services.
(See 3GPP TS 36.101)

## Slide 17: Machine Type Communications
Work started on this in Rel 10
14 MTC Features identified
  Low Mobility
  Time Controlled
  Time Tolerant
  Packet Switched (PS) Only
  Small Data Transmissions
  Mobile Originated Only
  Infrequent Mobile Terminated
In Rel 10, 3GPP will focus on the general functionality required to support these features
  Overload control (Radio Network Congestion use case, Signalling Network Congestion use case and Core Network Congestion use case)
  Addressing
  Identifiers
  Subscription control
  Security
  MTC Monitoring
  Priority Alarm Message (PAM)
  Secure Connection
  Location Specific Trigger
  Network Provided Destination for Uplink Data
  Infrequent Transmission
  Group Based MTC Features

## Slide 18: Convergence (Scale)
Machine-to-machine
Intelligent Transport Systems
Smart Grids
Smart Cards, eCommerce, USB, High Speed Interface
mHealth
RFID
Multi-Standard Radio (MSR-BS)
18

## Slide 19: Convergence (Technology)
19
2009 - CDMA Development Group (CDG) join 3GPP as a Market Representation Partner (MRP)
2009 - TD-SCDMA Forum pave the way for TD-LTE in China
2009 - Public Safety Agencies announce that LTE meets their requirements (See APCO, NENA, NPSTC Announcements)
2010 – 3GPP is working with Broadband Forum to support FMC using 3GPP EPC
3GPP LTE is a point of convergence, to unite the world’s operators on a common technology platform

## Slide 20: Conclusions
3GPP LTE is set to be the major enabler for mobile broadband
EDGE and HSPA remain hugely successful
Industrial input to the standards process is of an unprecedented level
The first commercial LTE Networks have been launched based on 3GPP Release 8 and R9
LTE-Advanced will enable new services & innovation beyond 3GPP Release 10
3GPP LTE is an evolution path which unites the GSM/UMTS, TD-LTE and CDMA families as well as the fixed/mobile communities
20

## Slide 21: Thank You
www.3gpp.org