## Slide 1
3GPP TSG RAN Meeting #110 RP-253180
Baltimore, USA, December 8-11, 2025
Requirements for 6G IoT
Agenda Item: | 8.2.1.4
Source: | Spreadtrum, UNISOC
Document for: | Discussion and decision

## Slide 2
Requirements for 6G IoT
5G IoT requirements
Proposal 1: Based on the experience from 5G and the scalable design for 6GR new IoT services, only one 6GR IoT device type is considered.
5G IoT techniques | Max. BW | Data rate | Coverage | Antenna | Use cases
NB-IoT | 200kHz | 25/60Kbps | 164dB MCL | 1T1R | Smog detector, door magnetism, gas meter, water meter, …
eMTC | 1.4MHz | 1Mbps | 164dB MCL | 1T1R | Industrial automation; smart building; metering; asset tracking; …
RedCap | 20MHz | 255Mbps | 140dB MCL | 1T1R 1T2R | Industrial wireless sensors; video surveillance; wearables; …
eRedCap | 20MHz | 10Mbps | 137dB MCL | 1T1R 1T2R | industrial wireless sensor network; video surveillance; wearables; smart grid; …
Consideration for 6G IoT
To avoid market fragmentation and achieve large scale benefit as well as considering IoT requirement with low cost/complexity, only one kind IoT device can be considered as a starting point.

## Slide 3
Requirements for 6G IoT
6G IoT requirements
Parameters | 6GR IoT device type
Smallest Maximum BW | 20MHz
Peak data rate | 40~200Mbps (can support smaller peak date rate by Scaling Factor)
Antenna/Layer | 1T1R/1L, 1T2R/1L
Duplex | TDD / FDD / HD-FDD
Coverage | 144dB MCL with 10 dB coverage extension
Simplified protocol stack | Compact protocol stack
Relax requirements | Processing time relaxation; RLM/BFD relaxation; DL and UL 64QAM (optional for 256 QAM);
Power class | PC3, PC5
Energy efficiency | eDRX, PSM, LP-WUS
Battery life | Rechargeable battery or [X] years
Proposal 2: Adopt above table as the starting point for 6GR IoT device type.
Notes: UL modulation order

## Slide 4
Requirements for 6G IoT
Text proposal for TR 38.914
Proposal 3: Adopt above text proposal for 6GR IoT.
5.4.3 Massive Communication (IoT)
The 6GR and 6G RAN architecture shall support the following minimum requirements for Massive Communication (IoT):
6G Massive Communication (IoT) shall be supported for FR1.
  6GR should have a common/scalable design that supports the above usage scenario in addition to eMBB
    Prioritize 6GR design for eMBB
  The above usage scenario should not overlap with Ambient IoT and NB-IoT
[PHY or MAC] peak data rate is [40~200] Mbps in DL and [40~200] Mbps in UL for lowest-tier device.
The minimum number of antenna/layer is 1T1R/1L.
The required UE bandwidth is 20MHz.
TDD, FDD, and HD-FDD operation are supported.
The modulation order can be up to 64QAM for DL and UL (optional for 256QAM).
The coverage is 144dB MCL with 10 dB coverage extension.
The power class is PC3 or PC5.
UE energy efficiency is supported, e.g., DRX, PSM, LP-WUS.

## Slide 5
WWW.UNISOC.COM