## Slide 1
3GPP TSG RAN Meeting #110 RP-253257
Baltimore, US, December 8-11, 2025
Agenda Item: 9.3.1.3
Source: vivo
Title: Discussion on Rel-20 AIML air interface inter-vendor collaboration and UE data collection
Document for: Discussion and Decision

## Slide 2
Background
In Rel-20 AIML air interface WID(RP-252445), there are following check points on inter-vendor collaboration and UE data collection
In this slide we discuss the related discussion in RAN1/RAN2/RAN4 and SA2/SA5 for situation check in RAN #110.

## Slide 3
Discussion in RAN4 for inter-vendor collaboration
DirC and DirA 3a-1
RAN4 started the work in Q4 and concluded the feasibility of standardization of DirC and DirA 3a-1, as stated in the following LS from RAN4(R4-2522434) to RAN:
Observation 1: RAN4 concludes the feasibility of Direction C and Direction A 3a-1 from model structure standardization perspective.

## Slide 4
Discussion in SA2/SA5 for inter-vendor collaboration
DirA 3a-1 and 4-1
In RANP #109, RAN sent LS to SA to conduct study on dataset and model parameter sharing for non-OTA scenarios.
Based on the request from RAN, SA2 and SA5 endorsed the SI objective for two-sided CSI compression in S2-2511314 and S5-255334.
Observation 2: SA is expected to start the study in SA2 and SA5 and to provide solution based on the study output.

## Slide 5
Discussion of UE data collection in SA2/SA5 and RAN2
During Rel-18&19, RAN2 studied candidate solutions for UE data collection to support UE-side model training.
Solution 2 (UE -> CN -> server) and solution 3 (UE->OAM->server) are selected as candidates for further down-selection, which include both CP- and UP-based approaches:
For the CP-based approach, RAN2 has already concluded that transfer of data over the CP can meet the RAN requirements for visibility and controllability, and has identified and captured some challenges of the CP solution in TR 38.843.
For the UP-based approach, RANP has requested SA2 to study UP-based Solution 2 and SA5 to study UP-based Solution 3 in LS RP-243316.
For UP-based Solution 2, SA2 has made significant progress:
SA2 sent an LS S2-2508119 to RAN2 to ask for further clarifications and guidance on aspects such as collection continuation and UE selection. In the reply LS R2-2507928, RAN2 indicated that some issues were not studied in RAN2 in Rel-19, and UE data collection will be further discussed as part of the 5G Advanced AI/ML for PHY in Rel-20.
As feedback to the request in RP-243316, SA2 has reached interim agreements with some remaining open issues on how to support the transfer of standardized data over UP as described in TR 23.700-04 v1.2.0, and would like to ask for RAN/RAN2 to provide feedback on whether Option 2 UP is selected in LS S2-2510958.
For UP-based Solution 3, SA5 has included the WT of UE data collection in SID S5-255334, but limited progress has been made.
Observation 3: For UP-based solution 2 (UE -> CN -> server) of UE data collection, SA2 has reached interim agreements with some remaining open issues.
Observation 4: RAN2 agreed to further study UE data collection as part of the 5G Advanced AI/ML for PHY in Rel-20.

## Slide 6
Proposal for next step
For two sided model cases, RAN4 and SA2/SA5 respond positively on the checkpoints. The checkpoint on inter-vendor collaboration for two sided model can be removed.
  RAN work related to SA2/SA5 can be conducted after SA finish study.
For UE data collection, RAN2 can collaborate with SA2 in the further study of UP-based Solution 2 and specify if deemed necessary.
  Besides, RAN2 may further consider solution 3 when SA5 provides feedback. RANP could further request SA5 to provide feedback and set up further checking point (e.g., June/2026) for final decision taking both SA2 and SA5 study into account.
Proposal 1: Remove checkpoints for inter-vendor collaboration for two-sided model. RAN WGs continue work correspondingly. Any additional update on the RAN work can be considered after SA finishes the study.
Proposal 2: Remove the checkpoint for UE data collection. RAN2 should collaborate with SA2 in the study of UP-based solution 2.
    RANP could further request SA5 to provide feedback and set up further checking point (e.g., June/2026) for final decision taking both SA2 and SA5 study into account.

## Slide 7
Summary
Observation 1: For two-sided model, RAN4 concludes the feasibility of Direction C and Direction A 3a-1 from model structure standardization perspective.
Observation 2: For two-sided model, SA is expected to start the study in SA2 and SA5 and to provide solution based on the study output.
Observation 3: For UP-based solution 2 (UE -> CN -> server) of UE data collection, SA2 has reached interim agreements with some remaining open issues.
Observation 4: RAN2 agreed to further study UE data collection as part of the 5G Advanced AI/ML for PHY in Rel-20.
Proposal 1: Remove checkpoints for inter-vendor collaboration for two-sided model. RAN WGs continue work correspondingly. Any additional update on the RAN work can be considered after SA finishes the study.
Proposal 2: Remove the checkpoint for UE data collection. RAN2 should collaborate with SA2 in the study of UP-based solution 2.
  RANP could further request SA5 to provide feedback and set up further checking point (e.g., June/2026) for final decision taking both SA2 and SA5 study into account.

## Slide 8
Proposed update for the WID