## Slide 1: Handling of test frequency tables for CA_n48B and CA_n77C.
Document for discussion and endorsement.
Agenda Item: 5.3.2.11
R5-255986
3GPP TSG-RAN5 Meeting #109
Dallas, Nov 17 – 22 2025

## Slide 2: Introduction
The purpose of this paper is to discuss and agree on that the existing tables for test frequencies for CA_n48B and for CA n77C is not complete as is, and to agree on the proposal to not add all possible BW combinations in the tables, since the tables would be too long/extensive.

## Slide 3: Observation 1
CA_n48B | CA_n48B | 5 | 15, 20 |  |  |  | 40 | 0
 |  | 10, 15, 20 | 10, 15, 20 |  |  |  |  | 
 |  | 15, 20 | 15, 20 |  |  |  |  | 
 | - | 10 | 50, 60, 80, 90 |  |  |  | 100 | 1
 |  | 15, 20 | 40, 50, 60, 80 |  |  |  |  | 
 |  | 40 | 40, 50, 60 |  |  |  |  | 
 | - | 10, 15, 20, 30, 40 | 10, 15, 20, 30, 40, 50, 60, 70, 80, 90 |  |  |  | 100 | 2
 | - | See n48 channel bandwidths in Table 5.3.5-1 for each carrier2 |  |  |  |  | 100 | 4 and 5
Table 5.5A.1-1, 38.101 above defines the supported BW combinations for CA_n48B. The two columns defining the BW combinations are not related to a specific CC. It means that the row defining BCS2 defines both 40 + 90 and 90 + 40 as possible combinations!
In test frequency tables for CA_n48B and CA_n77C the assumption, on how to interpret the table, was made that only 40 + 90 was defined as a possible combination.
The reason for the assumption is most likely due to that corresponding tables for E-UTRA CA configurations are containing the following text “Component carriers in order of increasing carrier frequency”, referring to the two columns defining BW combinations.

## Slide 4: Observation 2
It is defined, in 38.508-1 Annex C, C.2.4.3.4 for Intra band non contiguous CA, that if a test frequency table would include more that 35 BW combinations the number of added BW combination shall be reduced according to description.
For mentioned tables (4.3.1.1.3.48.1-1, 4.3.1.1.3.48.1-2, and 4.3.1.1.3.77.1-1) the number of BW combination would exceed 35 combinations.

## Slide 5: Proposals
Proposal 1:
Possible BW combinations for CA_n48B and CA_n77C includes also combinations where BW for CC1 is taken from second column and BW for CC2 is taken from first column.
Proposal 2:
The tables containing test frequencies for CA_n48B and CA_n77C, 4.3.1.1.3.48.1-1, 4.3.1.1.3.48.1-2, and 4.3.1.1.3.77.1-1, 38.508-1, will include the reduced number of BW combination according to 38.508-1, C.2.4.3.4.

## Slide 6: References
Related CRs RAN5 #109
R5-255989: Update of the description of reducing CA BW combinations in tables
R5-255990: Update of frequencies for CA_n48B.
R5-255991: Update of frequencies for CA_n77C.