## Slide 1
3GPP TSG RAN5#109 R5-256550
Dallas, USA, Nov 17-21, 2025
Agenda item: 4.2.3
Source: Qualcomm Inc
Title: AIML status update
Document for: Information

## Slide 2
RAN4 AIML status update – CSI prediction and CSI Compression
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items
CSI prediction | N/A | N/A | TDL channel model to be considered for Rel19 tests RAN4’s legacy framework of throughput ratio w.r.t Rel15 Type I codebook to be reused to verify AIML based predicted PMI Channel condition will not change during the middle of the test Core requirements for performance monitoring defined. | All the current agreements need to go into TS 38.101-4. Pending discussion on test config details for FDD and TDD Details (metric, delay and accuracy) of performance monitoring requirements
CSI compression | Study Item phase | Study Item phase | Study Item phase Evaluated the feasibility of fully specified decoder and partially specified decoder Agreed parameters that need to be specified in the spec for fully and partially specified decoder | Study Item phase Design structure and parameters of encoder-decoder for direction C and direction A, sub-direction 3a-1 of RAN1 Design performance tests for fully specified test decoder

## Slide 3
RAN4 AIML status update – Beam Management
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items
BM – Spatio-Temporal prediction | Study Item Phase RAN4 agreed that the ground truth for the predicted RSRP is the ideal measurement of RSRP on the predicted Tx beam | Study Item Phase Selection of beam prediction metrics Decision of whether UE knows Rx beam of predicted Tx beam Evaluation period of spatio-temporal beam prediction | Agreed L1-RSRP accuracy and beam prediction accuracy to be the performance metrics Introduced UE capability that allows UE to indicate whether it knows Rx beam of predicted Tx beam Use CDL-based channel model as starting point MultiAoA based Enh IFF with 4 probes to be used as baseline | Evaluation period of spatio-temporal beam prediction. Testing methodology of spatio-temporal beam prediction Spatial channel model details pending further analysis
BM – Spatial beam prediction | Study Item Phase Same as above | Study Item Phase Selection of beam prediction metrics Decision of whether UE knows Rx beam of predicted Tx beam Evaluation period of spatial only beam prediction | Agreed L1-RSRP accuracy and beam prediction accuracy to be the performance metrics Defined some details of L1-RSRP accuracy and beam prediction accuracy metrics. Abs L1-RSRP accuracy metric applies to all inferred beams Rel L1-RSRP accuracy req applies to all inferred beams Reuse evaluation period of legacy beam management as the eval period of reference resources in AIML based beam prediction Introduced UE capability that allows UE to indicate whether it knows Rx beam of predicted Tx beam Use CDL-based channel model as starting point MultiAoA setup (Enh IFF with 4 probes) as baseline Definition of TCI state switch in AIML BM | Inference time of spatial beam prediction. How to define performance tests

## Slide 4
RAN4 AIML status update - Mobility
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items | Rel20 WI
Mobility | N/A | N/A | Study Item Phase Ground truth definition of L3-RSRP prediction Absolute L3 predicted RSRP Definition of Relative L3-RSRP accuracy | Study Item Phase Ground truth definition of event prediction Overall test method for FR1 (FR2 is de-prioritized) | RAN4 discussions start in Oct 2025 meeting RAN2 discussions start in Nov 2025

## Slide 5
RAN4 AIML status update – Positional Accuracy
AIML usecase | Rel18 agreements | Rel18 pending items | Rel19 agreements | Rel19 pending items
Positioning Accuracy | Study Item Phase RAN4 scoped the five cases that RAN4 plenary considered for AIML based positioning | Study Item Phase Selection and details of the cases for which RAN4 requirements will be defined | RAN4 decided not to define requirement for case 2a and case 2b [out of Rel19 scope as per RAN plenary] RAN4 agreed to define reporting delay requirement for case 1. Measurement delay framework of legacy NR positioning would be used as baseline. | Inference timeline and number of measurement samples for case 1 Whether and how to define tests for case 3a and 3b

## Slide 6
Summary of Key features with Direct Impact to Signaling Work Plan, expected completion is RP#110 (Dec’25) with relevant CRs in normative spec TS 38.331, TS 38.300
LCM for UE-sided Model (Beam Management and CSI Prediction)
    AI\ML enabled Features/FGs and functionalities
    Inference Configuration and Applicability Reporting Procedures
    UE Cap definition
    Existing procedures and terminologies from the CSI framework should be used.
LCM for NW-sided Model
    Network Side additional condition left to NW implementation
    gNB is responsible for monitoring its own performance
    UE will not be informed about any gNB/LMF-sided model/functionality management decision
    UE will not be involved in any gNB/LMF-sided model/functionality management decision making except being configured to provide the required measurement/data.
Data Collection for UE Side Model
  Measurement Configuration(s) and Associate ID (s)
  Triggers for data collection; Activation/Deactivation
Data Collection for NW Side Model
  Configuration Details for Data Collection. Measurement resources and contents of Data Collection Report
  Reporting Procedures (new SRB), Handling power and UE memory issues
  Mobility Handling
RAN2 AIML status update

## Slide 7: Summary
Observation1: RAN4 still have not included requirements for any of the AIML scenarios in the core spec.
Observation2: RAN4 expected to add core part for CSI prediction use case in Nov 2025. Performance requirements addition expected to be completed by June 2026
Observation3: RAN4 expected to add core part for Beam prediction in Nov 2025. Performance requirements addition timeframe is TBD. May even spillover to Rel20
Observation4: RAN4 expected to add reporting delay requirements (no positioning accuracy requirements) in TS 38.133 for the Positioning usecase in Nov 2025. Performance requirements expected to be completed by March 2026
Proposal1: With the RAN2 core work comprising LCM (lifecycle management) and Data Collection procedures to support the 3 RAN4 use cases now completed, it is the right time to introduce the RAN5 WI.