## Slide 1: Disc on handling XR PDCP discard TCs
CMCC
3GPP TSG-RAN5 Meeting #109
Dallas, USA, 17th Nov 2025 - 21st Nov 2025 R5-256071r1

## Slide 2
XR PDCP discard TCs need to define RTP header extension
For XR PDCP discard TCs, PDU Set marking information is in RTP header extension (application layer packet) as per TS26.522, e.g. PDU Set Importance (PSI), PDU Set Sequence Number (PSSN) and PDU Sequence Number within a PDU Set (PSN).
Observation 1: an RTP packet within header extension needs to be constructed for XR PDCP discard TCs.
TS 26.522 j20

## Slide 3
A test loop mode for application layer packet is needed
Observation 2: The existing test loop modes specified in TS 38.509 are for DRB, QoS flow, MBS RB and Sidelink are not suitbale for application-layer RTP packets loopback test.
Proposal 1: It is proposed to introduce a new test loop mode for application-layer packets (e.g. RTP ) and to agree the related TS 38.509 CR R5-256079 (CR number 0090) and also the TS 36.509 CR.
TS 38.509 h50

## Slide 4
XR DL/UL awareness for PDU Set information
As per the description in TS 38.300 cl16.15.2, it is clearly said that XR UL awareness depends on UE implementation. The test purpose of PDCP discard TCs is to test whether UE sends the received application layer packet back to SS by using new defined test loop mode. Thus, SS only needs to 1)send the RTP packet and map it to a PDCP PDU through layer by layer encapsulation; 2) set up some XR PDCP discared related configurations and timers. Thus, no need to implement XR DL awareness in SS. E.g. How the RTP packet is mapped to GTP-U header (in core network) and GTP-U header mapped to PDCP PDU (in gNB).
Proposal 2: PDCP discard TCs are only related to XR UL awareness rather than DL awareness. SS needs to construct an RTP packet within header extension and map it to a PDCP PDU for test. Besides, SS also needs to set up some related configurations and timers case by case.
TS 38.300 j00

## Slide 5
How to map an RTP packet to a PDCP PDU
The picture on the left shows how to map an RTP packet to a PDCP PDU. Through this procedure involves many NAS layers but with no changes to them. The only affected layer is application layer with RTP header and header extension changed. Thus, there is no need to define specific UDP header, IP header and SDAP header. The default configuraiton of these layers headers from SS can be reused.
For the RTP header, the only affected field is X which indicates whether there is an RTP header extension. This field needs to be set to 1. For the other fields in RTP header, the default configuration can be used as well.
Proposal 3: It is proposed to define specific configurations for UDP header, IP header.
Proposal 4: RTP header is also needed to be defined with specific configurations.
RTP packet mapped to PDCP PDU

## Slide 6
Define RTP header extension for PDCP discard TCs
There are two kinds of RTP header extension: one-byte format and two-byute format. As the description in cl 4.2.1 of TS 26.522, if we only use RTP header extension for PDU Set Marking, then one-byte format is preferred since more simpler. As for the semantic of each field will be explained and specified in every TCs since the values may be different case by case.
Proposal 5: It is proposed to use one-byte RTP header extension for PDU Set Marking in XR PDCP discard TCs.
Proposal 6: It is proposed to construct number of “X” RTP packets with header extension and within number of “X” consecutive PSSN for PDCP discard TCs. Number of “X” RTP packets will be mapped to number of “X” PDCP PDU packets with number of “X” consecutive PDCP SN. The value of “X” could be specified case by case.
TS 26.522 j20
TS 26.522 j20

## Slide 7
PDU Set/PSI based discard
PDU Set based discard flow chart
R5-25xxxx
R5-25xxxx
PSI based discard flow chart

## Slide 8
PSI based discard and DSR triggering
Proposal 7: It is proposed to endorse the test procedures in Slide 6 and 7 as test procedures of PDCP discard TCs and also to agree TS 38.523-1 TC CRs R5-256073, R5-256074 and R5-256075.
R5-25xxxx
PSI based discard and
DSR triggering flow chart

## Slide 9: Thank you !