## Slide 1
Requirements for Computing Service in 6G
-an operator’s perspective
Source: AT&T
S2-2508649- SA WG2#171, Wuhan, China, October 13 – 17, 2025
© 3GPP 2025

## Slide 2: Background
The Rel-20 6G SID WT#6 scope and KI proposals are getting stable but cover a wide range
It is unclear however if the existing work task description captures the use cases from an operator’s perspective
  This deck presents scenarios of interest to AT&T that enable compute service in 6G (6G SID WT#6) in an effort to ensure they will get addressed as part of the study.

## Slide 3: Offload of UE Compute to Operator Cloud
This is the key use case for AT&T where UE compute is offloaded to the operator’s cloud
UE already has a relationship with the home operator, so this use case is much easier to deploy in an operator network
The UE may decide to move an application module into MNO’s cloud due to battery limit, processing power, user experience degradation, etc. and request for it
Application logic allows for work split across the UE, MNO’s cloud and the AS (that may reside in service provider’s edge/cloud)
Work split between the UE and the network operators’ cloud can be controlled by the UE
The MNO’s cloud may be pre-populated with standard versions of the application or download them in real time, e.g., LLM, XR rendering

## Slide 4: AF Compute Offload
This use case is of less interest to AT&T
In certain region of the world, the network operators’ cloud and the service providers’ cloud are separately owned and managed. The AF component therefore may or may not reside in operator’s cloud
Enabling this use case would require individual service providers to have business relationships with network operator for the offload and therefore harder to deploy

## Slide 5: Relationship of 6G Compute Service with 5G Edge Compute
AT&T considers Compute as a service to be different from edge computing
5G Edge Computing uses DNS-based approach for service discovery which carries limited information
5G Edge Computing in general tries to select UPF closer to the edge location whereas in this case, other factors such as availability of compute resources and latency to that location needs to be considered. The discovery process for these compute resources however would still be needed.