## Slide 1: Discussion on IP vs. Non-IP v2
ZTE, CMCC, MediaTek Inc.
(RoHC) (reduced RTP)
3GPP TSG SA WG2#172
17- 21 November, 2025, Dallas, US
S2-2510377

## Slide 2: IP with RoHC for voice
In SA2#170, SA2 raised several questions in LS(S2-2507636) to RAN1 and RAN2 to clarify whether RoHC is a potential factor that deteriorates the call interruption issue. The responses are as follows:
  Question 1 (To RAN2): Does RAN2 have any observation on how many consecutive packets lost or erroneously decompressed will trigger the RoHC state fall back at the compressor when using RoHC?
  RAN2 reply to Question 1: RAN2 is not able to make any observation on how many consecutive packets lost or erroneously decompressed will trigger the RoHC state fall back at the compressor when using RoHC, and thinks the implementation of ROHC functions (e.g., compression and decompression) falls outside of RAN2 scope.
  Question 2 (To RAN1): Can RAN1 provide any data regarding the probability that such number of consecutive packets e.g. 16 or 64 can be lost or erroneously decompressed? How often such event can occur?
  RAN1 reply: Assuming line-of-sight condition for the duration of the call, no change in large scale parameters (e.g. fixed shadowing), and using an NTN TDL-C channel model (which is a channel model previously used by RAN1 and SA4 evaluations), the probability of having 16 or 64 packets consecutively lost is negligible under typical operating conditions (e.g. up to 10% packet error rate)
  For the case of line-of-sight not being guaranteed for the duration of the call, an intermittent blockage (e.g. according to the land mobile satellite channel model in TR 38.811) may still occur in practice, in which case the probability of having 16 or 64 packets consecutively lost may not be negligible. RAN1 has not reached consensus on whether to consider this case.
  Question 3 (To RAN2): Can RAN2 confirm whether scheduling methods for support of IMS voice over NB-IoT NTN can handle the voice packets of different sizes changing dynamically?
  RAN2 reply to Question 3: Scheduling methods may handle the voice packets of different sizes (e.g., via semi-persistent scheduling and dynamic scheduling, including over-provisioning of resources in UL), but RAN2 will further study and discuss the details of the scheduling mechanism to avoid the potential issues.
Observation 1: Neither RAN1 nor RAN2 identify critical RoHC issues:
  Observation1.1: Assuming line‑of‑sight condition throughout the call, the probability of 16 or 64 consecutive packet losses is negligible; therefore, RoHC state fallback is unlikely to occur.
  Observation1.2: Scheduling method can support dynamically changing voice packet sizes, and the potential issues will be further studied and avoided by RAN.
LS replied from RAN

## Slide 3: IP with RoHC for voice
Based on S2‑2504678 (QC), S2‑2507102 (ZTE), S2‑2509144 (QC), and LS replies from RAN1/RAN2, the updated clarifications on RoHC issues are summarized as follows:
issue2-call interruptions:
  RAN1/RAN2 indicate the probability of RoHC state fallback due to packet loss is negligible→Call interruptions caused by RoHC fallback should not be considered.
issue3-over/under scheduling：Earlier concern: packet size difference (voice vs. SID) could waste resources, and that UOR2-EXT3 (10–12B) should be used to explicitly indicate TIME_STRIDE and prevent timing loss. However,
  For voice over GEO scenarios, the ptime of voice and SID packets is often identical or a multiple times of each other per SA4. Therefore, UO‑1 (2B) with TS_SCALED_LSB is sufficient to reconstruct the RTP timestamp.
  Timing loss (especially codec-related timing) should be considered as an issue caused by implementation, rather than the drawback of RoHC protocol.
  Based on RAN2’s feedback, further study can mitigate residual resource waste.
  Issue4-ROHC overhead bit rate: It was previously proposed that about 6–50% of packets are UOR2-EXT3, and the corresponding overhead data rate is shown in column 2. Based on the analysis in below table, if UO‑1 is used and the UDP checksum is disabled, the average RoHC overhead is only ≈ 120 bps under typical conditions. If Non-IP wants to achieve comparable performance, the Reduced RTP header would need to be limited to about 1.2B(120 bits / 12.5 pkts / 8 bits).
Observation2: RoHC issues are either un-likely to happen, or implementation‑specific and can be resolved through proper implementation.
Updated Clarification on RoHC Issues
Percentage of FO packets(UOR2-EXT3 or UO-1) | RoHC overhead data rate(bps) |  | 
 | UOR2-EXT3 Nums in S2‑2509144 (QC) | UOR2-EXT3+UDP checksum disabled (reduces each packet by 2B) | UO1+UDP checksum disabled (UO1 packet size = 2B)
5% | 400 | 200 | 110
10% (most typical situation) | 445 | 245 | 120
20% | 540 | 340 | 140
50% | 825 | 625 | 200
corner case due to implementation issue, shouldn’t be considered in standard discussion
Notes:   For voice over GEO scenarios, the ptime values of voice and SID packets are often multiples of each other—or even identical—and according to SA4, their packet sizes can also be similar. Hence, it is feasible to use the TS_SCALED_LSB field in the UO-1 (2 bytes) packet to reconstruct the actual RTP timestamp.
  Regarding timing loss (especially codec-related timing), it should be considered an implementation-specific issue rather than a general protocol limitation.
  Even if packet sizes differ, based on RAN2’s feedback, such issues can be mitigated through further study—for example, by transmitting other data when residual resources are available.

## Slide 4
[Constraint 1] Non-IP Delimma: More Non-IP features, more header overhead; Less Non-IP header overhead, less features supported.
  According to S2‑2507102, the reduced RTP header size grows as the supported features grow. To match the performance of a typical case with 10% UO1 packets (RoHC overhead data rate≈ 120 bps), the non‑IP header would need to be limited under only 1.2Bytes.
  However, features such as DTMF and multi‑call (dependent on SA1/SA4) would require a header of at least 6 bytes, thereby make it not as attractive as IP(RoHC).
    DTMF is a fundamental interactive mechanism in voice communication, allowing users to send control signals through keypad inputs during a call. Emergency calls, customer service voice menus (IVR), and banking voice services all rely on DTMF for command input.
    Multi‑call enables users to manage multiple voice calls on the same terminal simultaneously—such as call holding, or merging calls into a three‑party conference—making it a key function for enhancing user experience.
    Security is a critical consideration in voice over GEO, as such services may involve both military and civilian scenarios.
  Observation3: If Reduced RTP wants to achieve average performance of RoHC, the limited 1.2Bytes header provides only a limited feature set compared with the IP with RoHC.
Non-IP (reduced RTP) for voice
Technical constraints
Functionality wanted to be supported by non-IP (reduced RTP) | In order delivery | DTMF | MULTI-CALL/FEC | JBM | security | …
Cost | 1 octet (SN) | 1 octet (PayloadType) | 4 octets (SSRC) | 4 octets (TimeStamp) | Can’t support | 
Total Overhead | 1 octet | 1 + 1 == 2 octets | 2 + 4 == 6 octets | 6 + 4 == 10 octets | FFS | 

## Slide 5
[Constraint 2 ] RTCP Disabled: Loss of QoS and Congestion Control
  As specified in TS26.114, The RTP implementation shall include an RTCP implementation.
  For reduced RTP, essential fields such as SSRC are removed, meaning RTCP cannot associate SR/RR (Sender Report / Receiver Report) feedback with the correct media source.
  Without RTCP, the system cannot monitor round‑trip delay to estimate MOS dynamically, and loses its ability to perform congestion control based on QoS feedback, which may lead to performance degradation.
  [ Constraint 3 ] SRTP Incompatibility: Loss of Security
  As specified in TS33.328, The support for IMS media confidentiality protection is mandatory in an IMS UE supporting media plane security and mandatory in IMS core network elements (i.e., IMS Access Gateway) supporting e2ae IMS media plane security. The integrity and confidentiality protection for IMS traffic using RTP shall be achieved by using the Secure Real-Time Transport Protocol (SRTP), RFC 3711 [9].
  SRTP depends on critical RTP header fields—such as SSRC, SN—to generate keystream for encryption protection.
  In reduced RTP, an extensive SA3 workload would be required to achieve same security level the SRTP provides for IP.
Non-IP (reduced RTP) for voice
Technical constraints
Observation4: Without key RTP components such as the SSRC, timestamp, and the companion RTCP and SRTP protocols, reduced RTP loses end‑to‑end QoS feedback and congestion control, cannot establish the security context required by SRTP. As a result, it provides lower reliability, weaker security, and poorer interoperability compared with IP with RoHC.

## Slide 6
Given that IMS is an IP-based architecture, and satellite-access UE may need to communicate with legacy UE, the PGW or other network functions are required to reconstruct the reduced RTP headers into complete IP/UDP/RTP headers before forwarding them to IMS components.
According to the architectural assumption for IMS voice over GEO, “Enhancements to NB-IoT (GEO), EPC and IMS for supporting voice call via GEO shall be minimized.”
However, several aspects of this mechanism—which could have significant implications for the overall system—remain insufficiently analyzed and evaluated. These include, but are not limited to, the following concerns:
  concern1: UE may need to remove or insert specific fields in the IP, UDP, and RTP headers, which could require modifications to the modem/application.
  concern2: P-GW may need to remove or insert specific fields in the IP, UDP, and RTP headers, which could require modifications to the user plane processing module/protocol stack.
  concern3: P-CSCF may need to provide extra header information to P-GW, which could result in increased signaling load or necessitate interface enhancements.
  concern4: Without transmitting the RTP timestamp, it is not possible to accurately reconstruct it on the receiver side, which may affect media synchronization and playback quality.
  There may be additional aspects that have not yet been identified or listed.
Observation5: The feasibility and potential impact of sending non-IP voice packets require thorough evaluation and alignment among relevant working groups, given that it is considerably more complex than the IP-based solution.
Non-IP (reduced RTP) for voice
Concerns in Reconstructing Full IP/UDP/RTP Packet
(For information. Extracted from S2‑2507102)

## Slide 7: Conclusion and proposal
Compared to Non-IP(Reduced RTP), The IP (RoHC) approach :
  can achieve comparable or lower overhead
  is significantly more future-proof(can natively support DTMF, MULTI-CALL/FEC, JBM, etc.)
  has fewer dependencies on SA1, and no additional work for SA3 (Security work), and SA4 (Reduced RTP work)
  requires much fewer enhancements to existing system
  leverages the widely commercial deployed VoLTE design to the maximum
  provides higher reliability, stronger security, and better interoperability
  RoHC issues are either un-likely to happen or implementation‑specific and can be resolved through proper implementation.
Conclusion
Proposal
For IMS voice, it is proposed to tentatively reach consensus on selecting IP (with RoHC) at SA2#172.