## Slide 1
Discussion on GEO voice KI#2 next step
3GPP TSG-SA WG2 Meeting #172 S2-2510395
17 - 21 November, 2025, Dallas, USA
vivo, MediaTek Inc., Spreadtrum

## Slide 2
Contents
IMS Signaling over UP vs CP
IMS Signaling over IP vs non-IP
Proposals

## Slide 3
IMS Signaling* over UP vs CP
In SA2#171 meeting, the interim conclusion has been agreed as following (see S2-2509293):
The following interim conclusions for Key Issue #1 support of IMS voice call over NB-IoT via GEO satellite connecting to EPC are made:
- The voice packets shall be transported over the NB-IoT (GEO) user plane, i.e. using DRB and S1-U.
*: the IMS signaling can be text based signaling or binary based signaling
It is unclear how to transfer the IMS signaling: UP vs CP
  Option 1：IMS Signaling over UP
  1 DRB is used for IMS signaling
  1 DRB is used for IMS voice data
  Considering there are 2 DRBs limitation on NB-IoT, the following question should be considered:
  Question 1: Whether the number of DRBs are enough to support both IMS service and internet service?
  Option 2：IMS Signaling over CP
  1 SRB is used for IMS signaling,
  1 DRB is used for IMS voice data
  In Option 2, both CP and UP will be used to transfer IMS signaling and data respectively, the following question should be considered:
  Question 2: Whether the CP and UP can be used simultaneously？
  Considering CP uses NAS to transfer IMS signaling, the following question should be considered:
  Question 3: For CP, whether the NAS header can be reduced to small enough?

## Slide 4
IMS Signaling* over UP vs CP
Question 1: Whether the number of DRBs are enough to support both IMS service and internet service?
Answer: Based on the LS reply from RAN2 (R2-2507784), the question 1 can be resolved.
RAN2:
Question 6 (To RAN2): Is it feasible to support more than 2 DRBs for a UE accessing NB-IoT in Rel-20?
RAN2 reply to Question 6: RAN2 understands that it is technically feasible to support more than 2 DRBs for a UE accessing NB-IoT in Rel-20.
Question 2: Whether the CP and UP can be used simultaneously?
Answer: Based on the limitation given in TS 23.401 , the question 2 cannot be resolved.
TS 23.401
4.10 Introduction of CIoT EPS Optimisations
The MME shall consistently include Control Plane Only Indicator either in all SGi PDN connections of a UE or in none of them. All the SGi PDN connections of a UE shall either use S11-U or S1-U at any point in time.
Proposal 1：The IMS Signaling shall be transported over User Plane (UP)
Observation 2: Considering that it was already decided for KI#1 to use UP for the EPS bearer that will be used to transport voice packets, for IMS PDN connection the UE CANNOT use CP and UP simultaneously.
*: the IMS signaling can be text based signaling or binary based signaling
Observation 1: Based on the reply form RAN2, DRBs are enough for a UE to support both IMS PDN (EPS bearers for IMS Signaling and data) and internet PDN connection.
SA3
Question 7 (To SA3): Considering that in the context of alternative solutions documented in TR 23.700-19 for the support of IMS voice over NB-IoT NTN connected to EPC, a specific SRB (i.e. via a dedicated EPS bearer for Data over NAS) will be used for transfer of voice media packets only, is there a concern to eliminate the 5 bytes of NAS layer security overhead?
Answer: The majority of companies in SA3 were not in favour of allowing non-integrity protected voice packets to be sent over NAS to the MME. Hence there was no consensus in SA3 to eliminate the 5 bytes of NAS layer security overhead.
Observation 3: Based on the reply form SA3, the NAS header CANNOT be reduced to small enough.
Question 3: For CP, whether the NAS header can be reduced to small enough?
Answer: Based on the LS reply from SA3 (S3-253797), the question 3 CANNOT be resolved.

## Slide 5
IMS Signaling* over IP vs non-IP
*: the IMS signaling can be text based signaling or binary based signaling
Proposal 2：The IMS Signaling shall be transported over IP
Observation 4: There is no end-to-end security mechanism for IMS signaling transported over Non-IP which lowered the security level comparing to the end-to-end security as each hop nodes (e.g. eNB, S/P-GW) can see IMS signaling body.
Options | Security mechanism | Technical impacts
IP based |  | No impact, using the existing end-to-end security mechanism between the UE and the IMS network (i.e. IPSec).
Non-IP based |  | No end-to-end security: IMS signaling security relies on hop-by-hop security: AN security between UE and eNodeB; Network Domain Security (NDS) between eNodeB and S/P-GW; SGi security between P-GW and IMS network (e.g. P-CSCF) AN security: currently only support ciphering while integrity protection has not supported for NB-IoT. NDS: IPSec/TLS supported. SGi security: by default there is no security mechanism, reply on upper layer security mechanism, e.g. IPSec.
End to end security
Hop by hop security
UE
RAN
EPC
IMS network
IPSEC tunnel
UE
RAN
EPC
IMS network
AN security
NDS
SGi security
For IMS signalling, the security protection mechanism is mandatory. In below table, all security mechanisms are applied to UP.

## Slide 6
Proposals
  vivo’s initial proposals:
Proposal 1: The IMS Signaling shall be transported over User Plane (UP)
Proposal 2: The IMS Signaling shall be transported over IP