## Slide 1
Discussion on GEO voice KI#1 next step
3GPP TSG-SA WG2 Meeting #172 S2-2509915
17 - 21 November, 2025, Dallas, USA
vivo, Spreadtrum

## Slide 2
Contents
IMS voice data over IP vs non-IP
Proposals

## Slide 3
IMS voice data over IP vs non-IP: Technical evaluation
 | Option 1: Voice data is transported via UP IP UE, RAN supports DRB for voice UE and RAN supports ROHC
 | Option 2: Voice data is transported via UP non-IP UE, RAN supports DRB for voice UE and NF (e.g. P-GW) supports non-IP/IP conversion UE and NF (e.g. P-GW or AGW) supports red-RTP/full RTP conversion
UP non-IP
UP IP
Observation 1: In the high possibility cases, UP IP and UP non-IP has almost the same level of protocol overhead (UP IP: 1-3B, UP non-IP: 2B) when using ROHC in fully compressed state
Observation 2: UP IP has less UE and network impacts while the key challenge is performance of ROHC stability; UP non-IP has bigger UE and network impacts while there are no performance stability risks; Both UP IP and non-IP have the same RAN impacts.
Options | Protocol overhead |  |  | Key network impacts | Key challenges
 | Original | ROHC | RTP reduction | Protocol conversion | 
Option 1: UP IP | 40B (RTP/UDP /IP=12/8/20) | Yes Variable Header Sized: 1-3B: SO 8B: FO UOR-2EXT-3 >15B/40B: IR-DYN/IR | N/A | N/A | Yes ROHC header variation issues (e.g. ROHC configuration) may cause the whole protocol performance not so stable
Option 2: UP Non-IP | 12B (RTP=12) | N/A | Yes R20: (up to SA2/SA4): 1B: 1-SN only 2B: PT + 1-SN 6B: PT+1-SN+TS | Yes NF (e.g. PGW/AGW) performs protocol conversion between Red-RTP and full RTP for UL/DL voice NF (e.g. PGW) performs protocol conversion between non-IP/IP for UL/DL voice | N/A

## Slide 4
IMS voice data over IP vs non-IP: ROHC stability
As per Observation 2, the key challenge for IP based solution is ROHC stability. SA2 has sent related questions to RAN1/RAN2 in LS S2-2507636.
Question 2 (To RAN1): Can RAN1 provide any data regarding the probability that such number of consecutive packets e.g. 16 or 64 can be lost or erroneously decompressed? How often such event can occur?
RAN1 reply:
Assuming line-of-sight condition for the duration of the call, no change in large scale parameters (e.g. fixed shadowing), and using an NTN TDL-C channel model (which is a channel model previously used by RAN1 and SA4 evaluations), the probability of having 16 or 64 packets consecutively lost is negligible under typical operating conditions (e.g. up to 10% packet error rate)
For the case of line-of-sight not being guaranteed for the duration of the call, an intermittent blockage (e.g. according to the land mobile satellite channel model in TR 38.811) may still occur in practice, in which case the probability of having 16 or 64 packets consecutively lost may not be negligible. RAN1 has not reached consensus on whether to consider this case.
Observation 3: LS response from RAN1 indicated that ROHC performance stability can be considered guaranteed for LOS scenarios. However for NLOS scenarios, ROHC performance stability cannot be guaranteed.
RAN1 LS (R1-2508096) reply:
RAN2 LS (R2-2507784) reply:
Question 1 (To RAN2): Does RAN2 have any observation on how many consecutive packets lost or erroneously decompressed will trigger the RoHC state fall back at the compressor when using RoHC?
RAN2 reply to Question 1: RAN2 is not able to make any observation on how many consecutive packets lost or erroneously decompressed will trigger the RoHC state fall back at the compressor when using RoHC, and thinks the implementation of ROHC functions (e.g., compression and decompression) falls outside of RAN2 scope.
Observation 4: The configuration & implementation of ROHC functions are out of RAN2 scope as well as SA2 scope. 3GPP has no control of ROHC based solutions during the commercial deployment.

## Slide 5
IMS voice data over IP vs non-IP: Standard impacts evaluation
No. | Standard impact |  | IP option | Non-IP option
1 | Capability negotiation | Whether supports GEO voice | ✔ Negotiation during attach | ✔ same as IP option
2 |  | Whether supports IP/non IP conversion | ✘ N/A | ✔ UE negotiates with PGW or MME during attach
3 | Dedicated EPS bearer for voice | Support dedicated EPS bearer | ✔remove specification restriction on NB-IoT | ✔ same as IP option
4 |  | New QoS parameter | ✔define a new QoS class for GEO voice | ✔ same as IP option
5 |  | Extend the number of DRBs | ✔remove specification restriction on NB-IoT | ✔ same as IP option
6 |  | (optional) Pre-establish dedicated EPS bearer | ✔established during attach or PDN connection setup | ✔ same as IP option
7 | Voice data transfer | IP/UDP/RTP protocol overhead reduction | ✘No new impact, re-use ROHC | ✔ UE and NF (e.g. P-GW) perform non-IP/IP conversion ✔ UE and NF (e.g. P-GW or AGW) perform red-RTP/full RTP conversion
✔ has standard impact
✘ no standard impact
Observation 5: Non-IP option has standard impacts related to protocol conversion.

## Slide 6
Proposals
  vivo’s initial proposal:
Proposal: For IMS voice data transfer, conclusions for both IP and non-IP solutions should be captured in TR for the normative work.