## Slide 1: Discussion on Signalling transport for GEO voice service
China Telecom, NTT DOCOMO, CSCN

## Slide 2: Signalling transport options in TR 23.700-19
Solution Category：
Cat 1. via CP
  Solution 5, 6, 7, 8, 10, 29
Cat 2. via UP
  Solution 1, 2, 3, 4, 28
Cat 3. SIP Invite via CP，rest messages via UP
  Solution 9
NOTE：Since conclusion of voice packet via UP is made, voice packet via CP in some solutions in Cat 1 need no discussion in this paper

## Slide 3: Key aspects for comparison
ECST
Security for GEO access
Other IMS services, e.g. SMS
Assumption
There is no different between CP and UP for transportation of Text-based or Binary-based signalling
There is no different between CP and UP for transportation of IP or non-IP signalling

## Slide 4: Estimated Call Setup Time(1)
UE in ECM-CONNECTED
  CP by default has higher priority than UP
    In 23700-19, NOTE 1 in architectural assumptions: Solutions should take into account that CP CIoT EPS optimization data in current pre Rel-20 NB-IoT is regarded as NAS signalling and by default has higher priority than UP data.
    NB-IoT GEO access can be used not only for voice but also for low-speed data service, e.g. IoT data. If congestion happens, to ensure signalling priority CP can use existing featues of Inter-UE QoS for CP Optimisation(in 4.7.8 of TS 23.401)
      To achieve same priority as CP, UP needs new feature in RAN, e.g. supporting handing of QCI with high priority.
Observation 1: For UE in ECM-CONNECTED, transportation Signalling via CP is prior over UP hence less ECST, although reduced ECST value can not be quantified.

## Slide 5: Estimated Call Setup Time(2)
UE in ECM-CONNECTED
  CP has more overhead than UP due to NAS head, therefor CP causes more ECST in theory
    In R19(NORDAT_CP), NAS has 3 Bytes overhead; In pre-R19, NAS has 7 Bytes overhead
    Assuming using Text-based option and =2kbps, CP needs more than UP is listed below. CP extra = /×number of messages
      Since KI#2 is not concluded, how many signalling messages needed for ECST is variable.
NAS overhead | 2 messages(invite, 180) | 4 messages(invite,100,183,180) | 7 messages(pre-condition)
R19(3 Byte) | 0.024s | 0.048s | 0.084s
pre-R19(7 Byte) | 0.056 | 0.112 | 0.196
Observation 2: For UE in ECM-CONNECTED, extra ECST of CP due to NAS head is negligible.

## Slide 6: Estimated Call Setup Time(3)
UE in ECM-IDLE
  TR 23.700-19 A.1.4 (Estimated time of state transition) is empty with a EN. This slide try to fix it.
Observation 3: For UE in ECM-IDLE, ECST of CP is significantly less than UP due to quick state transition.
  Since CP CIoT optimization needs less RRC messages than UP, in theory CP has less ECST than UP and practical saved ECST can be calculated.
  For state transition from IDLE to CONNECTED, between UE and RAN there are 4 messages for CP approach and 9 messages for UP approach.
    CP has less 5 RRC meaasges than UP(2 SMC, 2 RRC reconfig, 1 RRC complete), then
    CP reduced =5 ×=5 × 0.285s= 1.425s
      If UE supports CP-EDT , CP has less 7 RRC messages than UP, then CP reduced =1.96s
  NOTE: For MT case, time for paging is FFS. It may be quite long in GEO access both for CP and UP.

## Slide 7
Estimated Call Setup Time(4)
For NB-IoT GEO access, RRC connection suspend/resume is not recommended, considering the capacity issue of storing huge amount of UEs context of a GEO, and UP CIoT optimisation being optional feature in NB-IoT
    Signalling of UP(9 messages)
    Signalling reduction of UP CIoT optimisation
    Messages can reduce to 5
    Signalling reduction of CP CIoT optimisation(4 messages)
    If using CP-EDT(optional feature in NB-IoT), NAS data can be in RRCEarlyDataRequest(in third message)

## Slide 8: Security for GEO access(1)
Security for GEO call shall be mandatory for commecial operation
  GEO is more vulnerable to data sniffing due to its huge beam, as revealed by recent article published in 2025 ACM CCS.
For non-roaming, using NAS security for SIP/I1 has advantage
  Although existing SIP security based on IPSec may be used for SIP/I1, it causes more security overhead(30-40 Bytes)as discussed in solution 29.
    Since NAS security achieves less overhead than IPSec, CP approach has less ECST to skip IPSec and rely on NAS security comparing to UP.
  If conclusion for KI#2 is non-IP for SIP/I1, then how to support IPsec is questionable. For CP approach NAS security can be used for SIP/I1 based on non-IP.
Whether above security assumption on using NAS security for GEO signaling is appropriate or not is left to SA3.

## Slide 9: Security for GEO access(2)
For HR roaming, using NAS security for SIP/I1 has advantage
  To support LI in vPLMN, in existing spec SIP security is used only for integrity protection and confidentiality protection is not used. Then SIP message including SMS can still be sniffed.
  To handle GEO security issue in slide 8, SIP signaling in the GEO path should be encrypted. NAS security can be used for SIP/I1 signaling security.
Whether above security assumption on using NAS security for GEO signaling for HR roaming is appropriate or not is left to SA3.
Observation 4: For both non-roaming and roaming case, CP approach has benefit for Signalling security
Practical deployment of EPS security:
  User Plane security in E-UTRAN/EPC even though it is standardized is not commercially deployed, as revealed solution 5, while NAS security is always deployed.

## Slide 10: Other IMS services
IMS based SMS service
  Since SMS is small-data in SIP signalling, transportation over CP has benefit over UP, from perspective of communication efficiency, radio resource saving, UE energy saving. Existing market and operation of NB-IoT justify the usage of CP to handle small-data transportation.
    For many operator, SMS over NAS is not supported in network for mobile phone but only for IoT device. With the completion of coverage of 4G/5G , legacy 2G/3G infrastructures for SMS, e.g. MSC, HLR, have been decommissioned from network. Since IMS session is activated for GEO voice , it is more efficient and simple to transport SMS via SIP but not via SGs.
Observation 5: Signalling via CP has benefit over UP for IMS SMS services

## Slide 11: Impact on UE and network
Existing spec supports simultaneously transport of CP and UP
Observation 6: Existing spec supports simultaneously transport of CP and UP but separated in PDN connections to SCEF and PGW, then for CP approach the enhancement is support of CP and UP within a single PDN conncetion.
In TS 23.401. The yellow highlighted means simultaneous transport of CP and UP is supported in UE and network.
The green highlighted further illustrates the
simultaneous CP PDN and UP PDN, but the two PDNs cannot both connect to PGW. It is because not supporting both S11-U and S1-U addresses in existing S11-C message. It can be easily extended to support both address if necessary.

## Slide 12: Summary
Observation 1: For UE in ECM-CONNECTED, transportation Signalling via CP is prior over UP hence less ECST, although reduced ECST value can not be quantified.
.
Observation 2: For UE in ECM-CONNECTED, extra ECST of CP due to NAS head is negligible.
Observation 5: Signalling via CP has benefit over UP for IMS SMS services
Observation 3: For UE in ECM-IDLE, ECST of CP is significantly less than UP due to quick state transition.
Observation 4: For both non-roaming and roaming case, CP approach has benefit for Signalling security
Observation 6: Existing spec supports simultaneously transport of CP and UP but separated in PDN connections to SCEF and PGW, then for CP approach the enhancement is support of CP and UP within a single PDN conncetion.

## Slide 13
Proposal
Proposal:
The following text shall be concluded in agreement of TR 23.700-19:
  The signalling packets shall be transported over the NB-IoT (GEO) control plane, i.e. using SRB and S11-U.
  For the UE, MME and SGW, IMS PDN connection in NB-IoT access shall support default bearer of CP for signalling and dedicated bearer of UP for voice packet.
    NOTE: There is no observed impact on RAN. Existing RAN specs support combined DRB and SRB for a NB-IoT UE.