## Slide 1
Discussion about 5G VN Group
China Mobile
© 3GPP 2025

## Slide 2: 5G VN group group member identification
GPSI is the unique information to identify whether a UE is a 5G VN group member or not.

## Slide 3: Relationship between 5G VN group adn DNN/S-NSSAI(1/3)
DNN/S-NSSAI are specified in Release15, and are stored in UE SM subscription information.
5G VN group mechanism is specified in Release 16, and the mainly idea is the UE can use DNN/S-NSSAI to access a single SMF and establish a PDU session which support the 5G LAN service.
However, whether a PDU session can support 5G LAN service is depending on two aspects, one is UE using the DNN/S-NSSAI, another is the UE GPSI is in the 5G VN Group membership management parameters.
Observation 1: Not only DNN/S-NSSAI, but also the GPSI, that should be considered to finally identify a UE that belong to a 5G VN group member.

## Slide 4
UE SM subscription information for a DNN/S-NSSAI is stored in UDR during the UE registration procedure.
The 5G VN group configuration is either provided by OA&M or provided by an AF by providing 5G VN Group Data (e.g. PDU session type, DNN, S-NSSAI and Application descriptor etc.) and 5G VN Group membership information (GPSIs) to 5GC via NEF. The NEF provides the received information to UDM, and UDM stores the information in UDR as 5G VN Group Data and Group Identifier data.
Observation 2: The UE SM subscription information for a DNN/S-NSSAI and 5G VN group data for a DNN/NSSAI are managed by different procedures and stored separately in UDR.
Relationship between 5G VN group adn DNN/S-NSSAI(2/3)

## Slide 5
In Stage 3 TS29.505 UDR clause 5.2.35.3.1
Resource: Individual5GVnGroup
Put method (create a new 5G VN group via AF/NEF).
NOTE: Creation of an Individual5GVnGroup has impacts to the UDR, to ensure consistency with other resources. These consistencies can be ensured by UDR-internal solutions.
Observation3: The DNN/NSSAI in UE SM subscription information and in 5G VN group data should keep consistent.
Relationship between 5G VN group adn DNN/S-NSSAI(3/3)

## Slide 6: 5G VN group 1:1 mapping(1/3)
Two different understanding for this above specification.
Understanding 1: all of UEs should be members of the 5G VN group associated with this DNN/S-NSSAI.
Understanding 2: only a subset of these UEs are members of the 5G VN group associated with this DNN/S-NSSAI.
Observation 4: Both of the understandings do not contradict with 1:1 mapping that specified in Rel-16.
TS 23.501:

## Slide 7: 5G VN group 1:1 mapping(2/3)
Understanding 1: all of UEs should be members of the 5G VN group associated with this DNN/S-NSSAI.
In the current Stage 3 TS 29.505 and all Stage 2 AF-NEF-UDM procedures, Interpretation 1 is nowhere explicitly mentioned. Consequently, a gap arises: when a new 5G VN group is created, implying the creation of a new S-NSSAI/DNN. How should the network handle it? Is the AF allowed to create the S-NSSAI/DNN, and does this conflict with existing mechanisms? Rel-16 specifications need to be enhanced.
The AF-NEF-UDM dynamic VN-group-management requirement originates from SA1. Under interpretation 1, any time a member is added or removed at the operator-deployment level, the user must ask the operator to provision or delete the corresponding S-NSSAI/DNN on the SIM. The SA2 solution therefore fails to satisfy the actual service requirement. (TS 22.261 )
Observation5: For understanding 1, current SA2 specification cannot satisfy the service requirement from SA1.

## Slide 8: 5G VN group 1:1 mapping(3/3)
Understanding 2: only a subset of these UEs are members of the 5G VN group associated with this DNN/S-NSSAI.
Under this understanding, the SA1 request for dynamic management can be met, and it is operator-friendly, user-friendly, and readily deployable.
The only drawback is that, when the PCF performs group-level policy-data control, the current specification still refers to S-NSSAI and DNN-based policy control, and 5G-VN group level QoS requirement cannot be supported.
Proposal: Based on the above analysis, understanding 2 is preferred.
Observation6: For understanding 2, only a Rel-18 CAT F contribution for 5G-VN group level QoS requirement is required, so forward-compatibility impact is minimal and the service requirement from SA1 can be fully supported.

## Slide 9: Reply to CT4 LS
Q1: Can a UE, that is not member (temporary/permanently) of any 5G VN group, have an SM subscription (in DNN configuration) with an S-NSSAI/DNN that is associated with a 5G VN group?
SA2 answer: Yes. There is no such limitation that a UE which is not member of a 5G VN group, cannot use the DNN/S-NSSAI to establish a normal PDU session.
Q2: Assuming an enterprise deployment with many UEs subscribed to an enterprise specific S-NSSAI/DNN, is it allowed to provision only a subset of these UEs into one 5G VN group with the same aforementioned S-NSSAI/DNN?
E.g., 100 UEs are subscribed to the enterprise S-NSSAI/DNN and only 10 UEs are required to be provisioned to the S-NSSAI/DNN associated 5G VN group. (still keep 1:1 mapping between the S-NSSAI/DNN and 5G VN group that one and only one 5G VN group is associated with this specific S-NSSAI/DNN)
SA2 answer: Yes. As the answer in Q1, an enterprise can customize the 5G VN group member list and only provide 5G LAN type service to a subset of UEs. The DNN/NSSAI in UE SM subscription information and in 5G VN group data should keep consistent.