## Slide 1: MnS Consumer-based confidence level for intent guarantees
Pedro Henrique Gomes
Ericsson

## Slide 2: Existing Concept: Confidence Level
Confidence level for intent guarantees was introduced in UC#8 of TR 28.881
Confidence level: probability (threshold) evaluated by the MnS Producer that the guaranteed expectations are fulfilled.
Expressed as: “current probability that the MnS Producer evaluates it can keep the requirements fulfilled.”
It should be reported by the MnS Producer
Used only for monitoring, not for planning or contractual guarantees.
Limitations:
  One-directional: consumer has no control on confidence threshold.
  No linkage with SLA / commercial guarantees.
  Yet only “best-effort” fulfilment of the guaranteed expectations.
MnS Consumer
MnS Producer
Guaranteed requirements
Confidence level reported

## Slide 3: Proposed Enhancement: Confidence Level Specified by MnS Consumer
  The concept of confidence level could be extend to allow MnS Consumer to specify confidence level as part of the intent (desired minimum probability of success).
  Enables two-way definition of confidence:
    Consumer-requested confidence level → required minimum probability (guarantee threshold).
    Producer-reported confidence level → actual measured probability.
  MnS Producer evaluates if it can commit to the requested probability and maintains reporting the current probability of fulfilling the requirements.
MnS Consumer
MnS Producer
Guaranteed requirements with Confidence Level > 95%
Report on the actual confidence level
Enhancement

## Slide 4: Benefits and Use Scenarios
  With MnS Consumer-based confidence level, there is an easy mapping between intent guarantees and contractual terms (e.g., SLAs)
  For instance, an SLO of “delay lower than X ms” with 95% compliance probability could be “mapped” to an intent with guaranteed expectation where the MnS consumer “asks” for 95% confidence level
Customer
MnS Producer
Guaranteed expectation
“latency lower than 10 ms”
Confidence level of 95%
Current confidence level (probability of fulfilling the expectation) is 93%
Operator (MnS Consumer)
SLO “delay lower than 10 ms”
Compliance probability of 95%

## Slide 5: For endorsement
The proposal complements the existing producer-reported confidence concept; it does not replace it.
Provides foundation for guarantee-based service assurance and intent-driven SLA management.
Proposal for endorsement: It is proposed that UC#8 of TR 28.881 (intent guarantee) be extended to also allow the MnS Consumer to optionally specify a confidence level, representing the minimum probability of fulfilling the guaranteed requirement to be committed by the MnS Producer. The calculation and reporting of the confidence level by the MnS Producer remains unchanged.