## Slide 1: Intents, Goals and Autonomous Agents
Stephen Mwanje
Nokia

## Slide 2: Introduction
In SA5#162, pCR S5-253529 proposed to break down the intent utility function into prioritized weighted targets.
However, the weighting of specific outcomes and their relative priority is also part of intent-handling which provides requirements to be accomplished by the entities supporting the intent handler
In 6G we plan to study Agents, Intent-driven management, and CCLs - All three are conceptually related functionalities
The work on Agent should leverage existing concepts – as a starting point
But clarity is required on how they are related.

## Slide 3: Observations and Proposals
Observation 1: An Agent needs a mechanism to derive appropriate actions and execute them.
  The agent is similar to a CCL in the functionality of observing network state, deriving actions and executing actions
  Proposal 1: The definition of agent should start from CCL as a building block
  Observation 2: An Agent needs to have intelligence with which to plan its constituent functionality (tools)  A the agent may utilize AI/ML or other resources of 3GPP management system
  Proposal 2: An agent is a combination of a CCL with some intelligence or an intelligent CCL
Fig. 1: Agents & CCLs (evolution of 5G Rel. 19)
Agent
intelligence
Closed control loop
Output= Reports/insights
Input?
Managed entity

## Slide 4: Observations and Proposals
  Observation 3: An intent handler takes input in form of an intent but no execution function is assumed for the intent handler
  Proposal 2: An agent cannot be equivalent to an intent handler
  Proposal 3: Like a CCL, an agent (i.e., intelligent CCL) is an example entity that supports an intent handler in fulfilling intents
  Observation 4: An Agent needs to take an input defining what the agent must achieve. The input cannot be the same as intent, otherwise the two become equivalent.
  Proposal 4: The Agent exposes a service different from an intents → Can be called an agent control MnS,
  Proposal 5: The input to an Agent should be content derived by the intent handler → Can be called goals or tasks,
  Proposal 6: The goals or tasks provided as input to CCLs or agents are the detailed target descriptions derived from intents.
Fig. 2: Possible E2E implementation
Agent Control MnS
Reports/insights
E2E Automation Requirement: Intents from consumer
AE
Intent handler
Agent
(intelligent CCL)
goals/tasks/..

## Slide 5: For endorsement
The group is requested to endorse the following proposals and related end-to-end figure (Fig. 3)
Proposal 1: The definition of agent starts with CCL as a building block
  Proposal 2: An agent cannot be equivalent to an intent handler
  Proposal 3: An agent is an example entity that supports an intent handler in fulfilling intents
  Proposal 4: The Agent exposes a service different from an intents → Can be called an agent control MnS,
  Proposal 5: The Agent control input can be derived by an intent handler  can be called goals or tasks
  Proposal 6: The goals or tasks provided as input to CCLs or agents are the detailed target descriptions derived from intents.
    The definitions of goals and tasks are FFS
Fig. 2: Possible E2E implementation
Agent Control MnS
E2E Automation Requirements: Intents from consumer
AE
Intent handler
Fig. 3: Input-output relations of intents, CCLs and Agents
intelligence
Output= Reports/insights
Input= Goals / tasks/..
Managed entity
IDM MnS
Agent
(intelligent CCL)
Closed control loop