## Slide 1: NWM Way Forward – Work Area 6 ISAC
InterDigital, CATT

## Slide 2: Outline
Justifications for WA6 ISAC WT inclusion in 6G study
  WT6.1 Support collecting sensing data from UE
  WT6.2 Expose converged sensing data to consumers
  WT6.3 Obtain sensing data from non-3GPP entities
Summary for WA6 ISAC WTs

## Slide 3: WA6: ISAC; WT6.1
TEMLATE
Summary of comments
  Comments about whether WT is more in SA2 (collecting sensing data) and SA3 (security related) scope
  Coordination with SA2 is required
  Questions about UE’s ability to collect sensing data (SA2 scope) from modem
Justification/Clarification
  In TS 22.137, definitions for “Sensing transmitter” and “Sensing receiver” in clause 3.1 includes
    “A sensing receiver is part of a RAN node or a UE” and “A Sensing transmitter is part of a RAN node or a UE”
  TS 22.137 lists functional requirements for sensing support in UEs:
    “Subject to local regulation, the 5G network shall enable UEs without 5G coverage to use unlicensed spectrum to provide 5G wireless sensing service”
    “Subject to regulation, the 5G network shall enable UEs supporting V2X application to perform 5G Wireless sensing when not served by RAN using the allowed ITS spectrum and unlicensed spectrum”
Candidate Work Task | Support | Do not support | Moderator Remarks
WT6.1: How to support collecting sensing data from UE considering UE privacy and user consent. | Interdigital, ZTE, CATT, MediaTek, CMCC, Apple | Lenovo, Nokia, Samsung, Ericsson | SA2 overlap /co-ordination, SA2/SA3 scope, non-3GPP sensing, Need clarification, Merge with WT6.3, UE aspects, Relation to FS_APCOT

## Slide 4: WA6: ISAC; WT6.1 (2)
TEMLATE
Justification/Clarification (cont)
  TS 22.137 also lists the support of collecting non-3GPP sensing data
    “Subject to user consent, regulation, and operators policy, the 5G system shall be able to collect non-3GPP sensing data from authorized non-3GPP sensors and securely provide it to 5G network”
  TR 22.870 describes 20+ use cases for the collection of sensing data by UEs, specifically in clauses 6.51 and 7.23
    6.10, 6.14, 6.15, 6.32, 6.35, 6.51, 7.2, 7.4, 7.6, 7.10, 7.11, 7.12, 7.13, 7.14, 7.16, 7.18, 7.19, 7.20, 7.21, 7.23, 7.24, 7.25.
  In TR 23.700-14, sensing study is limited to gNB (RF-)based sensing.
Way forward (e.g. revised WT, merging etc)
  WT6.1 can be addressed and combined with WT6.3 (with revisions)
Candidate Work Task | Support | Do not support | Moderator Remarks
WT6.1: How to support collecting sensing data from UE considering UE privacy and user consent. | Interdigital, ZTE, CATT, MediaTek, CMCC, Apple | Lenovo, Nokia, Samsung, Ericsson | SA2 overlap /co-ordination, SA2/SA3 scope, non-3GPP sensing, Need clarification, Merge with WT6.3, UE aspects, Relation to FS_APCOT

## Slide 5: WA6: ISAC; WT6.2
TEMLATE
Summary of comments
  Has dependency on SA2 work
  Need clarification of SA6 scope; relationship to other WT (e.g. 2.6) and SA6 5GA Rel-20 ISAC work
  Clarification needed of exposure to application client or enablement layer, not UE modem layers
Justification/Clarification
  TS 22.137 lists various function requirements for network exposure of sensing results in clause 5.2.3
    “Subject to operators policy, the 5G network shall be able to provide secure means to report sensing result to a trusted third-party requesting information about a target object when specific requested conditions are met”
    “Subject to users consent, regulation and operators policy, the 5G network may provide secure means to expose to a trusted third-party the combined sensing result derived from the joint processing of the 3GPP sensing data and non-3GPP sensing data”
Candidate Work Task | Support | Do not support | Moderator Remarks
WT6.2: How to expose the converged sensing data to the consumers (e.g. AF, UE). | Interdigital, ZTE, CATT, Lenovo, Nokia, MediaTek, CMCC, Apple, Huawei, Ericsson | Samsung | Related to WA1, UE aspects, SA2/SA3 scope, Need clarification

## Slide 6: WA6: ISAC; WT6.2 (2)
TEMLATE
Justification/Clarification (cont)
  TR 22.870 describes 20+ use cases for exposing sensing results obtained from multiple sensing data sources, specifically in clauses 7.6 and 7.21
    6.14, 6.15, 6.32, 6.51, 7.2, 7.4, 7.6, 7.7, 7.8, 7.10, 7.11, 7.12, 7.13, 7.14, 7.15, 7.16, 7.17, 7.18, 7.19, 7.20, 7.21, 7.23, 7.25
  TR 23.700-14 architectural requirement and key issue
    “The Sensing Service shall support exposure of the sensing results to a Sensing Service consumer”
    “Study what types of Sensing results with or without the Sensing contextual information defined in 22.137 [2] could be exposed from the Core Network to the Sensing Service Consumer”
  Converged is meant as the fusion of 3GPP and non-3GPP sensing data/results
Way forward (e.g. revised WT, merging etc)
  Revised to “Whether and how to expose the fusion of 3GPP and/or non-3GPP sensing data/results to consumers (e.g. AF, UE) in the application enablement layer.”
  Propose to consider revised WT6.2 for inclusion in 6G study
Candidate Work Task | Support | Do not support | Moderator Remarks
WT6.2: How to expose the converged sensing data to the consumers (e.g. AF, UE). | Interdigital, ZTE, CATT, Lenovo, Nokia, MediaTek, CMCC, Apple, Huawei, Ericsson | Samsung | Related to WA1, UE aspects, SA2/SA3 scope, Need clarification

## Slide 7: WA6: ISAC; WT6.3
TEMLATE
Summary of comments
  Question about relationship to Rel-20 5GA work and other WT (e.g. 2.6)
  Comment about rephrasing to use SA1 terminology
Justification/Clarification
  TS 22.137 defines non-3GPP sensing data as data provided by non-3GPP sensors (e.g., video, LiDAR, sonar) about an object or environment of interest for sensing purposes
  TS 22.137 lists various function requirements for support of obtaining non-3GPP sensing data
    “Subject to user consent, regulation, and operators policy, the 5G system shall be able to collect non-3GPP sensing data from authorized non-3GPP sensors and securely provide it to 5G network”
    “Subject to user consent, regulation, and operators policy, the 5G system should support the joint processing of the 3GPP sensing data and non-3GPP sensing data to derive a combined sensing result”
Candidate Work Task | Support | Do not support | Moderator Remarks
WT6.3: Whether and how to obtain the sensing data from non-3GPP entities (e.g. Radar, Camera). | Interdigital, ZTE, CATT, Lenovo, CMCC, Apple, Huawei, Ericsson | Nokia, Samsung | SA2 co-ordination, Need clarification, UE aspects, Gap analysis

## Slide 8: WA6: ISAC; WT6.3 (2)
TEMLATE
Justification/Clarification
  TR 22.870 describes 15+ use cases for obtaining non-3GPP sensing data, specifically in clauses 7.16 and 7.17
    6.15, 6.35, 6.51, 7.4, 7.6, 7.7, 7.10, 7.12, 7.13, 7.14, 7.15, 7.16, 7.17, 7.18, 7.20, 7.21, 7.25
  TR 23.700-14 architectural assumptions and requirements
    “The study only considers 3GPP access technologies”
Way forward (e.g. revised WT, merging etc)
  Revised to “Whether and how to obtain the sensing data/sensing results from UEs, including non-3GPP sensors (e.g. Radar, Camera), in the application enablement layer.”
  Propose to consider WT6.3 for inclusion in 6G study
    WT6.1 is addressed by WT6.3
Candidate Work Task | Support | Do not support | Moderator Remarks
WT6.3: Whether and how to obtain the sensing data from non-3GPP entities (e.g. Radar, Camera). | Interdigital, ZTE, CATT, Lenovo, CMCC, Apple, Huawei, Ericsson | Nokia, Samsung | SA2 co-ordination, Need clarification, UE aspects, Gap analysis
Notes: 22.870:.

## Slide 9: Summary
SA1 TS 22.137 provides definitions and functional requirements for ISAC in 5G Rel-19
SA1 TR 22.870 describes 15+ use cases supporting WT6.1, WT6.2, and WT6.3 in 6G
SA2 TR 23.700-14 identifies scope of ISAC work in 5G Rel-20
  “In this study, the scope is restricted to gNB-based sensing” (i.e., RF-sensing only, no UE based sensing)
  “Study what types of Sensing results with or without the Sensing contextual information defined in 22.137 [2] could be exposed from the Core Network to the Sensing Service Consumer”
  “The study only considers 3GPP access technologies” (no support for non-3GPP technologies)
Way forward
  WT6.1 is addressed by WT6.3; agree to revise WT6.2 and WT6.3
    Whether and how to obtain the sensing data/sensing results from UEs, including non-3GPP sensors (e.g. Radar, Camera), in the application enablement layer.
    Whether and how to expose the fusion of 3GPP and/or non-3GPP sensing data/results to consumers (e.g. AF, UE) in the application enablement layer.
  Propose inclusion of WT6.2 and WT6.3 in SA6 6G study