## Slide 1: Approaching 5G in China
CCSA
April. 2018

## Slide 2: CONTENT
5G Technology R&D Trial update
5G applications exploration and innovation
Page 2

## Slide 3: 5G Trial Roadmap
Scale Trial
Step 2:
Tech Scheme Trial
Step 3:
System Trial
Step 1:
Key Tech Trial
Phase 1: Technology R&D Trial
Phase 2: Scale Trial
2016
2017
2018
2019
2020
2015
Operator & Research Institute
Infrastructure
Chipset & Terminal
Instrument
Page 3

## Slide 4: Completely Meet ITU 5G KPI for Typical Scenarios
Seamless wide
-area coverage
Low-latency
high-reliability
Low-power
massive-connection
High-capacity
hot-spot (HF)
8 端口
64 Ports
200MHz
12UE
64 端口
200MHz
Peak data rate:
28Gbps
第三方仪表
UE
BS
User plane latency: 0.277ms
Connection density: >2.17M/MHz/cell
Peak data rate: 62.25Gbps @800MHz
Band: 26GHz
High-capacity
hot-spot (LF)
Area traffic capacity: 107Mbps/m2
Peak data rate (LF) | Air interface latency | Connection density | Peak data rate (HF) | Area traffic capacity
>10Gbps | <1ms | 1M/km2 | >20Gbps | >10Mbps/m2
ITU 5G KPI
62.25
BS
UE
28
277
4.8
Page 4

## Slide 5: New System Architecture Solution meet 5G KPI
Network function and NFV Platform can meet with the functionality and performance KPI.
Network Function
NFV Platform
Edge-central 2 layer DC networking
Separation of NF and HW
Different NFs for three typical scenarios
Meet latency, throughput and reliability KPI
UPF latency 0.2ms, 1MPPS/single CPU core, 9.8/10G throughput
Network slice
On-demand customization
Service based arch.
Align with 3GPP
standardizations
Edge computing
Low latency/network
capability exposure
Signaling
handling
Data
forwarding
Support quick time to market/
large-scale concurrent signaling
Page 5

## Slide 6: 5G Technology R&D Trial Step 3 Launched
2017Q4
2018Q1
2018Q2
2018Q3
2018Q4
2017Q3
Non-standalone (NSA) and Standalone (SA)
2019
NSA Test
SA Test
Specifications
Test & Verification
Step 3 Specifications Release
The first batch of Step 3 specifications released on Jan. 16, 2018
The test contents: Infrastructure, terminal, networking and inter-operability, 5G applications, R16 New features
Interoperability Test
Page 6

## Slide 7: The Principles of 5G Tech. R&D Trial Step 3
Networking
NSA
Scenario
eMBB
Frequency
3.5 & 4.9 GHz
Service
Data
SA
URLLC
mmWave
Voice
Page 7

## Slide 8: Spectrum for 5G Trial
Spectrum below 6GHz - Core frequency band
Spectrum above 6GHz - Supplemental frequency band
    3400-3600 MHz
    4800-5000 MHz
MIIT approved application of 3400-3600 MHz for 5G Technology R&D trial on January 7, 2016.
MIIT approved 4800-5000 MHz for the trial on July 3, 2017.
    24.75-27.5 GHz
    37-42.5 GHz
On July 3, 2017, 24.75-27.5 GHz and 37-42.5 GHz, a total of 8.25GHz spectrum in millimeter wave approved by MIIT for 5G Technology R&D trial.
2.1GHz frequency band for 5G NSA etc. test
Page 8

## Slide 9: 5G Industrial Applications
5G Industrial Applications still in the cultivation stage, need to explore from service, ecosystem, business models, laws and regulations aspects
IMT-2020 PG set up two new Working Groups
C-V2X WG and 5G Application WG
“5G Application Contest”
Encourage innovative applications of 5G
Open for submission from Feb. 1st, 2018
Page 9

## Slide 10: C-V2X, Cross-industry Innovation Platform
Industry-college-institute Cooperation， Cross-industry Integration
Page 10
2017
2018
No.2
(Jun.)
Establishment of C-V2X Working Group
Identified 4 Work Items
No.7
(Sep.)
4 WIs review
Release 2 specification for LTE-V2X test
(Jan.)
C-V2X White paper on service requirement, network and business models
(Jun.)
Report on C-V2X Test and Evaluation
Work Items for 2018
No.16
(Nov.)
MoU between IMT-2020 and 5GAA

## Slide 11: C-V2X Demonstrations and Pilot Areas
“5+2” C-V2X Pilot Areas
LTE-V2X Infrastructure and Application Scenarios
MIIT supported Shanghai, Zhejiang, Beijing-Hebei, Jilin, Chongqing, Hubei, Jiangsu to set up C-V2X pilot areas, to promote cross-industry demonstrations and test.
MIIT established the national cross-industry cooperation mechanism for C-V2X development, coordinated with MPC, MOT, NDRC, etc.
Page 11

## Slide 12: NB-IoT initiates small scale commercial deployments
芯片
Network: Three operators upgraded/built more than 300,000 NB-IoT BSs to provide full coverage service.
Commercial chipset: Huawei, Qualcomm, ZTE, MTK etc.
Module: Small & Medium enterprises, price from $30 falls below $6.
Platform: Operators and Huawei dedicate to providing platforms, towards the development of NB-IoT ecosystem.
Page 12

## Slide 13: NB-IoT applications focusing on Smart City
“Local governments dominant, Platforms + Applications” initialized NB-IoT commercial use.
To date, around million connections online. An application with million connections may appear in 2018.
60+ NB-IoT applications covering numerous areas, e.g. city management, industry upgrading, individual consumption.
Year 2018 is critical to build industrial ecosystem and explore business models.
Typical application: Metering, parking, lighting
Chart: 
| Water meter | Gas meter | Parking | Lighting | Smoke detector | Bike share | Animal | etc.
列2 | 70000 | 25000 | 3000 | 10000 | 10000 | 1000 | 5500 | 10000
Page 13

## Slide 14: Yingtan, leading NB-IoT innovation & application
Framework Agreement for strategic cooperation with CTC, ZTE, Inspur and SGCC
Framework Agreement for strategic cooperation with CMCC and Huawei
April 12
“Yingtan Cup” China Maker Innovation & Entrepreneurship Contest
2017
Jan. 5
June 12
Opening ceremony of China Yingtan MIoT Industry Park and Establishment of MIoT Alliance
Sept. 14
Oct. 12
March 10
Framework Agreement for strategic cooperation with CUCC
Yingtan 100,000 commercial water meters online
2018
Feb.
Yingtan incubated 40+ applications, 100,000+ online connections
Yingtan dedicated to the development of NB-IoT, with leading public platforms, innovative applications and online connections.
Contributed to the optimization of 3GPP NB-IoT specifications, and the construction of NB-IoT standardization system in China
Page 14

## Slide 15
Summary and Outlook
Building Unified Global 5G Standards and Ecosystem
In the framework of unified global 5G standards, synchronously promote the study of eMBB and URLLC standards
Actively promote 5G Middle-frequency allocation, 5G high-frequency planning study, and global harmonization
5G trial will be a carrier to facilitate the research and development of 5G pre-commercial products, for commercialization in year of 2020
Practice and exploration on C-V2X and NB-IoT, gain wide experience in 5G commercial deployment.
Page 15

## Slide 16
Thanks for your attention