## Slide 1
China Telecom
Discussion on Slice-based NPN Selection

## Slide 2
  Background and use case
In Rel-18 EASNS, the slice-based PLMN selection was studied and defined. During the scenario of network slice not offered by the serving network but available in the area from other network(s), the HPLMN shall be able to provide the UE with prioritization information of the VPLMNs with which the UE may register for the network slice.
This problem is also applicable in the NPN scenario.
NPN A, Slice A
NPN B, Slice B
NPN A, Slice A
NPN B, Slice B
① UE is in NPN A and requires service from Slice B, which is available in NPN B
② NPN A provides the prioritization information and NPN B is the highest prioritized NPN

## Slide 3
  Existing requirement and observation
In TS 22.261, there are existing requirements on the HPLMN to provide the UE with prioritization information of the VPLMNs with which the UE may register for the network slice.
6.1 Network slicing
6.1.2 Requirements
6.1.2.1 General
For a roaming UE activating a service/application requiring a network slice not offered by the serving network but available in the area from other network(s), the HPLMN shall be able to provide the UE with prioritization information of the VPLMNs with which the UE may register for the network slice.
Observation: This problem is also applicable in the NPN scenario. The existing requirement cannot support providing the UE with prioritization information of other NPN(s) with which the UE may register for the desired network slice.

## Slide 4
  Proposal
A CR is proposed with the following additional requirement to TS 22.261 subclause 6.1.2.1.
For a UE with no other active services requiring a network slice not offered by the serving NPN but available from other NPN(s), the 5G system shall be able to support the serving NPN to provide the UE with prioritization information of other NPN(s) with which the UE may register for the desired network slice. When the service/application concludes, the UE shall register to the highest prioritized available NPN.

## Slide 5
THANKS
感 谢 聆 听